191

                                  CHAPTER 19 - STRINGS


             Sometimes we want to deal with long strings of information. Here
             long means hundreds or thousands of bytes, not tens of bytes. The
             8086 provides a group of instructions to move and compare
             strings. These instructions have a rigid structure, but with a
             little bit of effort we can get them to work easily for us. We
             will start with SCAS, since it is simple, yet embodies all the
             rigid features of these instructions. 

             SCAS (scan string) compares either a byte to AL or a word to AX.
             The byte or word must be in memory, and the register must be AL
             or AX. SCAS also increments or decrements the pointer. First, the
             size:

                 scasb

             compares a byte to AL, while:

                 scasw

             compares a word to AX. But where's the pointer? You have no
             choice, it's DI. Not only is it DI, but it MUST be ES:DI. The ES
             segment is coded into the 8086 microcode; the DI register is
             coded into the 8086 microcode; there is nothing you can do to
             change it. What about incrementing or decrementing? In the flags
             register, there is a flag called the direction flag. It is set
             manually by the program. If DF = 0, SCAS increments DI; if DF =
             1, SCAS decrements DI.{1} The equivalent software for the
             instruction would be:

                           (scasb)                       (scasw)
             DF = 0        cmp  al, es:[di]              cmp  ax, es:[di]
                           pushf                         pushf
                           add  di, 1                    add  di, 2
                           popf {2}                      popf


             DF = 1        cmp  al, es:[di]              cmp  ax, es:[di]
                           pushf                         pushf
                           sub  di, 1                    sub  di, 2
                           popf                          popf

             ____________________

                1. Every time you have called show_regs DF has been there; it
             doesn't show 0 and 1, it shows + and -  (+ = 0 , - = 1).

                2. The microcode doesn't really push and pop the flags. This
             is only to indicate that the order of operations is (1) get the
             byte (word) from the string, (2) compare and set the flags, and
             finally (3) increment (decrement) the pointer without changing
             any of the flags.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             The PC Assembler Tutor                                        192
             ______________________

             Thus, at the end of the end of the instruction, DI is in a new
             place and the flags are set according to the compare result. DI
             is incremented by a byte for the byte instructions; it is
             incremented by a word for the word instructions. The same pattern
             holds true for decrementing DI. 

             We set the direction flag with the instruction STD (set direction
             flag) and we clear the direction flag by using CLD (clear
             direction flag). It only needs to be set or cleared once, and
             this should be done before starting the operation. DF is only
             changed by those specific instructions from the program - it
             can't be changed by any arithmetical or logical operation on the
             chip.

             If you have a string and you are looking for a specific number,
             (27 for instance), you simply put that number in AL (or AX) and
             run a loop. If:

                  long_string  db 5000 dup (?) 

             contains data and we want to look for a 27d then the operation
             is:

                 lea  di, long_string{3}
                 mov  al, 27
                 cld

             search_loop:
                 scasb
                 jne  search_loop

             on exiting, DI will point 1 PAST the matching byte (word). You
             move back one byte (word) to find the match. Why would anyone
             want this instruction? With a 0 in AL, it will find the end of a
             C (0d terminated) string quickly. Also, that number 27 is no
             accident. 27d is the ASCII escape character. For a lot of
             hardware, 27d indicates that the bytes that follow are not ASCII
             characters but are technical information. For instance, on my
             printer the sequence (27d, 65d, 0d, 11d) sets tabs every 11
             columns. SCAS can find where these substrings are so the program
             can operate on them. 

             In order to use string instructions, we need strings to work on.
             The one we will use is called CH1STR.OBJ. It is in \XTRAFILE.  It
             is an object file that contains one data segment containing a
             string of lower case characters. The string is several thousand
             bytes long, it is terminated by 0, and it contains ONLY the lower
             case letters (a-z). It is the first draft of part of chapter 0
             with all punctuation, numbers, spaces, carriage returns etc.
             deleted. All upper case letters have been converted to lower case
             so we don't have to worry about the difference between A and a, Q
             and q. 

             The name of the array in CH1STR.OBJ is CH1STR and it is defined:
             ____________________

                3. Assuming that long_string's segment address is in ES.





             Chapter 19 - Strings                                          193
             ____________________


                 PUBLIC  ch1str

             so that you can access it with the SEG and OFFSET operators.
             First, let's find out how long the string is.{4} 

             MYPROG1.ASM
             ; - - - - - - - - - -
             STRINGSTUFF  SEGMENT  PUBLIC 'DATA' 
             EXTRN  ch1str:BYTE
             STRINGSTUFF  ENDS
             ; - - - - - - - - - - 
             ;- - - - - - - - - - PUT CODE BELOW THIS LINE

                 mov  ax, seg ch1str      ; segment address of ch1str
                 mov  es, ax

                 mov  di, offset ch1str   ; offset address of ch1str
                 mov  al, 0               ; try to match zero
                 cld                      ; increment (DF = 0)

             string_end_loop:
                 scasb
                 jne  string_end_loop

                 dec  di                  ; back up one
                 mov  ax, di
                 sub  ax, offset ch1str
                 call print_unsigned

             ;- - - - - - - - - - PUT CODE ABOVE THIS LINE

             In all these string operations, we need to be careful about
             boundary conditions. What if there is no valid data? What if
             there is one valid item? What if the string is empty?

             On exiting the loop, DI will point 1 past the first 0d, so we
             need to back up one to point to the first 0d. Then subtracting
             the starting position will give us the count.{5} Try it out and
             find out how long it is. Since we now have 3 object modules, the
             link instruction must read:

                 link  myprog+ch1str+asmhelp ;

             assuming that you name your program myprog.asm. Save the result
             because we will need to use this number several times.

             ____________________

                4. Just to keep it from being too easy, I have put garbage
             both in front of the string and behind the string. That means
             that the string length is shorter than the length of the object
             file and the string does not start with the first byte of the
             object file.

                5. If the first byte in the string is 0d, we move one, then
             move back one which gives the length zero.





             The PC Assembler Tutor                                        194
             ______________________

             You will notice that we have gotten the segment address by using
             the SEG operator. You don't need to know the name of the segment.
             The segment doesn't even have to be PUBLIC. As long as the
             VARIABLE is either in the same file or is in another file and
             PUBLIC, the linker will find the correct segment address and put
             it there.


             To make things a little more complicated, we will make another
             infinite loop. This time you will enter a character, and the
             program will find the first occurance of that character. We need
             to add some error checking here. Since you will probably be
             dreaming about taking your next vacation in Hawaii while you are
             entering the data, a few characters that don't exist in the
             string (things like G $ ? ~ ) might creep in. It would be
             possible to run way past the end of the string before you found
             that character. We'll put the length of the string (from the last
             program) in CX, have a regular loop so we can't go too far, and
             jump out of the loop if we find a match. 

             MYPROG2.ASM
             ; - - - - - - - - - -
             STRINGSTUFF  SEGMENT  PUBLIC 'DATA' 
             EXTRN  ch1str:BYTE
             STRINGSTUFF  ENDS
             ; - - - - - - - - - - 
             ;- - - - - - - - - - PUT CODE BELOW THIS LINE

                 mov  ax, seg ch1str
                 mov  es, ax

             outer_loop:
                 call get_ascii_byte           ; returns character in al
                 mov  cx, $$$$$$$              ; enter string length here

                 mov  di, offset ch1str
                 cld                           ; increment (DF = 0)

             string_end_loop:
                 scasb
                 je   after_loop               ; if equal, we found the char
                 loop string_end_loop

                 mov  ax, 0                    ; we fell through the loop
                 call print_unsigned
                 jmp  outer_loop

             after_loop:
                 mov  ax, di                   ; move for printing
                 sub  ax, offset ch1str        ; number of bytes
                 call print_unsigned

                 jmp  outer_loop


             ;- - - - - - - - - - PUT CODE ABOVE THIS LINE






             Chapter 19 - Strings                                          195
             ____________________

             Those dollar signs are the place to enter the exact length of the
             string that you got from the last program. This time we jump out
             of the loop if we find a match; DI will be 1 past the matching
             character, but this will give us the right count (if we find the
             character in the first space, we increment once). If we can't
             find a match we fall through the loop and print a 0. Remember to
             link all 3 modules when you run the program. Run the program and
             then we'll move forward.

             This type of thing is so common with string operations that there
             is a special prefix for SCAS and all other string operations
             which makes the coding simpler. It has several forms:

                 rep       decrement cx ; repeat if cx is not zero
                 repe      decrement cx ; repeat if cx not zero and zf = 1
                 repz      decrement cx ; repeat if cx not zero and zf = 1
                 repne     decrement cx ; repeat if cx not zero and zf = 0
                 repnz     decrement cx ; repeat if cx not zero and zf = 0

             REP is for the move instructions which we will see later - it
             won't work here. For each prefix, if either (or both) of the
             conditions is not true, the repitition stops. For instance, with
             REPE, if cx is zero, and/or if the comparison was not equal (so
             the zero flag was not set), the instruction will stop. For our
             program, the coding is:

                 repne scasb

             That's it. That replaces the whole inner loop. Here is our new
             coding of the last program.

             MYPROG3.ASM
             ; - - - - - - - - - -
             STRINGSTUFF  SEGMENT  PUBLIC 'DATA' 
             EXTRN  ch1str:BYTE
             STRINGSTUFF  ENDS
             ; - - - - - - - - - - 
             ;- - - - - - - - - - PUT CODE BELOW THIS LINE

                 mov  ax, STRINGSTUFF
                 mov  es, ax
                 cld                           ; increment (DF = 0)

             outer_loop:
                 call get_ascii_byte           ; returns character in al
                 mov  cx, $$$$$$$              ; enter string length here
                 lea  di, ch1str               ; address of string

                 repne  scasb

                 je   found_the_char           ; an equal comparison
                 mov  ax, 0                    ; we didn't find a match
                 call print_unsigned
                 jmp  outer_loop

             found_the_char:
                 mov  ax, di                   ; move for printing





             The PC Assembler Tutor                                        196
             ______________________

                 sub  ax, offset ch1str        ; number of bytes
                 call print_unsigned
                 jmp  outer_loop

             ;- - - - - - - - - - PUT CODE ABOVE THIS LINE

             There are two possibilities for exiting the 'repne scasb'
             instruction. Either we found an equal comparison or we exhausted
             all the characters in ch1str. If we found an equal comparison, JE
             will send us to the print routine. Otherwise we print a 0 because
             we finished the loop without finding anything. 


             STOS

             We can ask the operating system to allocate memory for us while
             the program is running.{6} When you get it, however, it will
             contain trash. The fast way to clear it is to use STOS (store to
             string). The instruction is:

                 stosb
             or:
                 stosw

             The equivalent action (not counting changing the value of DI) is:

                 mov  es:[di], ax    ; or AL for byte moves

             Once again (1) the pointer is the ES:DI pair, which is mandatory,
             and (2) DI is incremented or decremented (by 1 for byte, by 2 for
             word) depending on the status of DF, the direction flag. The
             instruction moves a byte (a word) from the AL (AX) register to
             the memory address pointed to by ES:DI. We can use the REP{7}
             instruction to speed things up a bit. If we have a 11,872 word
             block of memory, we can clear it with the following instructions:

             ; - - - - - - - 
             DATASTUFF  SEGMENT
             my_bufferdw  11872 dup (?)
             DATASTUFF  ENDS
             ; - - - - - - -

                 mov  ax, seg my_buffer
                 mov  es, ax
                 cld                           ; increment (DF = 0)

                 mov  ax, 0               ; clear the buffer with 0s
                 mov  di, offset my_buffer
                 mov  cx, 11872
                 rep  stosw
             ____________________

                6. Cf. You-know-who's Programmer's Guide to You-know-what or
             "DOS Programmer's Reference."

                7. There is no comparison here, so REPE or REPNE doesn't make
             any sense.





             Chapter 19 - Strings                                          197
             ____________________


             That's as fast as it gets. Why does the STOS instruction use AX?
             Because that's the register that port i/o uses. If you are
             writing a communications program, you need speed. You can have
             the following:

             ; - - - - - - - - - 
             DATASTUFF  SEGMENT
             port_address   dw   0F2A8h        ; this address is legal but
                                               ; there's nothing there. 
             input_buffer  db   4000h     dup (?)
             output_buffer  db   4000h     dup (?)
             DATASTUFF  ENDS
             ; - - - - - - - - -

                 mov  ax, DATASTUFF
                 mov  es, ax
                 cld                           ; increment (DF = 0)
                 mov  di, offset input_buffer
                 mov  dx, port_address

             input_loop:
                 in   al, dx
                 stosb
                 jmp  input_loop
             ; - - - - - - - - - 

             A real program would be much more complicated because we would
             have to check to see if data was ready to come in and we might
             need to check the data for errors. Also we would occasionally
             have to clear the buffer. The port address F2A8h is just an
             arbitrary address. It's a legal address but there's nothing
             there.

             We should write a program, so let's input a character and have it
             fill the screen. We'll leave the last line of the screen alone so
             you can see your input. Move your cursor to the last line before
             beginning the program.

             ; - - - - - ENTER CODE BELOW THIS LINE

                 mov  ax, 0B800h          ; or 0B000h for a monochrome card
                 mov  es, ax
                 cld                      ; increment (DF = 0)


             outer_loop:
                 call get_ascii_byte      ; AL = fill char from input
                 mov  ah, 07h             ; black background, white letters
                 sub  di, di              ; set di to zero
                 mov  cx, 1920            ; 24 lines X 80 chars
                 rep  stosw
                 jmp  outer_loop

             ; - - - - - ENTER CODE ABOVE THIS LINE

             If you have a monochrome card, the segment address is 0B000h. If





             The PC Assembler Tutor                                        198
             ______________________

             you have a color card and are in text mode, the segment address
             should be 0B800h. This fills the first 24 lines with the input
             character. The STOS instruction has no effect on the cursor. 


             LODS

             The opposite of STOS is LODS (load string) It moves a byte (word)
             from the string to the AL (AX) register. This time, for a change,
             we use the SI register as a pointer, and the default register is
             DS.{8} As always, SI is incremented or decremented by a byte
             (word) depending on the setting of DF, the direction flag. The
             two possibilities are:

                 lodsb
             and
                 lodsw 

             The equivalent action (not counting changing the value of SI) is:

                 mov  ax, [si]  ; or AL for byte moves

             This is an instruction for people that write device drivers. You
             could use it if you are sending a string of characters to the
             printer, but that's about it. Code for doing that would have the
             following form:

             ; - - - - - - -
             buffer   db   1000 dup (?)
             ; - - - - - - -
                 lea  si, buffer   ; the buffer must be in the ds segment
                 cld                      ; increment

             out_loop:
                 lodsb
                 and  al, al              ; if 0, end of string
                 jz   quit_loop

                 mov  dl, al              ; move character to dl {9}
                 mov  ah, 5               ; int 21h function 5
                 int  21h                 ; print a character
                 jmp  out_loop

             quit_loop:
                 ; continue with the program 

             If you actually run this program, many printers will not print
             anything until they get an end of line signal ( 10d, 13d).


             ____________________

                8. Register DS can be overriden. We'll talk about that in the
             second part of this chapter.

                9. Int 21h (AH = 5) prints one character from DL to the
             printer. Why it's DL and not AL is a mystery.