HERCULES VIDEO CARD OWNERS

                                 (AND CGA USERS)

        I. HERCULES BACKGROUND

                The Hercules Graphics Adapter has proven to be a very 
        popular alternative to the IBM Monochrome Display Adapter. It
        is relatively inexpensive and, in addition to providing the
        crisp character display of the MDA, it also allows quite high
        resolution graphical displays.

                The original Hercules card has been cloned by every
        garage in Taiwan, and essentially every non-IBM computer with a 
        monochrome display has one installed.

                Normally, the Herc card may be set up in two modes: the
        first mode uses the upper 32K for text/graphics display and
        allows a Color Graphics Adapter (CGA) to run in the same system.
        The second mode uses the full 64K to provide two pages of 
        graphics and cannot be used in this mode with a CGA card.  Most
        users don't use two monitors, anyhow.

                The selection of mode may be made by hardware jumpers, or 
        it may be controllable with software.

                There have been a number of small utilities developed to
        enable Herc card owners to utilize the card's graphics capability 
        to emulate a CGA, thus providing the best of both worlds.  The 
        two I am most familiar with are SIMCGA and HGCIBM.  Both of these
        programs are widely available from shareware houses and BBS's.

        II. HERCULES MEMORY USAGE

                When a Herc card is used in monochrome mode, it emulates 
        the IBM MDA.  That is, the only memory available for video use is
        the first 4K, from B000 to B0FF - the remainder of the memory,
        from B100 to BFFF, or 60K, is available for other uses.

                When the Herc card is used with one of the CGA 
        simulators, it uses the bottom 32K, from B800 to BFFF.  Depending
        on the particular program in use, all of this memory may be used 
        or just the first 4K.  In either case, the upper 32K is still
        available, from B000 to B7FF.

                When using a Herc card for Hercules graphics, most 
        programs will try to take advantage of the entire 64K, so no
        'extra' memory will be available for other uses.

                With the above, admittedly brief, explanation in mind,
        you may determine for yourself whether it would be feasible to
        use the Herc card's 'free' memory to HILOAD your TSRs up there.




                By the way, some TSRs let you 'uninstall' them.  It would 
        seem that you could load some program, say SideKick, up into the
        video memory when working on a text application, and then 
        uninstall it when you want to do graphics work.  My advice is, 
        don't try it! Uninstalling TSRs is tricky at best, and when 
        they're loaded outside their 'normal' locations, this process 
        will almost always fail.

        III. CGA USERS
        
                Finally, CGA users may have noted that, when working in
        a text mode, thay also use only the first 4K of their memory, 
        from B800 to B8FF, leaving 28K free for experimentation.  The
        same cautions apply here as to the Hercules card when going into
        graphics mode.

        III. TRY IT OUT

                To try out the HILOAD software, you could use the Herc
        or CGA 'extra' memory to see if the stuff really works, and then
        decide if it would be worth it to get the upper memory in real 
        hardware.

                To see if the memory is addressable, run the utility
        MEMPEEK (you'll recognize it by Bernie Tern's logo).  When the
        display screen comes up, press "S" which will prompt you for a
        segment input.  Type B000 and press ENTER.  The display should
        switch to segment B000, and what is displayed will be what is on
        the screen at that point.  Then press "S" again, and enter a
        segment value of B100.  If the display repeats, then the card
        is remapping the memory into the upper 4K, providing what I call
        an overly slavish emulation of the IBM MDA.  Exit from the
        program (ESC) and either run the Hercules utility you got with
        the card, or dig out the documentation to set the jumper 
        switches.

                If all is well, running MEMPEEK at B100 and beyond should
        display random characters, indicating that memory is there and 
        may be addressed but is currently not filled with anything.

                By the same technique, examine memory at segment B800 and
        beyond. A Hercules card in FULL mode will show real memory at
        these locations, while a CGA card should show real memory from
        B800 to BFFF.

                As a final check, run the program ZERORAM with a block 
        input of B (i.e, type in ZERORAM B).  This will fill segment
        B000 with 64K of zero's.  Running MEMPEEK again should now show
        all zeros except in the upper 4K where the text is.
        
                When you are sure that real memory is available and will
        not conflict with the video display, you can try loading TSR's in
        this newfound space. 
        



                The utility VIDEOTSR looks at the interrupt vector table 
        and notices if any of them point to video memory. See the .DOC 
        file for details.  I occasionally use the video memory to load a
        TSR, and my graphics programs are executed from batch files.  This 
        utility is in all of them to remind me if I have a potential 
        disaster on my hands.

        IV. SET UP THE ENVIRONMENT VARIABLE

                As noted in the HILOAD documentation, the program uses a 
        DOS environment variable to determine where to start loading the 
        TSRs.  The SET command is used to establish values for the 
        environment.

                A. Using a Hercules card for text mode -

                        SET HILOAD=B100                 ;starting point
                        HILOAD                          ;reset program
                        HILOAD \TSR1                    ;load 1st TSR
                        HILOAD \DIR1\TSR2               ;load 2nd TSR

                                etc.

                        Up to 60K of TSRs can be installed

                B. Using a Herc card for CGA simulation -

                        SET HILOAD=B000                 ;starting point
                        HILOAD                          ;reset program
                        HILOAD \TSR1                    ;load 1st TSR
                        HILOAD \DIR1\TSR2               ;load 2nd TSR

                                etc.

                        Up to 32K of TSRs can be loaded

                C. Using a CGA card (in text mode) -
                        SET HILOAD=B900                 ;starting point
                        HILOAD                          ;reset program
                        HILOAD \TSR1                    ;load 1st TSR
                        HILOAD \DIR1\TSR2               ;load 2nd TSR

                                etc.

                        Up to 28K of TSRs can be loaded
        



        V. FINAL NOTES ON TSR SIZES

                Examining the size of the candidate TSR file using DIR
        or some such does not give a reliable indicator of the amount
        of memory a TSR will consume when actually loaded. The best way 
        is to load the TSR normally, and then use the MAPMEM utility
        provided to see how much memory is actually taken up when in
        use. Remember, some TSR's create buffers and such which will not 
        show up in the size of the program file.

                Also, HILOAD provides each TSR with a Program Segment 
        Prefix (PSP) just like DOS, so even a 10 byte TSR will take up
        at least 266 bytes (256 bytes for the PSP + 10 bytes for the
        program).  However, HILOAD does not copy the environment to
        upper memory, so a small saving is effected here.

                Finally, HILOAD aligns programs on paragraph boundaries
        (16 byte increments), so as many as 15 bytes per TSR may be 
        wasted.