Multiple Boot (Moot) Utilities

                                       by

                                   Eric Tauck
                               1304 Deerpass Road
                                Marengo, IL 60152

                             Compuserve: 72457,1557
                       Internet: 72457.1557@compuserve.com

     The Moot Utilities are a collection of device drivers and programs for
     implementing multiple DOS boot configurations using single CONFIG.SYS
     and AUTOEXEC.BAT files.  The device drivers CHOOSE, LOAD, and SKIP
     allow specific lines of the CONFIG.SYS file to be processed or
     ignored.  The programs MOOT.COM and INPUT.COM perform similar
     functions for batch files.  Additionally, the device drivers CLEAR,
     MOVE, and ECHO perform display functions from the CONFIG.SYS file.

     The files CHOOSE, CLEAR, ECHO, LOAD, MOVE, SKIP are DOS device
     drivers, even though their names do not end with SYS.  You may rename
     these files with a SYS extension as long as you also use the extension
     in the CONFIG.SYS file.  Device drivers are only 'run' via the
     CONFIG.SYS file.  The files INPUT.COM and MOOT.COM are executable
     programs that are usually run from batch files.

     If you do not place the device drivers in the root directory, you will
     need to specify a path in the DEVICE= statement.  You may also need to
     specify path when running the programs INPUT.COM and MOOT.COM.

     All of the device drivers, except CHOOSE, automatically remove
     themselves from memory once they have executed.  CHOOSE can be
     configured to remain resident or remove itself from memory.  When
     CHOOSE remains in memory, MOOT.COM can retrieve the configuration
     selection.

     The string arguments for the device drivers consist of sequences of
     characters enclosed by double-quote characters (").  Special back-
     slash codes may be used within strings:

       \"  double quote character
       \a  sound speaker (audible)
       \f  clear screen and move cursor to upper left (formfeed)
       \n  carriage return / linefeed (newline)

     Note that DOS usually converts the CONFIG.SYS file into uppercase
     when it is loaded, thus all letters in strings will be in uppercase.

     The keystroke arguments for CHOOSE and INPUT.COM consist of an ASCII
     code for standard keys and a negative scan code for special keys.  The
     codes for some commonly used keys are:

       Backspace          8
       Tab                9
       Enter              13
       Escape             27

       0 to 9             48 to 57

       a to z             97 to 122

       A to Z             65 to 90
       Ctrl-A to Ctrl-Z   1 to 26

       Left               -75
       Right              -77
       Up                 -72
       Down               -80
       Page Up            -73
       Page Down          -81
       Home               -71
       End                -79

       Insert             -82
       Delete             -83

       F1 to F10          -59 to -68

     The keystrokes for the device drivers are case-insensitive.  The
     keystrokes for INPUT.COM are case-insensitive only when the /U option
     is used.

     The color argument for CLEAR is a standard attribute byte.  An
     attribute byte consists of a color value (the foreground) plus a color
     value times 16 (the background).  Adding 8 to the attribute makes the
     foreground color brighter and adding 128 to the attribute makes the
     foreground blink.  The color values are:

       Black     0
       Blue      1
       Green     2
       Cyan      3
       Red       4
       Magenta   5
       Brown     6
       White     7

     Example: the attribute for bright white on blue is (Blue * 16) + White
     + 8 = (1 * 16) + 7 + 8 = 31.

     The programs INPUT.COM and MOOT.COM return an error code based on user
     input and the CHOOSE selection.  This error code is accessed in a
     batch file using the IF ERRORLEVEL batch command.

     The Moot Utilities have only been tested on PC DOS 3.2, MS DOS 4.01,
     and PC DOS 4.01.  Before changing the CONFIG.SYS and AUTOEXEC.BAT
     files on your hard disk, you should create a boot floppy from which to
     test the Moot Utilities and make sure they work properly on your
     system.

     What follows is a a description of each of the device drivers and
     programs.  At the end of this document are example CONFIG.SYS files
     and batch files using the Moot Utilities.

                                     CHOOSE
                                     ------

     The CHOOSE device driver allows you to dynamically select one of up to
     nine different blocks of lines in the CONFIG.SYS file to be processed.
     When CHOOSE is executed, the user will be prompted for the
     configuration to use.  The CONFIG.SYS file may contain multiple CHOOSE

     statements, as long as the blocks are not overlapped or nested.  The
     syntax for CHOOSE is:

       DEVICE=CHOOSE [prompt] [time] [default] [0]

       DEVICE=#1 [prompt] key

       :
       <normal CONFIG.SYS statements>
       :

       DEVICE=#2 [prompt] key

       :
       <normal CONFIG.SYS statements>
       :

       DEVICE=#END [prompt]

       -----

       prompt   A string to display.

       time     The number of seconds to wait for a response from the user.
                If the user does not respond, the default configuration
                block is used.  If no time is specified, CHOOSE will wait
                indefinitely.

       default  The default configuration block number to use if no key is
                pressed.  This value must be in the range 1 to 9 (it is not
                range checked).  If no default is specified, the first
                block will be selected.

       0        If zero is specified on the CHOOSE line, the resident
                kernel of CHOOSE will not be loaded.  Use this option if
                you do not need MOOT.COM to check the configuration or you
                use multiple CHOOSE commands.

       key      The keystroke that selects this block.

     When a choice is made, by keystroke or default, one (and only one) of
     the configuration statement blocks delimited by the #1, #2, ..., #9,
     or #END device statements will be loaded.

     Note: the device names #1 through #9 and #END are only used to delimit
     blocks of statements.  If CHOOSE works properly, the operating system
     will not attempt to load these statements as devices.  The character
     sequences #1, #2, #3, #4, #5, #6, #7, #8, #9, and #END can only be
     used as part of a CHOOSE.

     All the prompts are optional.  If a prompt is specified with the #END
     statement, the keystroke will be echoed, otherwise the keystroke will
     not be echoed.

     CHOOSE remains resident by default.  If zero is specified on the
     command line, CHOOSE will not remain resident.  If CHOOSE remains
     resident, MOOT will return the selection number.  If multiple CHOOSE's
     are resident, MOOT will return the selection number of the last CHOOSE
     loaded.  CHOOSE uses less than 150 bytes of memory when resident.


     The CHOOSE driver may crash if a default value is greater than 9 or
     there is no #END statement.

                                      CLEAR
                                      -----

     The CLEAR device clears the screen.  The syntax for CLEAR is:

       DEVICE=CLEAR [color]

       -----

       color  An attribute byte.

     If no color is specified, the attribute at the cursor location is used.

                                      ECHO
                                      ----

     The ECHO device displays a string.  The syntax for ECHO is:

       DEVICE=ECHO string

       -----

       string  The string to display.

                                    INPUT.COM
                                    ---------

     This program waits for specific keystrokes and returns an error code
     based on the keystroke.  Batch files can use this code to branch for
     specific input.  The syntax for INPUT.COM is:

       INPUT [/U] [/E] [/Tn] [/Dn] n[, n, ...]

       -----

       /E   Echo the keystroke.

       /U   Convert all ASCII codes to uppercase.  This option makes the
            input case-insensitive.

       /Fn  Display the file n before input.  This option lets you set up
            the screen before performing the input.  If you have ANSI.SYS
            loaded, you can clear the screen and position the cursor using
            ANSI sequences imbedded in the file.

       /Tn  Wait n seconds for response.  If no response if given, the
            default (/D) value is returned.  If this option is not
            specified, INPUT.COM waits indefinitely for input.

       /Dn  Return code n if timeout.  If this option is not specified,
            INPUT.COM will return 0.  This option is only meaningful when
            the /T option is used.

       n    A keystroke to wait for.  Multiple keystrokes may be specified
            and at least one keystroke is required. The error code returned
            is based on the position of the keystroke on the command line.
            The first keystroke returns error code 1, the second returns

            error code 2, etc.

                                      LOAD
                                      ----

     The LOAD device lets you selectively load or ignore the next line in
     the CONFIG.SYS file.  When LOAD is executed, you are prompted as to
     whether or not you wish to load the next line.  The syntax for LOAD
     is:

       DEVICE=LOAD prompt [time]

       -----

       prompt  The prompt to display.  A " (Y/N)? " is automatically
               appended to the string.

       time    The number of seconds to wait for a response from the user.
               If the user does not respond, the next CONFIG.SYS line will
               not be loaded.  If no time is specified, LOAD will wait
               indefinitely.

                                    MOOT.COM
                                    --------

     This program returns the selection number (1 to 9) from the CHOOSE
     driver.  Batch files can use this code to branch for specific CHOOSE
     configurations.  A code of 0 is returned if the CHOOSE driver isn't
     installed and a code of 255 if CHOOSE is installed but detected an
     installation error.  The syntax for MOOT.COM is:

       MOOT

                                      MOVE
                                      ----

     The MOVE device positions the cursor, presumably before something is
     displayed.  The syntax for MOVE is:

       DEVICE=MOVE row column

       -----

       row     is the screen row

       column  is the screen column

                                      SKIP
                                      ----

     The LOAD device lets you selectively skip or load the next line in the
     CONFIG.SYS file.  When SKIP is executed, you are prompted as to
     whether or not you wish to skip the next line.  The syntax for SKIP
     is:

       DEVICE=SKIP prompt [time]

       -----

       prompt  The prompt to display.  A " (Y/N)? " is automatically

               appended to the string.

       time    The number of seconds to wait for a response from the user.
               If the user does not respond, the next CONFIG.SYS line is
               will not be skipped.  If no time is specified, SKIP will
               wait indefinitely.

                                    Examples
                                    --------

     Here are example CONFIG.SYS and AUTOEXEC.BAT files, which are similar
     to the actual files I use on my system.  Note that the Moot files are
     stored in a directory called BOOT on drive C:.

     This CONFIG.SYS has three basic configurations: standard, minimum, and
     debugging.  The configuration is selected by pressing a number one,
     two, or three.  The standard configuration is used most of the time
     and is selected by default after four seconds.  The minimum
     configuration loads as little as possible for high memory requirement
     applications.  The debugging configuration forces my disk cache
     (NCACHE-S) to leave 640K of extended memory available so I can perform
     virtual debugging with Turbo Debugger.  The standard configuration
     also allows me to optionally load the device driver TDH386.SYS.

       CONFIG.SYS
       ----------

         device=c:\boot\CHOOSE "\f+--------------+"  4

         device=#1 "| 1. STANDARD  |" 49

         buffers=7
         stacks=8,64
         device=c:\os\ramdrive.sys 566 512 32 /e
         device=c:\os\himem.sys
         device=C:\boot\LOAD "LOAD TD386" 3
         device=c:\td\tdh386.sys
         device=c:\nu\ncache-s.exe /-w a: -a b: -a

         device=#2 "| 2. MINIMUM   |" 50

         buffers=10
         stacks=0,0
         lastdrive=f

         device=#3 "| 3. DEBUGGING |\n+--------------+" 51

         buffers=7
         stacks=8,64
         device=c:\os\ramdrive.sys 557 512 32 /e
         device=c:\td\tdh386.sys
         device=c:\nu\ncache-s.exe /ext=-640 /-w a: -a b: -a

         device=#END

     This AUTOEXEC.BAT reflects the three main configurations stored in the
     CONFIG.SYS file.  The first action performed is to run MOOT.COM to
     retrieve the configuration selection.  The standard and debugging
     configurations jump to the same locations.  My menu system is started
     by running C:\BAT\M, and at the end of this file, a prompt is

     displayed and if <ESC> is pressed in four seconds, my menu system is
     skipped.  If <SPACE> or <ENTER> is pressed, the menu system is entered
     immediately.  INPUT.COM is used to enter or skip the menu system.  The
     prompt displayed by INPUT.COM is stored in the file MENU.TXT.

       AUTOEXEC.BAT
       ------------

         c:\boot\moot
         IF ERRORLEVEL 3 GOTO standard
         IF ERRORLEVEL 2 GOTO minimum
         IF ERRORLEVEL 1 GOTO standard

         :standard

         c:\boot\mouse
         GOTO done

         :minimum

         c:\os\subst f: c:\trash
         GOTO done

         :done
         set nu=c:\nu
         CALL c:\bat\normal

         c:\boot\input /fc:\boot\menu.txt /t4 32 13 27
         IF ERRORLEVEL 3 GOTO skip
         c:\bat\m

         :skip
         c:
         cls