HARDWARE-SPECIFIC INFORMATION

Two of the DCA/Intel CAS functions, Get Hardware Status (12H) and Run
Diagnostics (13H), return information that varies depending on the kind of
hardware used to implement the specification.  This appendix lists that
hardware-specific information for the Intel Connection CoProcessor.

Be aware that if your code relies on the information returned by these
functions, that code might not work correctly on hardware other than the
Connection CoProcessor.  In addition, Intel reserves the right to change
without notice the information these functions return.

Get Hardware Status (12H):

Upon successful completion, this function returns a 51-byte status area
pointed to by DS:DX.  The status area contains the following information:

          Byte 0:
            Bit 7 - set if the hardware is busy sending or receiving.
            Bit 6 - set if this is the last page
            Bit 5 - set if no data on current page
            Bit 4 - set if re-transmit request for current page being
                     transmitted
            Bit 3 - set if NSF mode active
            Bit 2 - reserved
            Bit 1 - reserved
            Bit 0 - reserved

          Byte 1: Number of 1K-byte areas of free buffer space

          Byte 2:
            Bit 7 - set if the Connection CoProcessor has document(s) to
                     send
            Bits 6 -0:   number of discrete pages are in the buffer.

          Byte 3: Number of retries left to dial this number

          Byte 4: Page number to re-transmit

          Byte 5:
            Bit 7 - set if the Connection CoProcessor is originating a call
            Bit 6 - set if a Facsimile message will be sent
            Bit 5 - set if off hook (on line)
            Bit 4 - set if ring detected and receive is enabled
            Bit 3 - set if buffer dumped on receive
            Bits 2 - 0 tell what sequence state the hardware is in.  The
                     states are:
                           0 - idle
                           1 - dial
                           2 - answer
                           3 - transmit
                           4 - receive
                           5 - pre-message
                           6 - post-message
                           7 - disconnect

          Byte 6:
            Bit 7 - reserved
            Bits 6 - 4:
              6  5  4   Baud Rate
              0  0  0   300 baud   (SDLC mode)
              1  0  0   2400 baud  (V.27 ter)
              1  0  1   4800 baud  (V.27 ter)
              1  1  0   7200 baud  (V.29)
              1  1  1   9600 baud  (V.29)

            Bits 3 - 0: reserved and should be set to 0110

          Bytes 7, 8, 9: reserved

          Byte 10:
            Bit 7 - set if the modem option is installed
            Bit 6 - set if Connection CoProcessor has control of the DAA
                     (not latched)
            Bit 5 - set if offhook (not latched)
            Bit 4 - set if ring is detected (not latched)
            Bit 3 - set if data in command buffer (not latched)
            Bit 2 - set if DMA channel 1 is in use, cleared if DMA channel
                     3 is in use.
            Bit 1 - set if line length compensation bit 1 is set (not
                     latched)
            Bit 0 - set if line length compensation bit 0 is set (not
                     latched)

          Byte 11:
            Bit 7 - reserved
            Bit 6 - not used
            Bit 5 - set if spare switch is open
            Bit 4 - set if fax ADR1 switch is open
            Bit 3 - set if fax ADR0 switch is open
            Bit 2 - set if alternate interrupt switch is open
            Bit 1 - set if COM SEL 1 switch is open
            Bit 0 - set if COM SEL 0 switch is open

          Byte 12:
            Bit 7 - reserved
            Bit 6 - set if the auxiliary relay forced on
            Bit 5 - set if the modem select relay forced on
            Bit 4 - set if offhook relay forced on
            Bit 3 - 9600 bps (V.29) enabled
            Bit 2 - 7200 bps (V.29) enabled
            Bit 1 - 4800 bps (V.27 ter) enabled
            Bit 0 - 2400 bps (V.27 ter) enabled

          Byte 13: reserved

          Byte 14: low byte of error count (received errors or
                     retransmission requests.)  This value is reset
                     whenever the hardware goes busy; thus it represents
                     the errors for the most recent activity.

          Byte 15: high byte of error count

          Byte 16: low byte of file length for nonstandard file format
                     (NSF) in bytes

          Byte 17: file length for NSF in bytes

          Byte 18: file length for NSF in bytes

          Byte 19: high byte of file length for NSF in bytes

          Bytes 20 - 29: reserved

          Bytes 30 - 50: CSID

          Bytes 51 - 127: reserved


Run Diagnostics (13H):

If you use this function to report on the progress of the diagnostics and
the value returned in AX is a negative number, the Connection CoProcessor
failed the diagnostics.  Bits 0-3 contain more information.

     Bit 3 -    Set if 9600 bps fax modem module failed
     Bit 2 -    Set if SDLC chip failed
     Bit 1 -    Set if RAM failed
     Bit 0 -    Set if ROM checksum failed