Supplemental doc file CdCom protocols.

Protocols for CdCom are dynamic, meaning you can add/modify/delete at will.

All protocols mentioned in this doc file will be posted on Main Ave Books
(805) 987-7245 1200/2400/9600 HST-V.32.  They are all FREQ'able by filenames
mentioned in this doc file.

PROTOCOL FILES:

PROTOCOL.MNU   -  Menu dump file for protocols
PROTOCOL.DEF   -  Main configuration file that CdCom reads
PROTOCOL.BAT   -  Protocol batch file.
PROTOCOL.DOC   -  This file

Cdcom passes the following parameters via DOS variables %1, %2, %3 and %4.

%1 - Protocol name

%2 - Port number [1-4].

%3 - Baud Rate.  This is the value it reads from CALLINFO.BBS line 2.
     This is not the locked port speed (or at least should not be).

%4 - Filename to be sent.

PROTOCOL.MNU:

This is a simple text file that is dumped to the user when they change
or select a protocol.  It does not reflect what protocols are really
active.  You can modify this at will to have whatever format you like.
I include a sample one in the distribution file but you don't have to
keep that format.

PROTOCOL.DEF:

This is the main configuration file for adding/modifying/removing
protocols.  Format goes as follows:

1    2    3  4   5   6   7    8   9   10  11
----------------------------------------------
z,Zmodem,30,115,225,450,940,1200,1400,0,s or b

1:  Menu select command.  If the user presses z then they will get
    zmodem in this example.  I reserve Q and q for <Q>uit back to Menu.
    All other letters, numbers, characters are fair game. I convert it to
    upper case (if its a letter) in the program.  This must only
    be a single character.

2:  Protocol name.  This is the name that will be shown to the user
    when they select a protocol, also the name that will be passed to
    the protocol.bat file.  Insure you match this name exactly with the
    test name (%1 ==) in the batch file as it is case sensitive.  This
    name is also used in the log entries.

Items 3-9 are the character/second transfer rates for the given
protocol and baudrate.  This value is given to you by protocols like
DSZ and superk when the transfer is complete.  Other packages may do the
same.  If not you will have to time it yourself.  This give you the option
to tweak them to your hearts desire at will for each protocol and baudrate.
These are the values that will be used when calculating file transfer times.

 3:  ch/sec for 300 baud
 4:  ch/sec for 1200 baud
 5:  ch/sec for 2400 baud
 6:  ch/sec for 4800 baud
 7:  ch/sec for 9600 baud
 8:  ch/sec for 19200 baud
 9:  ch/sec for 38400 baud

10: This is the DOS errorlevel that is passed for a successful
    file transfer.  Most large packages like DSZ and superk pass
    an errorlevel 0 for success, 1 for any error.  CdCom will check
    this on return.  If a non-success error code is returned it will
    ask the user if they want to re-attempt the transfer, saving the
    hassle of re-compressing the disks to send.

11:
    This specifies whether or not the protocol is a batch or single
    file protocol.  To be batch the protocol has to be able to read
    a filename for the files to transfer.  DSZ, Puma, and Lynx (that
    I know of) do this with a @ before the filename.  Ex:
    @c:\cdcom\batch.dsz
    passed to DSZ will tell it to read the filename c:\cdcom\batch.dsz
    for the filenames to send.  This does away with the dos command line
    limitation for most protocols.  CdCom will automatically put the @,
    use the path from line 2 of cdcom.def and add the \batch.dsz so all
    you need to do is check to see if the protocol supports the @filename
    or not.

Sample PROTOCOL.DEF file:

The ch/sec rates may or may not be correct.  I did not verify most
of them so you may want to check them.

z,Zmodem,30,115,225,450,940,1200,1400,0
t,MobyTurbo,30,115,225,450,940,1200,1400,0
w,Wxmodem,30,110,210,450,940,1000,1200,0
y,Ymodem,30,110,175,400,900,900,1000,0
b,Ymodem-Batch,30,115,210,410,920,1000,1100,0
x,Xmodem,30,100,175,390,880,900,950,0
s,Sealink,30,100,175,390,880,900,950,0
m,Megalink,30,100,175,390,880,900,950,0
k,Kermit,30,100,175,390,880,900,950,0
9,K9Xmodem,30,100,175,390,880,900,950,0
j,Jmodem,30,100,175,390,880,900,950,0
8,Super8K,30,100,175,390,880,900,950,0
l,Lynx,30,100,175,390,880,900,950,0


BATCH FILE EXAMPLES:

Here are some examples for various protocol packages.  I will briefly
cover the few I found, it is up to you however to read the docs for
each protocol to get it to work correctly on your system, especially if
you are running locked port or anything like that.  The examples shown
should work for most systems.  PROTOCOL.BAT is already configured for
a non-locked port system and should need minimal editing even to work
with a locked port system.

DSZ:     (DSZ0411.ZIP)

DSZ supports Xmodem, Xmodem CRC, Xmodem 1k (also called Ymodem),
Ymodem Batch, Ymodem-G and Zmodem.  Versions after 06-07-88 must be
registered (ie: run putsnp) before Ymodem-G will work.

By default DSZ will use com1 (port 1).  To change it to another port
you could say DSZ port 1 on the command line but a more elegant
solution is to put:

SET DSZPORT=2  [or DSZPORT=3, DSZPORT=4]

in your autoexec.bat file.  DSZ will read this on start up.

DSZ also uses the comport at whatever baud rate it is currently set at.
There is no need to tell it what baud rate to use.

So commands to use DSZ with CdCom would be:

Zmodem
dsz sz %4

Xmodem    DSZ will check for checksum or CRC error detection automatically
dsz sx %4

Xmodem1k  (ymodem)  -k for 1k blocks
dsz sx -k %4

If you require handshaking for zmodem then you can add that into the
batch file.  ex: DSZ handshake on sz %4


SUPERK:     (SUPERK44.ZIP)

Superk supports Xmodem, Xmodem CRC, Ymodem (Xmodem 1k), WXmodem (windowed
xmodem), Jmodem, K9Xmodem, Super8K and MNP Super8K-G.  These are the
ones supported in Ver 4.4.  Earlier versions like 3.3 do not support
the MNP Super8k or Jmodem.  There are also command line differences
between the versions (I have only seen 3.3 and 4.4).  Version 4.4
will be posted on Main Ave Books if you are interested in it, otherwise
it can be obtained at the authors BBS at (206) 725-9233 12/24/9600.

Superk requires that you pass it the port number and baudrate.  These
are passed via %2 and %3 from CdCom.  It may also require the locked
port speed, this can be hardcoded into the protocol.bat file.

Examples (for ver 4.4):

Px      - Comm Port to use.
Sbaud   - Port Speed.
F name  - Filename to xfer

Protocols:
S is for Send.

X = Xmodem
C = CRC Xmodem
Y = Ymodem (1k Xmodem)
W = WXmodem
J = Jmodem
K = K9Xmodem
S = Super8K
M = MNP Super8K-G

Wxmodem
superk p%2 s%3 sw f %4

Super8k
superk p%2 s%3 ss f %4

for ver 3.3 an example would be:

t=protocol to use (same as above, sans J and M)
d=direction of transfer (s=send)

Super8k
superk p%2 s%3 ts ds f%4

Wxmodem
superk p%2 s%3 tw ds f%4

LYNX and PUMA:

Latest versions LYNX302.ZIP  Lynx Ver 3.02 and
                PUMA100.ZIP  Puma Ver 1.00

Lynx and Puma are easy to set up as they use the DSZPORT environment parameter
and like DSZ use the port at whatever baud rate it is currently set at.
Read the brief but thorough doc files in the zip files for other
configuration parameters if they are needed (CTS, handshaking, etc).
They also support the @filename for batch transfers.

Lynx
lynx s %4

Puma
puma s %4


MSKERMIT:

Latest version found was KERM231A.ZIP  - MS-Kermit  Ver 2.31a

mskermit requires a set-up file called MSKERMIT.INI, the minimum lines
you should have in it are:

set block-check-type 3
set port COM1

block-check-type 3 is the maximum error detection ms-kermit supports.
ms-kermit will use the baud, parity, etc that the port (given by set port)
is already set at.  It also works with locked ports.

Other protocols available from Main Ave Books:

PCZ0221.ZIP   - Sealink, Zmodem, Xmodem Chksum/CRC, Xmodem 1k (Ymodem) Ver 2.21
CLINK120.ZIP  - Sealink + C Source   Ver 1.2
MLINK16.ZIP   - Megalink  Ver 1.6

No option for Bi-Modem at this time, since it requires special files
to be created.  I have yet to put any serious time into bi-modem so
dunno if it feasible or not to work with the door.