DISKLIST LASER COMMAND GUIDE

     This is a guide to help you use DISKLIST on a HP LaserJet.  Since
     other brand laser printers emulate the HP PCL (Printer Control
     Language) this information is applicable to most laser printers.
     The purpose is to help you customize the laser commands that
     DISKLIST sends to the printer.  This will give you control over
     how and where DISKLIST is printed.

     The basic syntax of a PCL command is:

          The first character is ESC

          ESC is followed by printable ASCII characters - letters,
          numbers and symbols.

          The last character is always an uppercase letter.

     The simplest command is to reset the printer - ESC E.

     There is a space after ESC in this documentation for clarity.  In
     the actual HP laser command there is no space.  In the DISKLIST
     laser command editor, the ESC is displayed as a left arrow with
     no space.

     ESC is usually followed by two characters that identify a family.
     The first is usually a symbol and the second a lowercase letter.

     These are followed by a number.  It can be an integer or a
     decimal to 4 decimal places, depending on the command.

     Example:

          To set the point size to 12, the command is:   ESC (s12V

          To set the pitch to 10 characters per inch:    ESC (s10H


     Note that the integers match the desired value of the parameter,
     and the point command ends in V for vertical and the pitch
     command ends in H for horizontal.  Both commands have the family
     characters (s.

     One final rule.  Commands that have the same two characters after
     ESC can be grouped together without repeating the ESC or the
     common 2 characters.  In this case, the last letter of each
     imbedded command must be lowercase.

     Example:

          Using the commands of the previous example to form one
          command produces:



                                      -1- 




                           ESC (s12v10H

          Note the v is now lowercase.

     Warning:  Case is very important.  Also, do not confuse the
     number 0 and the letter O, or the number 1 and the lower case L.
     If you are not getting the results that you expect, look at your
     commands very carefully for these substitutions.


     LASER COMMAND SETUP

     DISKLIST has a set of laser commands for each format.  They are
     in the file DISKLIST.LSR.  It also has a laser command editor,
     accessed with FK 6, so you can easily change them.  Remember to
     save the changes you make in this file with FK 9.  The laser
     commands are setup in the following categories:

                             Symbol
                             Spacing
                             Pitch & Point Size
                             Orientation
                             Top Margin
                             Lines per inch
                             Left Margin, Row

                             Reset

     You can put any commands on any line.  These categories are for
     reference only.  Although the order is important because the
     value of one command effects the operation of other commands.
     This will be discussed later with left margin and row.

     When laser printer is selected, DISKLIST concatenates all of the
     commands in the first 7 categories and sends them to the printer.
     After the list is printed, DISKLIST sends the commands in the
     eighth category, Reset.

     You don't have to have any laser commands.  Many of these
     parameters are inherent in the default font or can be set by
     controls on the printer.  You may need a few commands, such as
     top and left margin, and lines per inch.  The editor has a key to
     delete the commands on one line, FK 7, or all commands for a
     format, FK 8.

     Laser commands are all printable ASCII characters except ESC.
     The IBM character set displays ESC as a left pointing arrow.  So
     does DISKLIST.  To enter ESC on the command line, just press the
     ESC key.  Since the ESC key is used for input, press Function
     Key 10 to exit the editor.  I try to make my software consistent,
     so DISKLIST will quit all functions when FK 10 is pressed.




                                      -2- 




     SYMBOL

     Within a font set are many symbol sets.  The IBM lines that
     DISKLIST uses to print the frames are in the symbol set called
     IBM-PC(USA).  The command to use this symbol set is ESC (10U.

     Some fonts do not have this symbol set, so the printer will
     select another set close to it, but that symbol set probably
     won't have the IBM lines.  In that case you can use the ASCII
     lines or select a label format that doesn't have lines.


     SPACING

     This command sets the character spacing to proportional or fixed.
     Since DISKLIST prints columns and a frame, the fixed spacing must
     be selected.  The command for fixed spacing is ESC (s0P.  For
     proportional spacing the command is ESC (s1P.

     Most fonts only come in one spacing, so this command is probably
     ignored.  And, you don't want to use a proportional font.


     PITCH AND POINT SIZE

     These commands were used in the example above.  DISKLIST uses two
     sets, one for normal and one for compressed.  They are:

          Normal         ESC (s10.00h12.0V

          Compressed     ESC (s16.66h8.5V


     ORIENTATION

     This command determines whether the list will be printed in the
     Portrait or Landscape mode.  The commands are:

          Portrait     ESC &l0O

          Landscape    ESC &l1O


     TOP MARGIN

     This command positions the list from the top of the page.
     Remember, with most lasers there is a border around the page
     where the printer cannot physically print.  If you set it up to
     print there, nothing will be printed in this area.  The command
     for the number of lines down from the top is ESC &l#E where #
     represents the number of lines.




                                      -3- 




     LINES PER INCH

     Lines per inch control the vertical spacing of the data lines.
     There are two ways to select this.  Either select a specific
     number of lines per inch, or select a fractional vertical motion
     index.

     The lines per inch command is ESC &l#D where # is the number of
     lines per inch.  However, unlike most of the other commands, this
     command only allows specific numbers.  They are 1, 2, 3, 4, 6, 8,
     12, 16, 24, and 48.

     Line spacing by vertical motion index command is ESC &l#C.
     # represents the number of 1/48 inch increments and can be a
     decimal.  The following table illustrates some useful values but
     any value is acceptable by PCL.


                               Lines
                                per
                               Inch          #

                                6.0         8.00
                                6.5         7.38
                                7.0         6.86
                                7.5         6.40
                                8.0         6.00
                                8.5         5.65
                                9.0         5.33
                                9.5         5.05
                               10.0         4.80
                               10.5         4.57
                               11.0         4.36
                               11.5         4.17
                               12.0         4.00


     LEFT MARGIN

     This command positions the list from the left edge of the page.
     The command for the column number to start printing in is
     ESC &a#L where # represents the column number.  This is important
     when you position the list on labels.  The positioning of the
     left margin is based on the current horizontal motion index which
     was set by the pitch command.


     ROW

     Row positions the start of the list down from the top margin,
     not the top of the page.  The command is ESC &a#R where # is the
     number of lines below the top margin.  Since it is in the &a
     family, DISKLIST puts this in one command with the left margin.


                                      -4- 




     The positioning of the row based on the current vertical motion
     index which was set by the lines per inch command.


     DEFAULT COMMANDS

     FK 6 will insert these commands in the editor for the selected
     format only:

                     Pitch ==>   Normal             Compressed

          Symbol              ESC E ESC (10U        ESC E ESC (10U
          Spacing             ESC (s0P              ESC (s0P
          Pitch & Point Size  ESC (s10.00h12.0V     ESC (s16.66h8.5V
          Orientation         ESC &l0O              ESC &l0O
          Top Margin          ESC &l0E              ESC &l0E
          Lines per inch      ESC &l6D              ESC &l8D
          Left Margin, Row    ESC &a0l0R            ESC &a0l0R

          Reset               ESC E                 ESC E

     The symbol command is preceded by the ESC E, the reset command.
     This forces a page eject in some printers, so you may want to
     eliminate it.  If laser printer is selected, CTRL E will also
     send a page eject from the control window.  If you want to print
     more than one list on a sheet, remove the reset, then use CTRL E
     to eject the page.


     DOWNLOAD FONT

     DISKLIST sends the following commands to the laser when it
     downloads your font that you have selected from the Download
     Window.

                    Reset                    ESC E
                    Font ID Assignment       ESC *c#D
                    The Font File
                    Font ID Assignment       ESC *c#D
                    Make Font Permanent      ESC *c5F
                    Select Font              ESC (#X

     # is the font number.  DISKLIST generates a number by adding 70
     to the sequence number of the font in the font selection window.
     Except selection 10, which is assigned the number 70.  So the
     range of font ID numbers that DISKLIST assigns is from 70 to 79.
     You can then reselect a font with the command ESC (#X.  The
     downloaded fonts are lost when the printer is turned off.







                                      -5- 




     MORE

     This is just a beginning of learning about PCL.  It is sufficient
     to produce useful lists and labels.  There are many more commands
     that may be of help in configuring DISKLIST to print lists
     exactly as you like.  They are all in your printer manual.  I
     hope this write-up helps you to read and understand the laser
     printer manual.


     HELPFUL HINTS

     If you download or select a font, try deleting all commands (use
     FK 8 in the editor), then insert a command for lines per inch and
     maybe commands for top, left margin, and row.  Otherwise the
     commands may override the selected font and the printer may
     select another.

     If the vertical IBM lines look like dashes, squeeze the lines
     together by printing more lines per inch.  Use the ESC &l#C
     command.

     With a laser printer you can create your own list formats.  For
     example, if you have a 6 point 25 pitch font, you can use the
     format for 5.25 inch 5 across to print a list that can hold 165
     file names and be cut to fit the size of a 3.5 inch disk.  Then
     tape the list to the back of the diskette with one small piece of
     tape placed along the edge of the diskette that doesn't go into
     the drive.  You then have a list that stays attached to the
     diskette even when it is inserted in the drive.

























                                      -6- 




     DISKLIST LASER COMMAND REFERENCE CARD



                    Reset                   ESC E

                    Point Size              ESC (s#V
                    Pitch                   ESC (s#H

                    Portrait                ESC &l0O
                    Landscape               ESC &l1O

                    Top Margin              ESC &l#E
                    Left Margin             ESC &a#L

                    Row                     ESC &a#R

                    Lines Per Inch          ESC &l#D

           Valid Values of # for lines per inch are:

                1, 2, 3, 4, 6, 8, 12, 16, 24, and 48.

                    Vertical Motion Index   ESC &l#C

           # represents the number of 1/48 inch increments and can be
           a decimal.  The following table illustrates useful values:

                               Lines
                                per
                               Inch          #

                                6.0         8.00
                                6.5         7.38
                                7.0         6.86
                                7.5         6.40
                                8.0         6.00
                                8.5         5.65
                                9.0         5.33
                                9.5         5.05
                               10.0         4.80
                               10.5         4.57
                               11.0         4.36
                               11.5         4.17
                               12.0         4.00










                                      -7-