______________
                              |              |
                              |    LAYOUT    |
                              |______________|

                           An Area Planning Program

                                 written by

                              Martin L. Waldman

                                Version 2.0
                               Copyright 1991
                             All rights reserved


                                published by
                               Software Co-op
                            5437 Honey Manor Dr
                           Indianapolis IN 46241


                              TABLE OF CONTENTS
                                                       Page
               PART 1. OVERVIEW
                        1.1  Introduction .............. 1
                        1.2  Upgrade from Version 1 .... 1
                        1.3  Starting LAYOUT ........... 2
                        1.4  Exiting from LAYOUT ....... 2
                        1.5  Screen Displays ........... 3
                        1.6  Using the Keyboard ........ 4
                        1.7  Selecting a LAYOUT File ... 5
                        1.8  Selecting a Sheet ......... 5


               PART 2. SHEET FUNCTIONS
                        2.1  Overview .................. 6
                        2.2  Sheet Framework Menu ...... 6
                        2.3  Area Contents Menu ........ 9
                        2.4  Drawing the Sheet .........10
                        2.5  Printing the Sheet ........11


               PART 3. FILE FUNCTIONS
                        3.1  Set Titles/Printer Type ...12
                        3.2  Print Inventory ...........14
                        3.3  Make a .CSV File ..........14


               PART 4. A PRACTICAL EXERCISE             15

               PART 5. LICENSE INFORMATION              24


     PART 1. GENERAL INFORMATION       LAYOUT 2.0 User Manual     Page  1

     1.1   INTRODUCTION

     LAYOUT is a program that you can use to describe, display, and print a
     drawing of any two-dimensional area.

     An area may be a floor plan of a home or business establishment, a map
     of a piece of land, a description of the contents of a printed page,
     the design for a quilt, the LAYOUT of components on a circuit board,
     etc. -- in fact any space for which you know the dimensions.

     LAYOUT is small (under 20k),fast, and easy to use. Menus are presented
     to allow you to initiate functions by pressing a single key.

     NOTE: In this manual a letter inside angle brackets is used to
     indicate a single key press -- the shift key need not be held down.

     All of the information for displaying and printing an area is entered
     from the keyboard and stored in a "sheet". Files may contain up to 26
     different sheets -- each describing a different area.

     New files and sheets are created as needed by the program. New or
     changed files are automatically written to disk whenever you exit from
     the program or when you select a different file.

     The program will run on any computer system that operates using
     DOS 2.x or higher, and has 256k of memory and a color monitor.


     1.2   UPGRADE FROM VERSION 1

     Version 2.0 has been expanded with functions that enable you to use
     either an Epson compatible dot matrix printer or an HP LaserJet
     compatible laser printer. You can now design, maintain, and print an
     inventory, and create inventory files that may be directly imported
     into most spreadsheet programs.

     The data files have been enlarged to accommodate the upgrade and now
     carry the extension ".LY2" --  NOTE: Because of the file size
     enlargement only 26 sheets per file are allowed instead of the 30
     sheets in version 1.

     Files that you may have created with version 1 (.LYO) can be converted
     to the new format with the conversion program LYOCONV.COM contained on
     the distribution diskette.

     You must log onto the directory where the .LYO files are located and
     then run LYOCONV. All of the version 1 files on the directory will be
     converted to .LY2 files -- the version 1 files will not be destroyed.

     NOTE: The files on the version 2 distribution diskette and files
     converted by LYOCONV specify a dot matrix printer.


     PART 1. GENERAL INFORMATION       LAYOUT 2.0 User Manual     Page  2

     1.3   STARTING LAYOUT

     The LAYOUT distribution diskette contains the program and sample data
     files. The program can be run directly on diskette or copied to a hard
     disk.

     LAYOUT reads and writes data files on the current default drive and
     directory. The program itself may be resident on any directory as long
     as DOS can find it or you include the path name in the command line.

     To start LAYOUT you must log on to the drive and directory where the
     LAYOUT data files are to be stored and, at the DOS prompt, enter  the
     command    LAYOUT

     From the first display you must select a file by entering a number
     (see 1.7  SELECT A LAYOUT FILE) -- if you do not the program
     terminates.

     Then you must select the sheet to be active (see 1.8  SELECT A SHEET).

     The Function Menu is then displayed. Pressing a letter key will invoke
     the named function. When you exit from a function you will be returned
     to the Function Menu.

     1.4   EXITING FROM LAYOUT

     If you press the <X> key at the Function Menu display, the following
     message will appear:   Exit from LAYOUT (Y/N) ?

     Pressing the <Y> key will exit from LAYOUT to the DOS prompt. Pressing
     any other key will return you to the Function Menu.


     PART 1. GENERAL INFORMATION       LAYOUT 2.0 User Manual     Page  3

     1.5  SCREEN DISPLAYS

     LAYOUT uses two different types of displays. On graphic screens a
     sidebar (first ten columns) is used to display information describing
     the current drawing, instructions for continuing, and printer status
     messages. The remainder of the screen displays a drawing of the active
     sheet.

     Text displays are used for file and sheet selection, menus, and data
     entry functions. For example, the Function Menu looks like this:

      ____________________________________________________________________
     /                                                                    \
     LAYOUT 2.0      Floor Plan C - The Erehwon Apt      13:13:40   1/01/91
       Sheet  1/7  Apartment Overview   Area Length 480   Width 276 inches
     ======================================================================
                               Function Menu

             Select a different Sheet         select a LAYOUT File

             revise the sheet Framework       set Titles/printer Type

             Change the area Contents         print Inventory

             Draw this sheet                  Make a .CSV file

             Print this sheet

     ======================================================================
         Press S, F, C, D, P, L, T, I, M, or eXit to quit LAYOUT

     \____________________________________________________________________/


     The top two lines on the screen are the "Banner". Line one of the
     Banner shows the system name and version number, the current active
     plan title and the current time and date. Line two shows the number
     and name of the active sheet and the area dimensions.

     The middle part of the screen is the "Window" which is used to display
     the name of the current activity and menus, lists, information from
     files, messages, special instructions, etc.

     The bottom two lines are the "Dialog Box". These lines carry the
     instructions for pressing a key or entering the other information,
     accept input from the keyboard, and display error messages.


     PART 1. GENERAL INFORMATION       LAYOUT 2.0 User Manual     Page  4

     1.6   USING THE KEYBOARD

     Each activity in LAYOUT requires a specific entry from the keyboard.
     The type of entry, and the specific limits for each entry, are shown
     in the Dialog Box. A beep is sounded and a blinking cursor appears.

     The instructions use the following terminology.

     "Press" means you need press only a single key, either a letter or a
     number. The key list refers to the highlighted characters in the
     window display or the letter printed between angle brackets on a
     graphic screen. The Shift Key should not be held down.

     If you press a key not listed in the instruction, an error message
     will be displayed and you will be taken back to the prompt.

     "Return" refers to a key that may be labeled RET, ENTER, or with the
     symbol <--'  on your keyboard.

     "Edit" indicates that you can change individual characters in the
     highlighted line directly on the screen. Typing a character replaces
     the one at the cursor.

     During editing the INS key inserts one blank space at the cursor, the
     DEL key deletes the character at the cursor, the BackSpace key deletes
     the character before the cursor. The left and right arrow keys move
     the cursor one character at a time. The HOME key moves the cursor to
     the beginning of the line, the END key to the end of the line.

     To save the changed line press Return. Pressing the ESC key exits from
     editing without saving the changes.

     "Enter" means you are expected to either type a number or a new
     character type entry (see "Edit"). For numbers use the backspace key
     to make corrections. Press the Return key when you have completed your
     entry.

     When entering a number pressing Return alone (not ESC) causes no
     change to be made. Entering a 0 (zero) causes that value to be stored
     where appropriate. The value zero is displayed as either a blank or a
     "0" on the screen.

     An error message will appear if your entry exceeds the limits of a
     number.  For example, there is a maximum of 6 entries for "Doors" on
     the Sheet Framework menu (see Part 2).

     After every addition or change, you will be given the opportunity to
     correct the information before it is saved on the permanent file.

     Every instruction in LAYOUT gives you an opportunity to "back out" of
     the routine, or continue on, without making a change in the displayed
     values. Pressing only the Return key, or the letter "X" where
     specified, will take you back to the previous instruction or display.


     PART 1. GENERAL INFORMATION       LAYOUT 2.0 User Manual     Page  5

     1.7  SELECT A LAYOUT FILE

     This function will be invoked when you first start LAYOUT and may also
     be accessed by pressing <L> at the Function Menu display.

     A numbered list of the Plan Titles in the files on the current
     directory will be displayed. Type the number of the LAYOUT File you
     want to work with, then press the Return key.

     If you press Return without typing a number, you will be returned to
     the Function Menu.

     To create a new file, enter a "+" sign. The program will check to see
     if there is room on the current drive and directory for a new full
     size file (64k) -- if not a warning message will be displayed.

     NOTE: A directory may contain up to 30 LAYOUT data files.

     If there is room for a new file, you will be asked if you wish to copy
     a current file.

     If you enter a file number, a new file will be created that is an
     exact copy of the selected file and will be named as a "COPY of" that
     file. Otherwise, a new file will be created that contains one sheet.

     You must then select a sheet to be the active one.


     1.8  SELECT A SHEET

     This function will be invoked automatically when you select a LAYOUT
     file and may also be accessed by pressing <S> at the Function Menu
     display.

     You will be presented with a numbered list of the Sheet names in the
     current file. Type the number of the sheet you want to work with, then
     press the Return key.

     If you press Return without typing a number, you will be returned to
     the Function Menu -- the current sheet remains active.

     To create a new sheet, enter a "+" sign. The program will check to see
     if there is room in the file and on the current drive and directory
     for a new sheet (4k) -- if not a warning message will be displayed.

     If there is room for a new sheet (maximum 26), you will be asked if
     you wish to copy a current one.

     If you enter a sheet number, that sheet will be copied to the next
     available sheet number and will be named as a "COPY of" that sheet.
     Otherwise a blank sheet will be added to the file.

     The selected, or newly created, sheet then becomes the active sheet.


     PART 2. SHEET FUNCTIONS           LAYOUT 2.0 User Manual     Page  6

     2.1   OVERVIEW

     Two menus are used to enter the information describing the active
     sheet -- the Sheet Framework menu by pressing <F>, the Area Contents
     menu by pressing <C>. Both can be accessed from either the Function
     Menu or the Drawing display.

     NOTE: The Sheet Name can be edited on the Set Titles/Printer Type menu
     -- see paragraph 3.1.3.

     The current values on file for the active sheet will be displayed.
     Press a letter key to change a value as explained below. Pressing the
     Return key takes you back to the Function Menu or Drawing display.


     2.2  SHEET FRAMEWORK MENU  - press <F>

     This menu is used to enter or change the information that controls how
     the sheet is displayed and printed. The information will be displayed
     and you will be prompted to press a key, or return. The action invoked
     by each key is as follows:


     2.2.1  DRAWING UNITS  - press <U>

     All objects are drawn on the screen (and printout) as a rectangular
     box whose "Size" and "Position" are specified as a number of "Drawing
     Units".

     The box represents the area occupied by the object -- not necessarily
     it's shape.

     The Drawing Units value is a word or abbreviation that states the
     units (e.g. inches, feet, meters, etc.) of the actual measurements
     entered for items to be drawn on the screen.

     The Size of an item specifies the actual measurements to be drawn on
     the screen. "Length" is the horizontal dimension (left to right),
     "Width"  is the vertical dimension (top to bottom).

     Position is defined by how far the upper left-hand corner of an item
     is offset from the "Base Point" (the filled-in block located in the
     upper left-hand corner of the drawing area).

         "Rt" = horizontal distance to the right of the Base Point.
         "Dn" = vertical distance down from the Base Point.

     The position of the Base Point itself is Rt 0   Dn 0


     PART 2. SHEET FUNCTIONS           LAYOUT 2.0 User Manual     Page  7

     2.2.2  DRAWING RATIO  - press <R>

     The number of different locations that can be physically displayed on
     the graphic screen is limited to 240 horizontally and 192 vertically.

     Actual dimensions that are larger (or smaller) can be optimally
     displayed by setting the appropriate Drawing Ratio for the active
     sheet. The data entered for each item will be adjusted for display
     purposes by the ratio -- the data itself is not changed.

     When you press <R> you will see a display of the ratios that may be
     used to enlarge or reduce the drawing so that it fits on the screen.
     The following table can be used to determine an appropriate ratio.

                  Code   Draw Ratio   Maximum Actual Measurement
                   No.                   Length      Width
                    0    Full Size         240        192

          Enlarge   1    Dble Size         120         96
                    2    Quad Size          60         48

          Reduce    3    Half Size         480        384
                    4    Qtr  Size         960        768

     Enter the code number of the Drawing Ratio you wish to use for the
     active sheet.


     2.2.3  INDEX TYPE  - press <T>

     Sheets may be drawn with tick marks on the borders of the drawing,
     full grid lines crisscrossing the drawing or with no index marks.

     When you press <T> you will see a display of the Index Types that may
     be used in the drawing and printing of the active sheet. Enter a code
     number or press Return for no change.


     2.2.4  INTERVAL  - press <I>

     The index interval is the number of drawing units between tick marks
     or grid lines on the drawing and printout. Enter a new number or press
     Return for no change.

     The index interval will be adjusted for display according to the
     drawing ratio.


     PART 2. SHEET FUNCTIONS           LAYOUT 2.0 User Manual     Page  8

     2.2.5  DRAWING AREA BORDERS - press <B>

     The borders of the drawing area may be displayed as "Walls" (double
     lines), "Edges" (single lines), or not at all.

     When you press <B> you will see a display of the Borders that may be
     used in the drawing and printing of the active sheet. Enter a code
     number or press Return for no change.


     2.2.6  HORIZONTAL and VERTICAL SIZES - press <H> or <V>

     Both of these dimensions should be entered as the actual measurements
     of the area represented by the sheet. Edges will be drawn at these
     dimensions, Walls outside of them.

     The boundaries of the drawing area will be indicated on all drawings
     by filled-in blocks located outside of each corner.


     2.2.7 DOORS and WINDOWS  - press <D> or <W>

     When <D> or <W> is pressed you will be prompted to press the number of
     the item you wish to change -- there are a maximum of 6 each.

     You will then be prompted to specify the wall in which the door or
     window is to be drawn, or you can remove this door or window from the
     list by pressing <C> (clear).

     Otherwise, press a letter key -- <T> for the top, <B> for the bottom,
     <L> for the left-hand, or <R> for the right-hand wall.

     Next you must enter the position at which the door or window starts:
        Top & Bottom walls - distance to the right of the base point.
        Left & Right walls - distance down from the base point.

     And finally you must enter the size of the window or door.

     The program draws doors and windows by erasing the specified part of
     the wall and drawing in the frame. For windows, the erased portion of
     the wall is filled with a dashed line.

     If the horizontal or vertical size of the walls is changed, the doors
     and windows will be drawn within the new walls -- the position and
     size are not changed.

     The doors and windows will only be drawn if the drawing area border is
     set to "Walls". The door and window data will not be changed.


     PART 2. SHEET FUNCTIONS           LAYOUT 2.0 User Manual     Page  9

     2.3  AREA CONTENTS MENU  - press <C>

     The Area Contents menu enables you to enter and change the
     specifications for other objects to be displayed on drawings and
     printouts and to enter the inventory data.

     The initial display shows the name, size, and position for each of the
     content blocks (A - Z) that are used to define the rectangular block
     of space occupied by an object regardless of shape. To change the
     specifications or the inventory data for a block, press the letter
     corresponding to the block.

     A window will open on the opposite half of the screen that displays
     all the data on file for the selected content block and you will be
     prompted to select an item to change.

     As you change an item the new data will be displayed in the window but
     will not be changed on the initial display (all 26 blocks) until you
     press return to exit from this window. When you do, you will be
     returned to the updated initial Area Contents display.


     2.3.1  BLOCK NAME  - press <N>

     The block's Name will be highlighted for editing. To clear an item
     completely, delete the block name by holding down the DEL key until
     the highlighted field is empty -- the size and position values will
     also be deleted.


     2.3.2  SIZE  - press <S>

     You will be serially prompted to enter the Length and Width. If the
     position values have not been set you will be automatically taken to
     the POSITION function.


     2.3.3  POSITION  - press <P>

     You will be prompted to enter the Position data (distances to the
     right and down) of the block. Pressing Return at a prompt leaves that
     value unchanged.

     NOTE: Content blocks may have size or position values that are outside
     the specified borders, but will not appear if values exceed the limits
     of the full drawing display.


     PART 2. SHEET FUNCTIONS           LAYOUT 2.0 User Manual     Page  10

     2.3.4  INVENTORY ITEMS  - press <I> or <1> to <6>

     Pressing a number key allows you to edit that inventory item. If you
     press <I> you will be serially prompted to edit all six.

     The number of characters in each inventory item is determined by the
     sizes set in the Set Titles/Printer Type menu (see 3.1.5  INVENTORY
     COLUMNS). If the sizes are changed after the data has been entered it
     may be neccessary to reedit all of the content blocks.


     2.4   DRAWING THIS SHEET

     Each block is drawn and printed with the following variations
     according to the values shown on the display:

          1)  Blocks with all four values for size and position specified
              will be drawn as a box on the screen and the printout.

          2)  If the name of the block starts with an asterisk (*) the
              name will not appear on the printout. Otherwise the name
              will be printed in the approximate center of the box.

          3)  If the size of a block is set at zero (blank on the
              display), a box will not be drawn. The block name will
              appear on the printout at the specified position.

          4)  Block names may be indented up to 8 spaces to change the
              place where they print.

     The Drawing function is accessed by pressing <D> at the Function menu.
     The Framework and Content values for the active sheet will be adjusted
     by the drawing ratio and then used to draw a graphic screen.

     Content block boxes, walls, doors, windows, index marks, and filled-in
     squares representing the four corners of the drawing area will be
     drawn in that order.

     The position of each content block for which information has been
     entered will be indicated by it's item letter on the screen.

     The drawing is a proportional draft of what will be put on paper when
     the sheet is printed except that full block names will be printed
     instead of just the item letters.

     The Plan Title, Sheet number and name, area length and width, drawing
     units and ratio, index interval, and the instructions for continuing
     will be displayed in the sidebar on the left-hand side of the screen.

     A beep will sound. Pressing <X> returns you to the Function menu. You
     can modify the drawing by pressing <F> or <C> to make changes to
     values on the Framework or Content menus -- the drawing will reappear
     when you exit from either.


     PART 2. SHEET FUNCTIONS           LAYOUT 2.0 User Manual     Page  11

     2.5   PRINTING THIS SHEET

     When you are satisfied with the appearance of the drawing, you may
     send it to the printer by pressing <P>.

     NOTE: Printing can also be done by pressing <P> on the Function Menu.

     The drawing will be displayed without the area content block item
     letters -- just the way it will be put on paper.

     A message in the left-hand sidebar will remind you to set the selected
     type of printer "on line". If you have a printer buffer attached, make
     sure it too is turned on.

     NOTE: The Printer Type can be set on the Set Titles/Printer Type menu
     -- see paragraph 3.1.3.

     The reports in LAYOUT are printed on 9 inches per page. For one inch
     top and bottom margins on a dot matrix printer, the paper should be
     set so that the first line will print one inch down from the top of a
     new page.

     The margins for a laser printer are set automatically.

     Press <P> again when you are ready, or <X> to abort the printing.

     If the printer is still not ready to print, you will see a second
     prompt that reminds you to make it ready or to exit without printing.

     A message will acknowledge that printing has started. Be patient !
     Aproximately 44k characters must be sent to the printer one at a time.

     Depending on the speed of your equipment, printing a sheet on a dot
     matrix printer may take up to 3 minutes, on a laser printer about 1
     minute.

     A single page will be printed that contains the titles and dimensions
     of the sheet, the graphic screen drawing with the full name of each
     block, and lists of the information on file for all doors, windows,
     and area content blocks.


     PART 3. FILE FUNCTIONS            LAYOUT 2.0 User Manual     Page  12

     3.1   SET TITLES/PRINTER TYPE

     This menu is used to select a printer type and enter the information
     describing the active file and sheet.  Press a letter or number key to
     change a value as explained below. Pressing the Return key takes you
     back to the Function Menu.

     The current values on file will be displayed, for example:
      ____________________________________________________________________
     /                                                                    \
     LAYOUT 2.0      Apartment #101 - The Erehwon        13:25:32   1/01/91
       Sheet  7/7  Kitchen/Dining Area  Area Length 216   Width 144 inches
     ======================================================================
                          Set Titles/Printer Type

                    Plan Title     Apartment #101 - The Erehwon
                    Sheet Name     Kitchen/Dining Area
                    Printer Type   Dot Matrix

                    Inventory Columns
                              No. Size  Title
                               1.  10   Purch.Date
                               2.  10   Purch.Cost
                               3.  10   Vendor
                               4.  13   Serial Number
                               5.  10   Repl. Cost
                               6.  13   Ins. Policy #
                                  =====
                              Tot  66 / 66 maximum

     ======================================================================
       To make a change press P, S, T, 1 - 6
                         or press Return (no change)
     \____________________________________________________________________/


     3.1.1  PLAN TITLE  - press <P>

     The Plan Title, as displayed in the banner, is used to identify the
     LAYOUT file that is currently being used and is the name that appears
     on the File Selection display. Edit it using the techniques explained
     in Part 1, paragraph 1.6. Press Return when finished, or press the ESC
     key if you do not wish to record the change.


     3.1.2  SHEET NAME  - press <S>

     The name of the currently active sheet is also displayed in the banner
     and is the name that appears on the Sheet Selection display. It can be
     edited using the technique described in Part 1.


     PART 3. FILE FUNCTIONS            LAYOUT 2.0 User Manual     Page  13

     3.1.3  PRINTER TYPE  - press <T>

     Printing may be done either with an Epson compatible dot matrix
     printer or an HP LaserJet laser printer.

     When you press <T> you will see a display of the Printer Types that
     are to be used to print all reports. Enter a code number or press
     Return for no change.

     NOTE: The program expects that the printer you select is the DOS
     default PRN device.


     3.1.4  INVENTORY COLUMNS - press <1> to <6>

     This function enables you to design the format of the printed
     Inventory and the .CSV file that can be created for the active file.

     When you press a number key, you will be prompted to enter the size
     for that column number (press Return for no change) and then to edit
     the title for the column.

     As indicated in the display, there are a maximum of 66 characters for
     the titles of the columns and for the data in each column for each
     Content Block (see below).

     The column size determines how the 66 characters are divided among the
     columns -- i.e. the title and data for column 1 use the first group of
     characters. Column 2 starts at the place where column 1 ends, column 3
     starts at the place where column 2 ends, etc.

     If you try to exceed the maximum, the higher number columns will be
     reduced in size by the program (highest first).

     NOTE: Changing a column size will change the title space and location
     at which all subsequent titles begin -- the titles and content block
     data may have to be reedited.


     PART 3. FILE FUNCTIONS            LAYOUT 2.0 User Manual     Page  14

     3.2   PRINT INVENTORY  - press <I>

     A message will remind you to set the selected type of printer "on
     line". If you have a printer buffer attached, make sure it too is
     turned on.

     The inventory is printed on 9 inches per page. For one inch top and
     bottom margins on a dot matrix printer, the paper should be set so
     that the first line will print one inch down from the top of a new
     page. The margins for a laser printer are set automatically.

     Press any key when you are ready.

     If the printer is still not ready to print, you will see a second
     prompt that reminds you to make it ready or to exit without printing.

     The print-out contains the data from all of the sheets on the current
     file and is divided into titled sections for each sheet -- multiple
     pages are printed if needed.

     The first line on each page carries the Plan Title and the current
     date. The second line carries the inventory column titles set in the
     Set Titles/Printer Type menu. For clarity, the columns are separated
     from each other by the 3 characters  " | "

     The data for each Sheet starts with a line that carries the sheet
     number/total and the sheet name.

     This is followed by a line for each content block that lists the sheet
     number, block letter, block name, and the inventory data entered for
     the block in columns separated as above.

     NOTE: The Inventory data will NOT be printed on the report or included
     in the .CSV file (see section 3.3) if a content block is empty, the
     name of the block starts with an asterisk (*), or the length or width
     of a block is set at zero.


     3.3   MAKE A .CSV FILE  - press <M>

     Many spreadsheet programs can import data directly from a "comma
     separated value (.CSV)" file -- an ASCII file formatted with commas
     between data for columns and a carriage return for a new row.

     This function will create a file of that type with the same file name
     as the current .LY2 file but with the .CSV extension.

     The file will contain the plan title and column title lines and then
     all of the sheet information described above (no page breaks). The 3
     character column separator is replaced by commas between data items.

     HINT: When importing this file, set the width of the first column of
     the spreadsheet to 32, the others to each Inventory Column Size + 2.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  15

     In this part we will explore various features of LAYOUT using the
     sample files on the distribution diskette. Place a copy of the
     diskette into a disk drive, log on to that drive and enter   LAYOUT

     The plan titles of the files will be displayed like this:
      ___________________________________________________________________
     /                                                                   \
     LAYOUT 2.0                                         16:58:04   1/01/91

     =====================================================================
                            Select a LAYOUT File

        ----------- Plan Titles of Files in Current Directory-----------
         1. Floor Plan C, The Erehwon Apts
         2. Apartment #101, The Erehwon
         3. Additional LAYOUT Examples


     =====================================================================
          To start a new file enter a + sign or
          enter a LAYOUT file number  or Return
     \___________________________________________________________________/

     The first two files contain the floor plans for the same apartment.
     File # 1 shows the unfurnished apartment with it's built-in fixtures,
     # 2 has had some furnishings placed in it.

     We will start with File number 1 - press the number 1 and then the
     Return key. The next display will look like this.
      ___________________________________________________________________
     /                                                                   \
     LAYOUT 2.0      Floor Plan C - The Erehwon Apts    16:58:35   1/01/91
       Sheet  1/7  Apartment Overview   Area Length 480  Width 276 inches
     =====================================================================
                             Select starting Sheet

            --------------- Sheets Currently in File ---------------
              1. Apartment Overview
              2. Workshop and Study
              3. Study Bath & Closets
              4. Living Room
              5. Bedroom
              6. Main Bath & Closets
              7. Kitchen/Dining Area


     =====================================================================
          To add a new sheet enter a + sign or
          enter a Sheet number  or Return
     \___________________________________________________________________/

     Sheet 1 is a block overview of the apartment. The others show details
     including interior walls and doors. Choose sheet number 2 to start.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  16

     The next display you will see is the Function Menu.  Note that Sheet
     number 2 is now listed in the banner as the active sheet.

     Press <D> to draw the sheet on the screen. You will then see a display
     that looks something like this (but much better on the screen):
      ___________________________________________________________________
     /                                                                   \
     Floor Plan *===============         ========================*
      C, The    ||               A                              ||
     Erewhon Ap ||                                              ||
     Sheet #    ||
       2/7      ||                                                 B
     Workshop    |
     and Study   |                                              ||
     ----------  |                                              ||
     Length 204  |                                              ||
     Width  132  |                                              ||
     Units       |                                              ||
      inches    ||                                              ||
     Index      ||
      Interval  ||                                                 C
         12     ||
     Drawing is ||                                              ||
      Full size ||                                              ||
     ---------- *====================================        ====*
     Press                                             D
     <F>ramewk,
     <C>ontent,
     <P>rint
     or e<X>it
      to Menu
     \___________________________________________________________________/


     The information in the sidebar and the data for drawing the four doors
     and the one window can be changed on the Framework menu.

     Press <F> to view that menu. Press Return to come back to the drawing.

     The four letters in the drawing area (A-D) show the locations where
     the names for each of the doors will be printed on paper. These
     locations can be changed on the Contents menu. Press <C> to bring up
     the Contents menu.

     Note the block names assigned to each of the letters. Since the size
     (Len and Wid) of each of these blocks is zero (blank) no box will be
     drawn. The names will be printed in the positions defined for each.

     We will discuss other aspects of the Area Contents menu later in this
     manual. Press Return to come back to the drawing.

     Remember, you can print a sheet at any time by pressing <P> at the
     drawing display -- see the instructions in Part 2.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  17

     Let's examine the effects of changing some of the values displayed on
     the Framework menu. Press <F> to bring up that menu. The following
     display appears:
      ___________________________________________________________________
     /                                                                   \
     LAYOUT 2.0      Floor Plan C - The Erehwon Apts    17:40:45   1/01/91
       Sheet  2/7  Workshop and Study   Area Length 204  Width 132 inches
     =====================================================================
                              Sheet Framework

           Drawing Units  inches              Index Type  not drawn
                   Ratio  Full size             Interval   12  inches

                     Drawing Area Borders      Walls
                     Horizontal size (length)  204 inches
                     Vertical size (width)     132 inches

         Door   Wall  Position  Size       Window  Wall  Position  Size
           1.    Top   Rt  60    36           1.    Lft   Dn  40    48
           2.    Rht   Dn  24    24           2.
           3.    Rht   Dn  84    24           3.
           4.    Bot   Rt 162    32           4.
           5.                                 5.
           6.                                 6.

     =====================================================================
       To make a change press S, P, U, R, T, I, B, H, V, D, W
                         or press Return (no change)
     \___________________________________________________________________/

     Distances on a drawing can be difficult to evaluate without some
     indication of the scale of the drawing. Let's add indexing marks to
     this sheet.

     Press <T>. A list of the available indexing types will "pop up" on the
     screen. Select code number 1 (Tick marks). The new index type will be
     indicated on the display. Press Return to go back to the drawing.

     The whole drawing area is now outlined on all 4 sides by a series of
     short vertical and horizontal dashes. The distance between marks is
     defined by the index interval. Because of variations in monitors,
     horizontal distances should be compared only with the top or bottom
     row of marks, vertical distances with the left or right column.

     Go to the Framework menu and reset the index type to "Grid lines" and
     return. The drawing area is now divided into a set of squares.
     Although the drawing seems somewhat crowded, grid lines can be useful
     in determining the amount of floor-covering needed for a room -- in
     this case for example, the number of 12 inch square floor tiles.

     Press <I> on the Framework menu, set the interval to 36, and return to
     the drawing -- the grid now shows the amount of carpeting needed in
     square yards.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  18

     The next thing we will evaluate is the Drawing Ratio.

     First set the index type as grid lines and the index interval at 36.
     Now examine the drawing. The sidebar shows that the area is 204 inches
     long, 132 inches wide, and is drawn "Full size".

     Since the dimensions are within the maximum limits (240 L x 192 W),
     the drawing fits completely on the screen.

     Press <F> to bring up the Framework menu and then press <R> to see a
     display of the available drawing ratios. Enter code 3 (Half) and
     return to the drawing.

     The sidebar now shows that the drawing is "Half size".

     Although you have not changed the sizes and positions of the
     structures, all measurements have been cut in half and therefore only
     occupy half their normal distance on the screen.

     The grid lines still represent the same interval (36 inches) but there
     is now room for twice as many squares on the screen.

     Take a few minutes and explore the effects of enlarging or reducing
     the drawing ratio. Note that all sizes and positions are
     proportionally adjusted for drawing and that only those parts of the
     sheet that will fit are drawn -- the rest do not appear.

     When you are finished, reset the Ratio to "Full size", the index type
     to "Tick marks", the interval to 12, and return to the drawing.

     For the next part of this exercise we will be changing some of the
     numbers used to create the drawings. Before we do that we want to have
     a picture of the sheet and a record of what the current numbers are.

     Press <P> (to print). The drawing will be redisplayed without the item
     letters of the content blocks -- the graphic portion of the drawing
     now looks just like it will be printed.

     The sidebar messages are to remind you to set your printer "online"
     -- make sure you have set the appropriate printer type for your
     equipment.

     When the printer is ready, press <P> again. The sheet will be printed.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  19

     Since this sheet is the drawing of a room, the Drawing Area Borders
     are specified to be "Walls". Press <B> on the Framework menu, change
     this value, and return to the drawing.

     Depending on your choice the borders of the area will be drawn as
     single lines (code 2) or not at all (code 3). Try out both. Note that
     in these cases the doors and windows are not drawn, but the data for
     them has not been lost. The blocks indicating the corners of the area
     are always drawn.

     Reset the Border value to "Walls" (code 1) and return to the drawing.

     The length and width of the drawn area are listed in the sidebar.
     These two numbers determine where the borders and the corner blocks
     will be drawn.

     Try changing the Horizontal or Vertical size on the Framework menu.

     Note that the doors and windows will always be displayed according to
     their positions and sizes within the walls specified by the listed
     dimensions, even if the position or size of a door or window extends
     the drawing beyond the new dimension.

     The location of the item letters indicating where the door names will
     be printed is NOT adjusted to changed dimensions. The locations must
     be changed on the Area Contents menu.

     Reset the area sizes to their original dimensions (204 x 132) and the
     wall, door, and window drawings will be returned to their original
     locations.

     This sheet shows the presence of four doors in the walls of this room
     (each indicated by a letter) and one window in the left-hand wall.

     The data for the window and the doors, and for the door names, are
     listed in the bottom part of the sheet you just printed.

     The Wall, Position and Size data for the window and doors is a copy of
     what appears on the Framework menu. The specifications for the door
     names comes from the Area Contents menu.

     As an exercise let's split the window into two 24 inch parts with 6
     inches between them. Press <F> to invoke the Framework menu.

     Press <W> and then <1> -- this lets you change Window number 1.

     Then press <L> to specify the left wall of the drawing.
     For Lft Dn Position enter 40 and for Size enter 24.

     This places a window that is 24 inches long starting 40 inches down
     from the top in the left wall of the room.

     Return to the drawing to observe the results of these entries.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  20

     Now let's put in the second part of the window. On the Framework menu
     select Window number 2 and specify that it too is in the left wall.

     Since we want to leave 6 inches between windows, we must do a little
     arithmetic as follows:
        Window # 1 starts        40  inches down
                   and is        24  inches long
        Window # 2 starts         6  inches down from the end of Window # 1
                            ========
        Adding these gives       70  as the starting position of Window # 2

     Enter this value for the position of Window # 2 and again specify 24
     as the size.

     Return to the drawing. Note that we have now split the original 48"
     window into 2 - 24" windows with 6" between them.

     To restore the original window you would first clear Window # 2 -- on
     the Framework menu press <W>, <2>, and then <C>.

     Then select Window # 1 and respecify it as being in the left wall at
     position 40 and size 48.

     Return to the drawing to confirm that you have restored it to what it
     looks like on the printout.

     The same techniques are used for creating, changing, or clearing doors
     -- start with <D> instead of <W>.

     Now try putting windows and doors in other places on the drawing.

     Note that if you overlap a door with a window, the window will be
     drawn as specified but the door will not be drawn correctly and
     extraneous marks will appear in the window.

     This is because doors are drawn before windows -- the extraneous marks
     are the door frames that were drawn after a portion of the wall was
     erased for the door.

     Examine the printout you have. From the specifications for the doors
     note that Door # 3 is in the right wall, starts 84 inches down from
     the top, and is 24 inches wide.

     In the Area Contents information the block indicated by the item letter
     "C" places that letter on the screen at the position Rt 210, Dn 96 and
     will put the name "Study Closet" at the equivalent position on the
     printout -- no box is drawn because the block sizes are blank.

     Now clear Door # 3 on the Framework menu and return to the drawing.
     Note that although the door no longer appears, the key letter is still
     displayed. Remove it by blanking the block name on the Contents menu.

     Now reset Door 3 and Block C to the specifications on the printout.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  21

     To further examine the uses of the data entered on the Area Content
     menu we will use a different sheet.

     Return to the Function Menu, press <S> to invoke the sheet select
     function and choose sheet number 3, Study Bath & Closets.

     Draw the sheet on the screen. You will see that this sheet is a
     detailed continuation to the right of the sheet we just worked with.
     Print a copy of this sheet.

     The bottom part of the printout contains the specifications on file
     for the blocks whose position on the drawing are indicated by the
     letters A - H.

     The specifications are reproduced in the following table.

                Content Blocks     - Size -   Position
                  --- Name ---      Len Wid    Rt  Dn
                A.* bath-closets    112   2     0  60
                B.* closet-closet     2  70    60  62
                C.Counter            49  22     0   0
                D. Sink              18  16    26   2
                E. Toilet            21  29    54   0
                F.Bath tub/shower    31  60    81   0
                G.Linen Cabinet      41   8     0  52
                H.Study Closet                  8  96
                I.Hall Closet                  76  96

     Block A is the horizontal interior wall between the bathroom and the
     two closets. This wall goes the whole length of the drawing area (112
     inches), is 2 inches thick, and starts at the left edge of the drawing
     area (Position Rt 0).

     Since the bathroom is 60 inches wide, the vertical position of the
     wall is placed 60 inches down from the base point.

     Block B is the vertical interior wall that divides the two closets. It
     is 2 inches thick and runs the entire width of both closets (Wid = 70
     inches).

     Since the study closet is 60 inches long and this wall abuts on to the
     horizontal wall, Block B's position is Rt 60  Dn 62.

     The block names for these two items have been entered to identify the
     walls in the data but they will not be printed as they each start with
     an asterisk.

     Blocks C - G draw and label the fixtures in the bathroom. Note that
     the Sink and Toilet names have been indented to center the labels.

     Blocks H and I put the closet names in the center of their areas.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  22

     Now let's put some fixtures into the Study Closet. We will use the
     following information.

                Content Blocks     - Size -   Position
                  --- Name ---      Len Wid    Rt  Dn
                N.Clothing rod       60   1     0  72
                O.Shoes              12  24    48  84
                P.Shelves            60  18     0 114

     Block N is a 1 inch thick rod that runs the whole length of the closet
     and is 12 inches away from the top inside wall. It's Position Dn
     therefore equals 12 plus the width of the bathroom (60).

     Block O represents a 12 inch by 24 inch shoe rack placed against the
     right hand wall of the closet (Position Rt = Closet length 60 - block
     Len 12) directly opposite the door (Dn 84).

     Block P outlines a set of 18 inch shelves along the full length of the
     bottom wall of the closet.

     Bring up the Contents menu and enter the information into Blocks N-P.
     Return to the drawing and print a copy of it.

     Now let's check our work. Return to the Function menu and press <L> to
     select a different LAYOUT file -- your changed file will be saved to
     disk. Choose file number 2 and then sheet number 3. Print a copy.

     Now go back to file number 1, sheet number 3. Compare the sheet from
     file 2 (Apartment #101) to your printout of the same sheet from file 1
     (Floor Plan C). If they do not match, make the needed corrections.

     Before going any further, let's take a look at an overview of the
     apartment. Go to the Function menu and select Sheet # 1. Draw it and
     print a copy.

     Since the dimensions of the whole apartment (480 x 276 inches) exceed
     the physical limits of the screen (240 x 192) the drawing ratio for
     this sheet has been set at Half size.

     The drawing shows the whole apartment divided into a series of blocks
     outlining the location and dimensions of each room in the apartment.
     The position and size of the doors and windows in the external walls
     of the apartment are shown.

     Content Blocks are used to define a room or group of rooms. The
     additional labels on this printout show the relationships of the
     detail sheets where the placement of interior walls, doors, fixtures,
     etc. are shown -- see your printouts of sheets 2 and 3.

     Note that the numbers describing the actual dimensions of a block on
     the overview are the same as those on the specific detail sheet for
     the comparable structure -- the difference in the appearance of the
     drawing is due to different drawing ratios.


     PART 4. A PRACTICAL EXERCISE      LAYOUT 2.0 User Manual     Page  23

     For example, the block outlining the area of the Workshop/Study on the
     overview is 204 x 132 in size. Therefore the same dimensions are
     specified for the walls on Sheet # 2.

     From the overview we can see, for example, that the area drawn on
     Sheet # 3 lies immediately to the right of that drawn on Sheet # 2.

     Since both these sheets are drawn to the same scale (unit = inches,
     ratio = full size) the two pieces of paper can be superimposed (right
     wall of sheet 2 to left wall of sheet 3) to create a larger overall
     plan of the apartment that includes all the detail.

     Similarly, sheet 4 describes the area to the right of sheet 3, Sheet 5
     the area below sheet 2, etc. (all drawn to the same scale).

     The filled-in blocks printed at the intersections of the borders will
     help you to match up adjoining sheets.

     You can create a large composite area plan by cutting each sheet along
     it's top and left-hand borders and, starting with sheet number 1 as
     the base, paste adjoining sheets onto their relative positions.
     The size of such a composite is limited only by your imagination.

     Some other ways to use the features in LAYOUT are illustrated on other
     sheets in the sample files.

     Sheet # 4 (either file): - The living room actually has only three
     walls. To remove the fourth wall from the drawing of the borders, a
     door was placed the full length of the bottom wall.The structures that
     lie across the hallway from the living room have been included on this
     sheet -- see area content blocks E - H.

     Sheet # 7 (either file): - the boundaries of this sheet include the
     front part of the hallway, the kitchen, and the dining area. Door 1 is
     the hallway closet door and Door 2 is the absent wall of the living
     room. The interior walls lining the hallway are Blocks N and O. The
     pass through and wall separating the kitchen and dining area are
     Blocks Q and R.

     The fixtures in the kitchen are in Sheet # 7 on both files. Sheet # 7
     on file # 2 (Apartment #101) shows the furniture placed in the dining
     area by the tenant and some entries have been made in the inventory
     data.

     Print a copy of the Inventory. Go to the Set Titles/Printer Type menu
     and change some of the column sizes to see the effects on the column
     titles and the content block inventory data.

     The third sample file carries a miscellaneous collection of sheets to
     demonstrate how other kinds of areas, besides floor plans, can be
     described with LAYOUT. These samples illustrate how combinations of
     drawing ratios and units, either fractional or whole, can be used to
     describe any sized area.


     PART 5. LICENSE INFORMATION       LAYOUT 2.0 User Manual     Page  24

     LAYOUT and documentation distributed or shipped with it are copyrighted
     works protected by U.S. and international copyright law. You are granted
     a license to use your copy of LAYOUT only under the terms specified in
     this license agreement.

     LAYOUT is a software package representing many long hours of
     programming, development, and support. LAYOUT is not public domain or
     free software. LAYOUT is distributed as shareware, supported by you, the
     users that find these programs productive!

     If you benefited in some way from LAYOUT or make regular use of any of
     the programs, you should register your copy. Registered users are sent a
     program disk containing the latest release of the programs, complete
     printed documentation, and published announcements of future releases of
     LAYOUT. Support for the program via telephone, mail, Bulletin Board, and
     Compuserve is also provided to registered users.

     Single user registration of LAYOUT costs $35 and entitles you to use
     this software on a single computer and to make as many copies of this
     software as you wish for backup purposes.

     Upon receipt of your registration fee you will receive a printed manual,
     a disk with the latest version of the software, notice of updates to the
     software, notice of any bugs that may be found in the software, and you
     will be eligible for telephone support (317-856-6052 during business
     hours). Support can also be obtained by BBS (PBS-BBS 317-856-2087 Author
     Conference - Leave a message to BOB OSTRANDER) or on CompuServe
     (Leave email to BOB OSTRANDER 76635,1760).

     Registration by private individuals for non-commercial uses is available
     for $20. This registration level does not include a program disk or
     printed manual.


     Site licenses are available for LAYOUT for $200. A site license entitles
     you to use this software on all of the computers in a building, campus,
     or plant. You will receive 2 master disks and 2 manuals to make copies
     from as you wish. Additional master disks and manuals are available, if
     you wish, at a cost of $4 and $3 respectively.

     Telephone support and update notices for site licensees of LAYOUT must
     be directed through one person at the licensee's location.


     PART 5. LICENSE INFORMATION       LAYOUT 2.0 User Manual     Page  25

     Anyone not charging a "duplication" fee, individual or non-profit user
     groups, and Bulletin Board systems, may freely copy and share exact
     duplicates of LAYOUT. All program and documentation files must be
     distributed together and unmodified.

     Distributors of shareware software disks may distribute LAYOUT if they
     notify the Software Co-op that they are doing so. Members of the ASP do
     not need to notify Software Co-op that they are distributing LAYOUT.

     There is no warranty of any kind associated with LAYOUT. You, the user,
     are advised to experiment and become familiar with all of the programs
     before relying on them. You assume all risk for the selection, use, and
     operation of LAYOUT to achieve your intended results.

     You alone are responsible for any loss of profits, loss of savings, or
     other incidental or consequential damages arising out of the correct or
     incorrect use of these programs, even if we are advised of the
     possibility of any damages due to a defect in any program.

     By using any of the programs composing LAYOUT programs you agree to the
     above limitations.


             _______
        ____|__     |               (tm)
     --|       |    |-------------------
       |   ____|__  |  Association of
       |  |       |_|  Shareware
       |__|   o   |    Professionals
     -----|   |   |---------------------
          |___|___|    MEMBER



     This program is published by a member of the Association of Shareware
     Professionals (ASP). ASP wants to make sure that the shareware principle
     works for you. If you are unable to resolve a shareware-related problem
     with an ASP member by contacting the member directly, ASP may be able to
     help. The ASP Ombudsman can help you resolve a dispute or problem with
     an ASP member, but does not provide technical support for members'
     products. Please write to the ASP Ombudsman at 545 Grover Road,
     Muskegon, MI 49442 or send a Compuserve message via easyplex to ASP
     Ombudsman 70007,3536.



                             SINGLE USER INVOICE


   Remit to:                        From:

   Software Co-op                      ____________________________________
   5437 Honey Manor Dr
   Indianapolis  IN  46241             ____________________________________

   or VISA/MC call:                    ____________________________________

   317-856-6052                        ____________________________________

                                       ____________________________________



   Send me _____ copy/copies of fully registered LAYOUT at $35 each.


   Register me for _____ copies of LAYOUT without disk or manual at $20 each.


   Send me _____ copy/copies of LAYOUT distribution diskette at $4 each.


                                                   Total: __________





   -------------------------------------------------------------------------

   Checks, Money Orders, VISA, MasterCard are accepted.  Written Purchase
   Orders are accepted for quantity purchases and site licenses from most
   companies, schools, and governmental units.  Terms NET 30.


   VISA/MC #  _________  _________  _________  _________  Exp Date:___ /____


   Signature ________________________________   Phone ______________________

   -------------------------------------------------------------------------

   To Purchasing, Accounts Payable:

   Note that LAYOUT have been delivered and
   accepted by the customer.  Upon receipt of this paid invoice, printed
   manual(s) and current disk(s) will be sent.

   Our federal employer ID number is 35-1689317.



                            SITE LICENSE INVOICE

   Remit to:                        From (street address):

   Software Co-op                      ____________________________________
   5437 Honey Manor Dr
   Indianapolis  IN  46241             ____________________________________

   or VISA/MC call:                    ____________________________________

   317-856-6052                        ____________________________________

                                       ____________________________________

                                   Contact individual _____________________

                                   Phone number ___________________________



   Send _____ site license packages at $200.




   Send _____ additional master disks at $4.

   Send _____ additional printed manuals at $3.




   -------------------------------------------------------------------------

   Checks, Money Orders, VISA, MasterCard are accepted.  Written Purchase
   Orders are accepted for quantity purchases and site licenses from most
   companies, schools, and governmental units.  Terms NET 30.


   VISA/MC #  _________  _________  _________  _________  Exp Date:___ /____


   Signature ________________________________   Phone ______________________

   -------------------------------------------------------------------------

   Our federal employer ID number is 35-1689317.