HELMHZ.WKQ
                                   README.DOC


                This brief .DOC file is intended to explain the 
         HELMHZ.WKQ file. 
                During a recent speaker building project I found the 
         need to use not only the basic Helmholtz vent length 
         equation, but I also wanted to look at the interactions of 
         the four variables that make up the basic formula in order to 
         help fine "tune" my design. The formula is a bit cumbersome 
         and after having spent considerable time with a handheld 
         calculator, I decided that this was an ideal application for 
         spreadsheet calculations.
                The .WKQ extension is for Borland's Quattro *
         spreadsheet software. However, if you have Lotus 123**, simply 
         change the extension to WK1 and load it in. Once loaded, you 
         will see that the spreadsheet is divided into (4) separate 
         calculation boxes. The upper three are worked with 
         individually depending on what paramater you are looking for. 
         Simply select the box with the output you want to calculate 
         and input the 3 remaining variable values that are called for as 
         inputs. The output is then found automatically using some 
         variation of the basic vent length equation I found in the 
         third edition of the LOUDSPEAKER COODBOOK written by Vance
         Dickason.
                The large, lower box is for evaluating a wide range of 
         vent lengths for a variety of vent diameters for both single 
         and dual vent designs over a broad range of resonant 
         frequencies. You only need to enter a box volume in cubic 
         inches at the upper left corner and the lengths are 
         automatically calculated. If you are working with some 
         intermediate frequency not listed, simply substitute it for 
         one of those I listed and you will see the effect on vent 
         length over all the single and dual vent sizes based on the 
         exact frequency you are interested in. Although this 
         spreadsheet does not address Mach number calculations, you 
         should look for the largest single or dual vent you can 
         physically fit into your design. This will minimize any vent 
         "whistling" that can occur with large cone excursions and 
         too-small a vent size.
                For your convenience I have designed the spreadsheet 
         so it can be printed out on a single 8.5x11 sheet using 
         Sideways*** software.
                This is my first foray into uploading software to a 
         bulletin board. It's the least I can do in light of all the 
         software I've downloaded. I hope that some of you will find 
         this minimal offering useful. If you have any spreadsheets of 
         similar type you would like to share please leave me a note 
         on the Madisound Audio Projects Bulletin Board. So long....

                                              Carl Richard
         * a product of Borland Int'l Corp.
         ** a product of Lotus Development Corp.
         *** a product of Funk Software Inc.