D - 1 0   C O N T R O L
                                   version 1.0



                                  by Harry Mark

                                REFERENCE MANUAL

















        (c) 1990 MIDIEVAL SOFTWARE
        P.O. Box 902
        North Bay, Ontario, Canada
        P1B 8K1




        D-10 Control and this manual are
        Copyright (c) 1990 by MIDIEVAL SOFTWARE
        ALL RIGHTS RESERVED.
        Some company and product names contained in this document are
        trademarks of various companies.



        TABLE OF CONTENTS
        -----------------

        Introduction...................1
        System Requirements............1
        Installing D-10 Control........2
        Running D-10 Control...........2

        Control Panel..................3

        Select Tone....................4

        Tone Edit......................5
           Load........................5
           Save........................5
           Compare.....................6
           Editing the tone............6
           Select PCM..................7

        File...........................8
           Loading a Sound File........9
           Saving a Sound File........10

        Timbre Map....................11

        Configuration.................11

        Info..........................12

        Quit..........................12

        Note to D-20 Users............12

        Disclaimer....................13
        License.......................13
        Order Form....................15

        D-10 CONTROL 1.0         1


        INTRODUCTION
        ============

        D-10 Control is a MIDI application that allows you to control
        various aspects of the Roland D-10, D-110, D-20, and D-5
        synthesizers.  High resolution EGA graphics and a mouse are used
        for fully graphical editing of all aspects of the multi-timbral
        mode of these synthesizers;  the computer becomes an extension of
        your synth.  You will find that this program is a fun way to
        experiment and learn more about your synthesizer, without the
        numerous cumbersome key presses that would be required on the
        synth itself.

        D-10 Control allows you to change volumes, panpots (stereo
        direction), reverb, timbre and tone parameters easily and
        quickly.  Refer to the synthesizer documentation for explanation
        of these terms and any other concepts relating to the synth,
        since they are beyond the scope of this manual, or try
        experimenting with this program!

        Tone, timbre and patch information can be stored on disk to be
        retrieved and loaded back into the synthesizer later.  You can
        tailor the colours and other defaults to your liking and they
        will be automatically used by the program.

        This program is user supported software (i.e. Shareware) and is
        not free or public domain.  You are granted a license to try this
        program for 14 days.  If you wish to continue to use this product
        after the 14 day trial period, you must register.  Registration
        information, benefits and distribution rules are located at the
        end of this document.


        SYSTEM REQUIREMENTS
        ===================

        D-10 Control requires an IBM-PC compatible with at least 150K of
        free memory running under MS-DOS with:

        1) a Roland D-10, D-110, D-20 or D-5 synthesizer
        2) a MPU-401 compatible MIDI interface
        3) an EGA capable video card (with at least 256K memory) and
        monitor
        4) a Microsoft compatible mouse

        The mouse driver (usually called MOUSE.COM or MOUSE.SYS) must be
        installed before the program will run (refer to your mouse
        documentation for more information).


        INSTALLING D-10 CONTROL
        =======================

        D-10 CONTROL 1.0         2


        The following files should be found after the the archive
        containing this package extracts itself:

        1) 'CONTROL.EXE'  The program
        2) 'CONTROL.DOC'  This document
        3) 'CONTROL.CFG' Configuration file
        4) 'CONTROL.REG'  Registration and license
        5) 'README.COM' Reads 'CONTROL.DOC'

        There are no special installation instructions; just copy these
        files to any directory you wish and run D-10 Control from this
        directory.

        To print this manual, CONTROL.DOC, enter 'COPY CONTROL.DOC PRN:'
        or LPT1, LPT2, etc. instead of PRN, depending on your printer
        configuration.


        RUNNING D-10 CONTROL
        ====================

        If necessary, go to the directory where the program resides
        (using the command CD followed by the directory name).  Type
        'CONTROL' at the MS-DOS prompt and press RETURN.

        The message 'Looking for configuration file...' should appear
        while the computer looks for the program configuration file
        'CONTROL.CFG' in the current directory.  If it finds the file and
        the file is valid, it will read the defaults from the file.

        The title page will appear.  At this point the program will be
        requesting information from the synthesizer through MIDI.

        If the synthesizer does not respond with the information within a
        fixed period of time:

           You will be given three choices: 1) Retry  2) Config 3) Quit.
           Select 'Config' if you are using this program for the first
           time.  It will take you to the Configuration page where you
           can set the program defaults.  Chances are that your synth's
           MIDI exclusive unit number is different than the program's
           default 17.  To check the synth's setting, press'MIDI' on the
           synth, then 'DISPLAY down' until this parameter is shown in
           the synth's window.  Adjust the program's exclusive unit
           setting by pressing a mouse button on the '<' or '>' of the
           top rectangle until it matches.

           Click on ACCEPT to continue.

           The program will try again.  If the synth still does not
           respond, make sure that the synth is turned on and connected
           to the properly installed MIDI interface with the proper
           cables.

        D-10 CONTROL 1.0         3


        If the synth is not in its 'Multi-Timbral' mode (i.e. in its
        'Performance' mode), a message will appear.   Press the 'Multi
        Timbral' button on the synth then press a mouse button to
        continue.  You must change the mode to continue; this program was
        designed for the multi-timbral mode only.    Do not change the
        mode or perform any editing on the synth while the program is
        running, since this may cause some of the displayed information
        to be inaccurate.


        CONTROL PANEL
        =============

        This is the core page of the program.  At the top are several
        options to be discussed later.  Underneath are the volume and
        panpot 'slides'.  There are ten for volume; the first is the
        master volume, the next eight correspond to the eight 'Parts'
        (consult synth manual for description) and one for the rhythm
        section.

        There are eight sections of information consisting of the tone
        name (which is highlighted) and the timbre parameters for the
        Part.  Note that the information for the Parts are in a
        'temporary' area; any changes here are lost when the synth is
        turned off or the mode switched.  The timbres and tones in these
        areas can be copied to or from the synth's more permanent memory
        (this memory is retained even when power is off) or saved to disk
        files (see FILE).

        Reverb parameters and master tune appear at the bottom.  For D-5
        users, the reverb parameters will not have any affect.

        In each timbre section, there is a 'slide' at the bottom (looks
        approx. like <[   |   ]>).  This feature appears here and in
        other pages.  This is where you change the value of a parameter
        with the mouse.  To the right of it is the value of the current
        parameter.  Only one parameter can be modified at a time.  To
        change the current timbre parameter, press a mouse button on the
        parameter's name (if it is not already highlighted).  The new
        parameter will be highlighted.

        There are three ways of changing the value with the slide:

        1) decrement the current value by positioning the mouse pointer
        at the '<' and holding a mouse button down or by clicking (click
        - to press then quickly release a mouse button).  (The repeat
        speed parameter in the Configuration page determines how fast the
        value will change if you hold the button down.)

        2) increment the current value by positioning the cursor at the
        '>' and holding a mouse button down or clicking.

        3) select a value directly by pressing the mouse button anywhere
        inside the rectangle between the '<' and '>'.  This will select a

        D-10 CONTROL 1.0         4


        value which is proportional to the range of the parameter. eg.
        clicking in the middle will move the slide to the middle of the
        parameter's range.  You can 'drag' the mouse around within the
        box by moving the mouse while a button is held down.

        If you play some notes on the keyboard while values are being
        changed, you can hear the changes taking effect.
        Example: Try changing key offset using the slide while playing
        some notes.

        NOTE: Depending on the settings for MIDI TxCH (transmit channel)
        and MIDI PARTn CH (where n is the Part you are editing on), you
        might not hear the changes when you press a note on the synth (to
        hear Part n, these two should be on the same channel).  To check
        which channels the keyboard will play on, press MIDI then DISPLAY
        UP/DOWN to check these channels settings.  E.g. if LOWER TxCH = 5
        and MIDI PART1 CH =5, then Part 1 will sound when you play a note
        on the lower portion of the keyboard (This also depends on where
        the split point is...consult the manual for further info).  An
        easier way is to play some notes and watch the lights that turn
        on when the key is held down; they will tell you which Parts the
        keyboard controls.

        If the Part number (1 through 8) is clicked on, it will toggle
        between being highlighted and not.  If a group of numbers is
        highlighted, a change in parameter or value in a member will also
        affect the others in the group.  This allows you edit several
        timbres simultaneously.

        At the bottom are slides for reverb parameters and master tune.
        Master Tune fine tunes the instrument.   To change the kind of
        Reverb, click a mouse button at the '<' or '>' to cycle through
        the choices.  In this case (and a few others), holding down a
        button will not cycle through the choices; you must click several
        times to do so.

        To edit or change the tone for a specific Part, click on the name
        of the tone.  This will bring up another page:


        SELECT TONE
        ===========

        You can select any of the tones stored in the synth, of which
        there are 256 in total.  Only 128 will be displayed at a time.
        To alternate between the pages of 128 tones, click on PAGE.  The
        tones stored in the synth are divided into 4 banks, A, B, I, and
        R (the percussion bank).  I is where user tones can be stored
        (discussed later in SAVE in next section).

        On the top line, the name of the tone and the current Part is
        displayed at the top.

        D-10 CONTROL 1.0         5


        To select a tone, simply click on it; it will automatically be
        highlighted and this tone will be copied to the Part.  The
        changes are instant; try playing several notes as you select
        different tones.

        It is not necessary to select a tone in this page.

        To edit the tone, click on EDIT.  This will bring up the tone
        editor.

        To return to the control panel, click on ACCEPT or click on the
        same tone twice.


        TONE EDITOR
        ===========

        This is where most of the fun will take place!  Here you can see
        what parameters make up the tone and change them with ease.  If
        the description sounds too complicated, don't worry; once you use
        it, you will find that it is quite easy and powerful to use.

        Tones are the sounds the synth produces.  A tone is made up of
        one through four partials.  Though the tone editor will display
        four partials, you can mute them to effectively have less than
        four.  Each partial is either a P or S type of wave.  P is a PCM,
        or digitally recorded wave and S is an analog wave.  Which type a
        partial is is determined by the 'structure' used to combine each
        pair of partials.

        On the top line, there are several options plus the current Part
        number.  You can select one of these options by clicking on the
        word:

        LOAD - To select a tone from the synth's memory to edit (same as
        the SELECT TONE page).  Any changes to the tone will not affect
        the 'original' in the synth's non-temporary memory.

        SAVE - To save the tone from this edit page into the synth's user
        tone memory (Bank 'I'). There are 64 slots, 'i01' through 'i64',
        where the tone can be stored.  The user slots are listed on the
        left side of the page along with the name of the tone currently
        stored in the slot and the number of timbres and patches (patches
        occur only in the Performance mode) that reference the tone.

           If the program has not read this reference information since
           the program was run, it will read it now before going to this
           WRITE SELECT page.  There will be a short delay as this
           information is being read and organized.

           If you click on a slot, the slot will be highlighted and the
           corresponding list of timbres and patches that reference the
           tone is shown on the right half of the page.  This is to help

        D-10 CONTROL 1.0         6


           you decide which slot to use and which timbres/patches would
           be affected.

           Clicking on a the slot alone will not save the tone.  Only
           when a slot is selected and the option WRITE is clicked on
           will this occur.  When you write into a slot, all the timbres
           and patches that reference the previous one will now use this
           tone.  (The tones that timbres reference can be changed in the
           TIMBRE MAP page (discussed later)).  The status of the save
           will be displayed briefly in the upper left corner.

           If you decide not to save, simply click on ABORT.


        COMPARE - This will alternate between the current tone and the
        original (the tone before editing; it can also be changed) for
        comparison purposes.  The word COMPARE will be highlighted if the
        'original' is the current tone.

        PANEL - Returns you to the first page, the control panel.


        EDITING THE TONE
        ================

        The edit page has several graphic elements (starting from the top
        down):

        1- the name of the tone is shown highlighted in the upper left
        corner.  To change the name, click inside the rectangle then
        enter the new name through the keyboard.  You can BACKSPACE to
        erase the last character.  There will be a beep once you reach
        the maximum number of characters allowed.  Press RETURN when you
        are finished.

        2- the 'structures' of both partial pairs are displayed below the
        tone name.  The top structure is the one used for partials 1 and
        2; the other one is used for partials 3 and 4.
        To change a structure, click on it and a selection of all
        thirteen partials will appear; click on one to select it.

        3- the envelope mode appears beneath the structures.  Click on
        the text to toggle between 'Normal' and 'No sustain' mode.

        4- to the right are several parameters listed with values beside
        them.  They are categorized by type.  These values belong to the
        partial whose number is highlighted (just below the TVF
        envelopes).  To change the partial whose parameters are seen
        here, simply click on the number of the partial and it will be
        highlighted.

        5- the current edit parameter is shown with its numeric range
        underneath.

        D-10 CONTROL 1.0         7


        Beside are the options [RND] and [ALT].  [RND] allows you to
        select random values, [ALT] alternates between the previous and
        current value.

        6-Beside are four slides, which operate in the same fashion as
        described before.  The numbers 1 through 4 are the partial for
        whom the slide changes the value of its parameter.  By clicking
        on these numbers, they will be highlighted (click again to undo
        it).  When more than one partial is highlighted and the value for
        one of these partials is changed, the rest will be changed to the
        same value.  This allows simultaneous editing of several
        partials.

        7-Below are several envelopes which graphically describe the
        PITCH, TVA (Time Variant Amplitude) and TVF (Time Variant
        Frequency) envelopes for each partial.  The envelopes are defined
        by the envelope parameters listed above them.  These envelopes
        are affected by changes (performed with the slides) in related
        parameters; button presses at the envelopes will not do anything.
        The dashed vertical line represents the key off point for the
        envelope (ie. the time when you release a key).

           NOTE: not every partial will have a TVF envelope because this
           is related to whether the partial is a square/sawtooth wave or
           a PCM wave.  For this same reason, the TVF parameters may or
           may not be listed for a given partial.

        8-There are more parameters and values for each partial below.
        If you click on the partial number, you change which partial has
        their parameter values shown at the upper right.  If you click in
        the empty space beside the number, you can mute/unmute the
        partial.  If muted, the word MUTED will appear.

        9-The wave name is shown below the partial number.  Depending on
        the structure being used, the wave is either SQUARE/SAWTOOTH or a
        PCM wave.  If an 'S' appears in the corresponding structure, the
        wave is a synthesized wave (ie SQUARE/SAWTOOTH); a 'P' means that
        the wave is a PCM wave and the wave name appears.  If you click
        here, if the wave is 'S' type, the wave will toggle between
        SQUARE and SAWTOOTH.  Otherwise, another page will appear where
        you can select the PCM wave from 256 preset waves (only 128 will
        appear at a time).

           A list of PCM waves will appear with the current wave
           highlighted. To select one, just click on the name; it will be
           highlighted.  The options which appear at the bottom are:

           PARTIAL # - You can change which partial you are selecting a
           wave for.  If the partial is not a PCM wave, its # will not
           appear.

           ORDER - Changes the list order from the synth's internal order
           to alphabetic order and vice versa.

        D-10 CONTROL 1.0         8


           ALT - Alternates between the current and previous selection.

           PAGE - Displays the other 128 waves.

           If you click on a wave twice in a row, you will return to the
           edit page.


        To edit a parameter, click on the name or value of the parameter.
        This will make it the current edit parameter, which the slides
        can alter.  You can now edit this parameter for any of the four
        partials in the manner described in points 5 & 6.  The values
        will instantly change and be updated on the page.

        If you are entering a tone from a magazine for example, some of
        the parameter values may be listed as a number that are not shown
        as numbers in this page (eg. the structures).  No problem - for
        example, the structures are listed in increasing order from left
        to right, top to bottom; if the structure is '1', click on the
        upper leftmost structure.  For PCM waves, first click on ORDER if
        the waves are listed in alphabetic order.  Now use PAGE to change
        banks.  PCM Bank 1 has 'Bass Drum 1' in the upper left corner,
        PCM Bank 2 has 'Bass Drum 1*'.  For PCM number, the waves are in
        increasing order from top to bottom, left to right (ie. 1 is in
        the upper left, 128 in the bottom right).


        Now, back to the CONTROL PANEL top line options.  Click on the
        word for the following features:

        FILE
        ====

        This page allows several sections of the synth's memory to be
        saved onto the hard disk or floppy and retrieved later.  If you
        have an unregistered copy, you will not be able to load or save
        sound files; only after you register your copy and follow
        registration instructions will you be able to.

        The page contains two columns of check boxes which correspond to
        different sections of the synth's memory that can be saved.  The
        leftmost one (with letter 'L' at the top) displays the sections
        that a sound file contains (if you click on a sound file in the
        directory section).  The right one defines what sections you wish
        to save.  The sections are:

        Timbre temp area - contains the timbres assigned to the eight
        Parts.
        Tone temp area - contains the tones assigned to the eight Parts.
        Tone memory i01-i32 - 32 of the tones stored in the synth's user
        memory
        Tone memory i33-i64 - the other 32 tones in user memory
        Timbre memory Bank A - the 64 timbres in timbre bank A
        Timbre memory Bank B - the 64 timbres in timbre bank B

        D-10 CONTROL 1.0         9


        Patch memory - 128 patches for use in the Performance mode.

        The reason why the tone and timbre memory have two sections each
        is to allow the ability to mix and match information between the
        halves (because they can be saved and retrieved separately).

        If you save either or both of timbre & tone temporary area, the
        volume, panpot, master tune and reverb settings will
        automatically be saved with them.


        Beside are SAVE and LOAD with three boxes.  The top one contains
        the current file name, the two below the comment areas.  The
        comment areas are for the entering/viewing of comments, if any,
        about the sound file.

        The bottom half of the page consists of the directory window.
        Directories are always listed (they have 'dir' beside them).
        Click on one to move to another directory.  Click on '..' to go
        to the parent directory.

        Files that match the file specification (displayed in the middle
        of the page) and are in the current directory (displayed to the
        left of the file spec) are listed.  To change the file spec,
        click inside the rectangle and type in the new one.  You may use
        the wildcard characters '*' and '?'.  Use BACKSPACE to erase the
        last character, RETURN when done.  Only the file name and
        extension will be used (e.g. if you specify a drive name in the
        mask, it will be ignored).  The message "Bad file spec" will
        appear if the file spec is invalid;  the previous one will be
        used instead.

        If there are more directories and files than can be shown in the
        window, click on PREV PAGE or NEXT PAGE to see the other
        directories and files.

        You may change disk drives by clicking on one of the drive names
        labelled 'A' through 'D' on the bottom line.  If you are
        accessing a floppy disk, click on the drive name after inserting
        a different disk, so that its directory will be read.

        If there are any problems encountered or messages, they will
        appear in the message window to the right of the file spec,
        otherwise it will be blank.


        LOADING A SOUND FILE
        ===================

        If you click on a file inside the dir window, the program will
        check if it is a sound file and if it is not, "Not a sound file"
        will appear in the message window.  Otherwise, the file name and
        the comments in the file, if any, are displayed in the load area.
        The sections that the file contains are shown in the check boxes

        D-10 CONTROL 1.0         10


        under the 'L'.  If you click on LOAD, the computer will read from
        the disk and send the information to the synth.  If successful,
        the word LOAD will not be highlighted anymore.  The section that
        the computer is currently sending will be highlighted during the
        duration of the send.


        SAVING A SOUND FILE
        ===================

        To save a configuration, first set the check boxes (by clicking
        on the boxes or the section names; the boxes will toggle on/off)
        to the sections to be saved.  Next, write any comments into the
        boxes by clicking inside a comment box (in the SAVE section) and
        typing in the comments (press BACKSPACE to delete last character,
        RETURN when finished; a beep will sound if the maximum comment
        length has been reached).  Previous comments will be erased.
        Finally, click inside the rectangle beside SAVE and enter the
        file name.  The file extension '.D10' will automatically be
        appended if no extension is specified.  If the file name is
        invalid, the message "Bad file name" will appear, otherwise the
        current directory will be searched to see if there is a file
        using the same name.  If so, the warning "Name already used" will
        appear.  This file will be replaced if SAVE is performed.  Avoid
        playing on the keyboard while save is occuring since this would
        add more MIDI traffic and would slow down the SAVE process (and
        possibly cause a 'Synth not resplying' error because the synth is
        not able to send the info in the time the computer expects).

        The sound file will only be saved when SAVED is clicked on; if
        successful, the word SAVE will not be highlighted anymore.  The
        computer will then read the memory sections from the synth and
        save it to the file.  The sections that the computer is currently
        reading from synth and writing to disk will be highlighted.  If
        any errors occur, save will be aborted and the incomplete file
        erased.

        Click on PANEL to return to the control panel.

        There are several other messages that might appear in the message
        window:

        - "No files or dirs" - no files matched the file specification
        plus there were no directories
        - "Can't read drive" - there was a problem in trying to
        read/write from the specified drive (attempting to save on a
        write protected disk will cause this)
        - "File not found" - the selected file was not found
        - "Can't overwrite" - could not overwrite the selected file
        because it was read only
        - "Not enough space" - ran out of room for the file on the disk
        - "OutOfMem" - ran out of memory for storing the directory; the
        directory listing will be incomplete
        - "Error during save" - an error occurred during save

        D-10 CONTROL 1.0         11


        - "Error during load" - an error occurred during load
        - "Synth not replying" - the synth was not responding to a read
        request
        - "Couldn't change dir" - an error was encountered while trying
        to change directories


        TIMBRE MAP
        ==========

        This is a 'map' of all of the timbres stored in the synth:
        timbre banks A, B and those of the Parts.  Beside the timbre
        bank/number, the tone referenced by the timbre is shown with its
        bank (A,B,I,R)/number.

        If the program has not already read the timbre-tone references,
        it will do so before displaying this page.  There will be short
        delay as this information is received and organized.

        You can copy timbres from either the synth's timbre banks OR
        Parts to other timbre slots OR Parts.  To do this, click on a
        source timbre (the one to be copied) then on a destination
        timbre.  There are no restrictions on which timbres can be source
        or destination.  You can UNDO the most recent change by clicking
        on UNDO.

        For the eight Part timbres at the bottom, the tone listed might
        not necessarily match the current tone for the Part.  This means
        that the tone for the timbre has been changed.  Every timbre has
        a reference to a tone in the synth's memory; this tone reference
        (as opposed to the actual tone information) is copied to the
        Part's timbre memory.  Once there, the tone can be changed in
        this temporary area, and thus there may be a discrepancy.

        Return to the control panel by clicking on ACCEPT.


        CONFIGURATION
        =============

        This page allows you to customize the program.  This page will
        always have fixed colors, but any color changes will affect all
        other pages and the color sample on the right half of the page.
        If your copy is unregistered, you will not be able to change the
        colors.

        The parameters are:

        1) Exclusive Unit# - this has to match the MIDI exclusive unit
        number which the synth is set to, otherwise the computer cannot
        communicate with it.  Press 'MIDI' on the synth then 'DISPLAY
        down' until the number is displayed to check if it matches.

        D-10 CONTROL 1.0         12


        2) Travel Ratio - this is the ratio of mouse movement to cursor
        movement.  High values mean that the mouse has to be moved
        considerably for small changes in the cursor's position.

        3) Repeat Speed - the speed of increment/decrement on the data
        slides.  The higher the value, the slower the slide will move
        when the mouse button is held down at the '<' or '>'.

        4) Colors - there are several color parameters.  The colors of
        all pages (except the Configuration page) will be affected.  The
        colors of the sample window in the right half will change,
        allowing you to judge the color changes.

        5) Registration Number- The registration number will be shown
        here.

        6) User Name - once you are registered, enter your name here.  In
        the INFO page, your name will be shown.

        To save these changes, press a button at the word SAVE (on the
        top line).  This will save the configuration to the current
        directory (D-10 Control automatically checks for a configuration
        file in the current directory when it is run and will
        automatically load it if found).  If you have saved since
        entering this page, the word SAVE will not be highlighted
        anymore.

        To change back to the default settings, press a button at the
        word DEFAULTS.

        Press ACCEPT to return to the control panel.


        INFO
        ====

        This page displays information about the program.  If the copy is
        not licensed, a message will appear with registration
        information.  If the copy is licensed, the registration code and
        the user name will be shown.


        QUIT
        ====

        This exits the program.   You must click on either the Q or U to
        quit; I or T will not quit.


        NOTE FOR D-20 USERS
        ===================

        There is a 'bug' on some older D-20's which causes the master
        tune and volume settings to be forgotten (and set to the lowest

        D-10 CONTROL 1.0         13


        possible values) when power is turned off, or the mode is
        switched to performance mode and back when these parameters are
        adjusted through MIDI.  The remedy is to get new ROM's (I think!,
        I haven't got mine yet...).  To check which version of ROM's you
        have, hold EDIT and DATA TRANSFER, when you power on until it
        appears in the window.  Contact your dealer for the numbers of
        the latest versions and information on how to obtain an upgrade.


        DISCLAIMER
        ==========

        Midieval Software hereby disclaims all warranties relating to
        this software, whether express or implied, including without
        limitation any implied warranties of merchantability or fitness
        for a particular purpose.  Midieval Software will not be liable
        for any special, incidental, consequential, indirect or similar
        damges due to loss of data or any other reason, even if Midieval
        Software or an agent of Midieval Software has been advised of the
        possibility of such damages.  In no event shall Midieval
        Software's liability for any damages arising out of the use of or
        inability to use this software exceed the price paid for the
        license to use this software, regardless of the form of the
        claim.  The person using this software bears all risk as to the
        quality and performance of the software.


        LICENSE
        =======

        D-10 Control is distributed as User Supported software.
        Unregistered users of D-10 Control are granted a license to use
        this software for 14 days for evaluation purposes.  After this
        period has expired and the user decides to continue using it, the
        user must register the copy.  A registered copy of D-10 Control
        must be treated just like a book; the same registered copy may
        only be used on one computer at the same time.

           You may give this software to others to try out under the
           following conditions:

        1. You may NOT modify or remove the program or any other files in
           this package.
        2. You may not levy any charge or payment for D-10 Control.

        Clubs and user groups may charge a nominal fee not exceeding $10
        US for expenses and handling while distributing D-10 Control.


        When you register, you will receive a registration number and
        instructions as to how to store it on your copy.  This will allow
        you to use all of the features of the program and avoid messages
        about registration.  You will also receive notices of updates and
        technical support.  If you require technical support, have

        D-10 CONTROL 1.0         14


        comments or suggestions, send your correspondence to the address
        below or if you have a modem, leave the message at 'Midnight MIDI
        BBS'(tm) at (613)747-1718 to 'Harry Mark' on FIDO-Net's MIDI-Net 
        conference, or send NetMail to address 1:163/230.0.
        
        Your support will help us create more high quality software at
        reasonable prices.

        Registration just costs US$29/CDN$36.  The cost of a license plus
        disk plus printed documentation is $36 US/$45 CDN (Ontario
        residents must add 8% sales tax if ordering reg+disk+docs).

        To register, send the order form (or reproduction) with the check
        or money order (payable to Midieval Software).  For fastest
        processing possible, please send a money order.




        D-10 CONTROL 1.0
        --------------------------
        Midieval Software
        P.O. Box 902
        North Bay, Ontario, Canada
        P1B 8K1
        --------------------------


        Please check one of the following:

        [ ] Registration ($29 US/$36 CDN)

        [ ] Registraton + Disk + Printed Documentation ($36 US/$45 CDN)
            Ontario Residents add 8% sales tax (Total Cost $48.60 CDN)
            Diskette type (please check one): [ ] 5.25"   [ ] 3.5"


        NAME:
        ____________________________________________________________

        ADDRESS:
        ___________________________________________________________

        ___________________________________________________________

        ___________________________________________________________

        PHONE: _________________________________


        Where did you get your copy of D-10 Control?

        ___________________________________________________

        Comments/Suggestions

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________

        _________________________________________________________________


        Thank you for your support.