ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³             ASCII Documentation File for ... CAPQUANT               ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
³                   A MS-DOS Software System for...                   ³
³                                                                     ³
³            ***  Quantification of Process Capability  ***           ³
³                                                                     ³
³           Via the Cumulative Distribution of Regret Indices         ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
³                  A Quality Assurance Training Tool:                 ³
³              Statistics Committee of the QA Section of              ³
³            the Pharmaceutical Manufacturers Association             ³
³                                                                     ³
³                  Bob Obenchain, Research Scientist                  ³
³     Statistical and Mathematical Services, Eli Lilly and Company    ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

Any type of quantitative (variables) data measurement can be used as a
basis for Process Capability Quantification via a three-stage analysis
process:

    (i) Convert each observed numeric value into a REGRET, which is a
        measure of long-range economic impact or customer/regulatory
        dissatisfaction that results from product deviations from an
        intended TARGET value (or values.)

             CapQuant allows the user to pick the regret function from
             any of 9 general families and to specify the target value.

   (ii) Smooth and Standardize the observed distribution of historical
        regret values (via POISSONIZATION) to form a REGRET INDEX.

             CapQuant determines an EQUIVALENT NONCONFORMANCE value for
             each regret and the corresponding EQUIVALENT EXPECTANCY,
             the expected regret within historical capability levels.
             The corresponding INDEX is simply the ratio of observed
             to expected regret.  An index value of 0 is ideal, while
             an index value of 1 is the historical quality standard.

   (iii) Generate PROCESS CAPABILITY PLOTS ...medium resolution CGA
         graphical displays (320 x 200 pixels) of the Cumulative
         Probability Distribution Function of the Regret Index.

             CapQuant can plot the cumulative distribution function for
             process history consisting of as many as 2500 observations.
             Both the observed (raw) and Poisson smoothed forms are
             displayed.  CapQuant also allows direct graphical
             comparisons between "new" sample results (most recent
             history) with the that portion of older history deemed most
             relevant to current operations.

CapQuant software provides the computational tools needed to implement
specific analyses of the above type.  CapQuant creates an ASCII output
file of extremely detailed results that, following minor manual editing,
provides an ideal data input file to statistical and/or presentation
graphics systems, such as SAS.  But only a small fraction of CapQuant's
outputs (those which are displayed on your computer screen as well as
written to the ASCII output file) are needed to characterize the
(historical) capability of a manufacturing process.


                           TABLE-OF-CONTENTS

Usage of the CapQuant Pop-Up Menus . . . . . . . . . . . . . . . . . 2
REGRET FUNCTIONS: Quantify Impact of Deviations from Target. . . . .10
Equivalent Nonconformance and Expectancy . . . . . . . . . . . . . .15
References . . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
Appendix: Technical Descriptions of the Poissonization Process . . .20

                    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                    ³  *** USAGE of CAPQUANT ***  ³
                    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The CapQuant software system is invoked from MS-DOS by entering its
8-character name, CAPQUANT, at your DOS prompt...

                            Prompt> capquant

CapQuant does not expect or accept any "command-line" arguments.
Instead, CapQuant will prompt you to provide all information it needs to
perform analyses.  And each such prompt usually displays a [default value]
in square brackets that you may accept by simply pressing the ENTER key.

CapQuant Input/Output File Naming Conventions...
------------------------------------------------

The ASCII (text) files used by CapQuant for data input and output
consist of a filename (of at most eight characters) specified by the
user followed by a period (.) and one of four specific 3-character
filename EXTensions.

    BILINEAR.HST  ...Batch Input of Historical Data (at most 2500 obs.)
    BILINEAR.NEW  ...Batch Input of New Data (at most 250 observations)
    BILINEAR.OUT  ...Batch Input of Historical Data (at most 2500 obs.)
    BILINEAR.XXX  ...CapQuant Output  for Automatic REGret Calculations.
    BILINEAR.REG  ...Edited .XXX File for Automatic REGret Calculations.

Example CapQuant Walk-Through...
--------------------------------

The CapQuant start-up screen will appear as follows...

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ  Capability Quantification ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                                   º
º                      CAPQUANT.EXE...Version 9010                  º
º                                                                   º
º                   A Quality Assurance Training Tool:              º
º           Statistics Committee of the QA Section of the PMA       º
º                                                                   º
º ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ» º
º º  Will Process HISTORY be Input via K = Keyboard ? ...or       º º
º º                                    B = Batch File ?           º º
º º                                                               º º
º º  Press the   K   or   B   key now -->                         º º
º ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

If you select Keyboard input, you will be prompted to type in all
historical data values using your keyboard.  But, in this case, CapQuant
will also be creating a "Batch Input" file that you could use in future
CapQuant runs to repeat and/or modify your initial analyses.

On the other hand, if you are familiar with a "screen oriented" personal
computer (ASCII) text editor, you might prefer to start by creating your
own "Batch Input" file.  This strategy can give you more flexability in
data entry and validation than is possible inside of CapQuant.  Simply
mimick the format of an example CapQuant Batch Input file.  For example,
the Batch Input file could consist for the following 7 records (rows),
each starting in column 1:

               1        ...Number of Data Values per Observation
               THICKNES ...Name of Variable ONE
               1.09
               2   
               13  
               4.7 
               3   
               q

where the letter Q at the start of the last record signals the "end of
data entry."

Once you respond to the initial CapQuant prompt by pressing either the K
or the B key, the "Window" will clear itself, and you will be prompted
to specify a MS-DOS filename, consisting of at most 8 characters.

If you have selected Keyboard input, this filename will be used to
capture the data you will be entering.  Or, as shown below, that
filename (with a MS-DOS filename extension of ".HST") will be read in as
Batch input.  For either Keyboard or Batch input, the CapQuant Output
file can have either the same filename or a different filename (8
characters maximum.) But the 3-character MS-DOS filename EXTension will
always be ".OUT".
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ  Capability Quantification ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                                 º
º  Batch File Input Selected...                                   º
º                                                                 º
º  At colon Prompts : ...simply press ENTER to get the [default]. º
º  -------------------------------------------------------------- º
º                                                                 º
º  Specify filename for Batch Input [capquant] : batfname         º
º  The Batch Input file is to be: batfname.hst                    º
º                                                                 º
º  Specify filename for Detailed Output [batfname.out] :          º
º  The CAPQUANT Output Save file is to be: batfname.out           º
º                                                                 º
º          Press Q to QUIT now...Other Key to Continue...         º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

A [Black on Green] window for Parameter Specification appears next...
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ    CapQuant  Parameters    ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                                 º
º  Does data consist of Single Values or Pairs (1 or 2) :         º
º  Number of Data Values per Observation =  1.                    º
º                                                                 º
º  What is the NAME of Variable ONE ? [variable1] :               º
º  First  Variable Name: DISSOLUT                                 º
º                                                                 º
º  Historical Data, in any sequence, are to be entered            º
º  in the Next Window...  Press Q to QUIT now...                  º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

A [Blue on Cyan] Data Entry window now appears.  If you are using
Keyboard input, CapQuant will continue prompting for either single
values or data pairs until you ENTER the letter Q to signal an end to
data entry.  The number of observations entered will then be
displayed...
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   Data Entry Window    ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                                 º
º        List Historical Data in Output File? [y|n] : n           º
º                                                                 º
º        Number of Historical Observations =  264                 º
º                                                                 º
º        Data Entry Complete...                                   º
º        Press Q to QUIT now...Other Key to Continue...           º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

Small windows will now Pop-Up within the [Blue on Cyan] Large Window.

You first selection from the left-hand "Process Capability MENU" should
always be "R".  (...Unless you wish to "eXit" without making any
calculations!)

You first selection from the middle "REGRET Analysis MENU" should always be
"S".  (Unless you wish to Return without making any calculations!)

Then you choose a Regret-Function-Family from the right-hand "REGRET
Function MENU."  (Unless you wish to Abandon/Quit without making
any calculations!)

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º  Process Capability MENU    º
º                             º
º     R = Regret Analysis     º
º                             º           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º     C = Capability Plot     º           º REGRET Function MENU    º
º             ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍº                         º
º     M = Moniº     REGRET Analysis MENU  º 1...ATTRIBUTES          º
º             º                           º 2...QUADRATIC           º
º     X = eXitº S = Specify Regret Functioº 3...ABSVALUE            º
º             º                           º 4...1-SIDED QUADRATIC   º
º Choice --> Rº I = Regret INDEX Computatiº 5...BILINEAR            º
º             º                           º 6...END-POINT QUADRATIC º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍº L = Poisson Lack-of-Fit Teº 7...BOUNDED MAXIMUM     º
              º                           º 8...RANGEMAX            º
              º A = Automatic Regret Calcsº 9...NONCONFORM/EXPTANCY º
              º                           º 0...Abandon/Quit        º
              º R = Return to Main Menu   º                         º
              º                           º Choice -->              º
              º Choice --> S              º                         º
              º                           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
              ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

The regret functions which can be defined in CapQuant belong to one of
nine general families.

        1) attributes regret, which is zero inside an interval and one
           outside that same interval,

        2) quadratic regret, where the regret is the square of the deviation
           of the measurement from its target value,

        3) linear regret, in which the economic impact of a measurement is
           directly proportional to the measurement's value,

        4) one-sided regret, which is quadratic on one side of a target
           and zero on the other side of that target value,

        5) opportunity regret, in which the economic impact of a demand
           for a perishable product is measured relative to the
           inventory on hand,

        6) end-point quadratic regret, in which the minimum and maximum
           observed values in samples of fixed size are monitored, and
           regret is the sum of the quadratic regret at the two end-points,

        7) bounded max regret, in which regret follows a double-logit
           pattern that is V-shaped in its center (at the target) but
           flat like attribute regret in its tails, and

        8) range (linear) regret, in which the minimum and maximum
           observed values in samples of fixed size are monitored, and
           regret is the difference, maximum minus minimum.

        9) an unspecified pattern called "nonconformance-expectancy."
           In this case, the data are assumed to have been "Poisson"ized
           outside of CapQuant, but you can still use CapQuant to make
           Capability Plots and/or to test Lack-of-Fit.

See the section of this CapQuant documentation, starting on page 10,
that discusses REGRET FUNCTIONS for detailed information on these nine
families.

The numerical example used here is based on...

         Regret Type:    ONESIDED
         TARGET = Value corresponding to ZERO REGRET = 100.00
         PARM1  =   -1  ... ZERO REGRET to LEFT of TARGET.

Once you have specified a functional form for your Regret Function and
have selected values for its Parameters (TARGET, PARM1, PARM2), the
"REGRET Analysis MENU" will re-appear.  One's second selection from this
menu is usually the second item, "I"...

               ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º     REGRET Analysis MENU     º
               º S = Specify Regret Function  º
               º I = Regret INDEX Computationsº
               º L = Poisson Lack-of-Fit Test º
               º A = Automatic Regret Calcs   º
               º R = Return to Main Menu      º
               º Choice --> S                 º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   Regret Calculations  ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                         º
º Observations (Periods) = 264                            º
º Regret Type   =  4                                      º
º                                                         º
º Observed Average (Expected) Regret =   51.608           º
º                                                         º
º Observed Std. Error of Regret =  88.6406                º
º                                                         º
º Corresponding Equivalent Expectancy = 0.3390            º
º                                                         º
º Enter Objective Expected Regret [   1.000] : 50         º
º         using...   50.000                               º
º                                                         º
º Enter Objective Std. Error [  85.879] : 100             º
º         using...  100.000                               º
º                                                         º
º Equivalent Expectancy per Observation =   0.2500        º
º                                                         º
º End of Regret & Equivalent Nonconformance Calculations. º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

As in the above example, the "Objective Expected Regret" value is
usually taken to be a convenient, "rounded" value (50, here) that is
fairly close to the observed, sample value (51.6).  The initial default
value for Expected Regret will always be [ 1.000].  But, if you select
item "I" on the "REGRET Analysis MENU" more than once, the subsequent
default value will be the value you entered in the previous iteration.

The default value [85.879] for the "Objective Std. Error," is the
numerical value that (given an objective expected regret of 50 rather
than the observed 51.6) would equate the objective "Equivalent
Expectancy per Observation" to the observed value of 0.3390.  This
default value will not, necessarily, also equate the mean and variance
of the rescaled regret distribution...unless the objective and observed
expected regret values are exactly equal.

In the above example, a convenient, "rounded" value (100) is also
entered for the "Objective Std. Error,"  and the resulting "Equivalent
Expectancy per Observation" is computed by CapQuant to be 0.25.  Later,
if you use item "L" to test Lack-of-Fit of rescaled regrets to the
Poisson distribution, the Poisson "intensity" parameter ( = mean =
variance ) will be the "Equivalent Expectancy per Observation" value
(0.25, here.)

The "REGRET Analysis MENU" will re-appear again.  As implied above, your
selection might again be the second item, "I".  For example, you would
re-run "I" if you were unhappy with the "Equivalent Expectancy per
Observation" ( .25 above ) that resulted from your two choices...for
"Objective Expected Regret" and "Objective Std. Error" (50 and 100,
respectively.)  See the section of this documentation, starting on page
14, that discusses Equivalent Nonconformances and Expectancy for
detailed information on this CRITICAL phase of the analysis.

Here... EXPREGRET objective =    50.0 ...observed =   51.6075
        VARREGRET objective = 10000.0 ...observed = 7857.1484

The third item ("L") on the "REGRET Analysis MENU" provides optional
(rather than mandatory) calculations.  But statistically significant
Lack-of-Fit revealed via this "L" item can suggest the need to change
one's regret mean and variance objectives ( item "I" ) if not the very
form of that regret ( item "S" ).

NOTES:  Always re-run item "I" after each change you make to the regret
function via item "S".  And never select item "L" except after item
"I"...
               ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º     REGRET Analysis MENU     º
               º S = Specify Regret Function  º
               º I = Regret INDEX Computationsº
               º L = Poisson Lack-of-Fit Test º
               º A = Automatic Regret Calcs   º
               º R = Return to Main Menu      º
               º Choice --> L                 º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍPoisson Lack-of-Fit TestÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                         º
º Kolmogorov-Smirnov Statistic =   0.03938                º
º 5% Critical Value =  0.08                               º
º 1% Critical Value =  0.10                               º
º Distribution is not significantly                       º
º different from the fitted Poisson.                      º
º                                                         º
º Value, Frequency, CumFreq, and Poisson Fit...           º
º    0   0.81818   0.81818   0.77880                      º
º    1   0.14773   0.96591   0.97350                      º
º    2   0.03030   0.99621   0.99784                      º
º    3   0.00379   1.00000   0.99987                      º
º    4   0.00000   1.00000   0.99999                      º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

NOTE: All "Equivalent Nonconformance" values were rounded to the nearest
full integer value for the purpose of the above Lack-of-Fit test because
Poisson random variables take on only integer values.  But this rounding
really represents an unnecessary loss-of-precision in most quality
monitoring applications.  Thus CapQuant does not round nonconformance
numbers to integers before invoking the CPQ algorithm.  In fact,
CapQuant lists nonconformance/expectancy results to 2 decimal places in
the ASCII output file.

Let us suppose that you now select item "R" on the REGRET MENU followed by
item "C" on the Main MENU...
         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
         º  Process Capability MENU    º
         º     R = Regret Analysis     º
         º     C = Capability Plot     º
         º     M = Monitor Capability  º  <--- 2 nd Selection
         º     X = eXit CAPQUANT       ºÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
         º Choice --> C                ºysis MENU       º
         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼oss Function    º
                          º A = Automatic Regret Calcs  º
     1 st Selection --->  º R = Return to Main Menu     º
                          º Choice --> R                º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                                                      
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ CPQ Trend Calculations ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                                º
º Observations (Periods) = 264                                   º
º                                                                º
º View Listing of Results Now? [y|n] : y                         º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

Graphics HELP Screen...
                  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                  ³  This HELP screen .... Space Bar or F1. ³
                  ³                                         ³
                  ³  ERASE PLOT......press ENTER or ESCape. ³
                  ³    Note: 2nd KeyPress sometimes needed. ³
                  ³                                         ³
                  ³  On-Screen Cursor & VALUES ... press V. ³
                  ³  Move Right/Left with ArrowKeys by 0.01 ³
                  ³             or... Tab/BackSpace by 0.25 ³
                  ³                                         ³
                  ³  Screen PRINT/SAVE Keys:  First Press S ³
                  ³  and then press a Second Special Key... ³
                  ³   L or F10 dumps to HP LaserJet/DeskJet ³
                  ³   I or F9  dumps to IBM Graphics Matrix ³
                  ³   E or F8  dumps to Epson FX, JX, or LQ ³
                  ³   O or F7  dumps to Okidata Microline   ³
                  ³   S saves screen to disk in PCX format. ³
                  ³                                         ³
                  ³  CapQuant, ver9010.......Press any key. ³
                  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

One iteration through the three-stages of quality monitoring
calculations is now complete.  You now have the options of either
pressing "L" to return to the REGRET Menu for further calculations or "X"
to exit CapQuant and return to DOS.  (It would be an absolute waste to
repeat CPQ Trend Calculations, item "C", without first changing either
the regret function or the objective regret mean or variance.)

                         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                         º  Process Capability MENU    º
                         º     R = Regret Analysis     º
                         º     C = Capability Plot     º
                         º     M = Monitor Capability  º
                         º     X = eXit CAPQUANT       º
                         º Choice --> M                º
                         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ    Capability Monitoring   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                                                                        º
º  Display Historical Capability in R = Raw     ...or                    º
º                                   S = Smoothed Form ?                  º
º                                                                        º
º  Press the   R   or   S   key now -->  S                               º
º                                                                        º
º  Will NEW Process Data be Input via K = Keyboard ? ...or               º
º                                     B = Batch File ?                   º
º                                                                        º
º  Press the   K   or   B   key now -->  B                               º
º                                                                        º
º  Batch Input of New Data Selected...                                   º
º                                                                        º
º  Specify filename for New Data Batch Input [batfname] :                º
º                                                                        º
º  The New Data Batch Input file is to be: batfname.new                  º
º                                                                        º
º  Pause at each New Data Value [Y|n] :                                  º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

When you do eXit from CapQuant, you screen will display...

                         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                         º  Process Capability MENU    º
                         º     R = Regret Analysis     º
                         º     C = Capability Plot     º
                         º     M = Monitor Capability  º
                         º     X = eXit CAPQUANT       º
                         º Choice --> X                º
                         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
        REMINDER(S):

        CAPQUANT created an Output File named... batfname.out

                Use the DOS invocation... LIST batfname.out
                to review detailed computational results from
                this CAPQUANT run.

-----------------------------------------------------------------------

                             REGRET FUNCTIONS

We need a rule for transforming every possible value for the variable
into its corresponding regret value.  In other words, we need to specify a
"functional relationship."  The variable may assume negative values, but
the corresponding regret must be zero or positive.  This usually means
that the regret function is "non-linear" and that more than one value for
the variable can yield the same value for the regret (i.e. regret may be a
non-invertible function.)  All that is really necessary is that the
regret
function provide some sort of common-sense "proxy" for the economic
impact of deviations from intended target value(s).

In CapQuant, you may select a Regret Function from any of nine general
families:
                ATTRIBUT        QUADRATC        ABSVALUE
                ONESIDED        BILINEAR        ENDPOINT
                BOUNDMAX        RANGEMAX        NONCEXPT

Each of these Regret Functions can have as many as three Parameters:
TARGET (the value of the variable resulting to Zero-Regret), PARM1,
and PARM2.


REGRET Type:    ATTRIBUT

Description:    Economic Impact is either 0 (negligible) or 1
                (complete).  A variable measurement outside of an
                acceptable range indicates a nonconformance (defect.)

                          Variables Measurement -->

                            |                   |
    Regret = 1  ************|                   |*************
                            |                   |
                            |                   |
                            |                   |
    Regret = 0  ------------*********************------------
                            |                   |
                          Lower               Upper
                          Bound               Bound

Parameters:     No single TARGET value is specified.  Regret is zero
                over the interval from  PARM1 = Lower Bound
                                  to    PARM2 = Upper Bound.

REGRET Type:    QUADRATC         (Taguchi's "Loss-to-Society")

Description:    Economic Impact is assumed to be proportional
                to the SQUARE of the deviation of the measured
                value from its (zero nonconformance) TARGET value.

                    *      Variables Measurement -->  *
                                     |
                      *              |              *
                       *             |             *
                        **           |           **
                          **         |         **
                            ***      |      ***
                               ***   |   ***
    Regret = 0  ------------------*******---------------------
                                     |
                                  TARGET

                     REGRET = ( Value - TARGET )^2

Parameters:     TARGET = Value corresponding to ZERO REGRET.

                No PARM1 or PARM2 values need be specified.

-------------------------------------------------------------------

REGRET Type:    ABSVALUE    (...symmetric BILINEAR )

Description:    Economic Impact is assumed to be directly
                proportional to the measured value.

                                     |    Variables Measurement -->
         ***                         |                         ***
            ***                      |                      ***
               ***                   |                   ***
                  ***                |                ***
                     ***             |             ***
                        ***          |          ***
                           ***       |       ***
                              ***    |    ***
                                 *** | ***
      Regret = 0 -------------------***------------------------------
                                     |
                                TARGET = 0

Parameters:     No TARGET, PARM1 or PARM2 values need be specified.

Restrictions:   Variable measurements must be non-negative.
                TARGET is implicitly ZERO.

REGRET Type:    ONESIDED

Description:    Economic Impact is ZERO on one side of the TARGET
                and proportional to the SQUARE of the deviation
                from TARGET on the other side.

                           Variables Measurement -->
                     *               |
                                     |
                      *              |       PARM1 = +1
                       *             |
                        **           |       Zero Regret on
                          **         |       Right Side.
                            ***      |
                               ***   |
    Regret = 0  ------------------**********************************
                                     |
                                  TARGET

Parameters:     PARM1 is a LEFT(-1) or RIGHT(+1) indicator.
                PARM1 = -1 indicates zero regret left of TARGET.
                No PARM2 value need be specified.

-----------------------------------------------------------------

REGRET Type:    BILINEAR  (...asymmetric ABSVALUE)

Description:    Two variables measurements are required, a DEMAND
                level & an INVENTORY level for a perishable product.
                Economic Impact is proportional to production cost per
                unit when inventory > demand, but there is a Profit
                (Opportunity) Loss per unit when demand > inventory.

        ****            Demand -->
            ****                                        **
                ****                                  **
                    ****                            **
                        ****               |      **
                            ****           |    **
                                ****       |  **
                                    ****   |**
    Regret = 0  ------------------------****-----------------------
                                           |
                                       Inventory
                                         Level

Parameters:     PARM1 = Regret per Unit of Excess Inventory.
                PARM2 = Regret per Unit of Inventory Shortage.
                No TARGET value need be specified.

REGRET Type:    ENDPOINT (quadratic)

Description:    Two variables measurements are required, the MINIMUM
                and MAXIMUM observed values in a random sample of fixed
                size (say, 10 measurements.)  Economic Impact is assumed
                to be the SUM of the QUADRATC regrets at the min. and max.
                values.
                     *---------------|               *
                     |*              |              *
                     | **            |            **
                     |   **          |          **
                     |     ***       |-------***
                     |        ***    |    ***|
    Regret = 0  -----+-----------*********---+----------------
                    MIN              |      MAX
                     |            TARGET     |

           REGRET = ( MIN - TARGET )^2 + ( MAX - TARGET )^2

Parameters:     TARGET = Value corresponding to ZERO REGRET.
                No PARM1 or PARM2 values need be specified.

---------------------------------------------------------------------

REGRET Type:    BOUNDMAX

Description:    Economic Impact follows a double-logit pattern that
                is V-shaped at the target but flat like ATTRIBUT
                absolute DEVIATIONS of values from the TARGET.

                               Measurement-->
     PARM2     ------------|---------|---------|------------
                  *        |         |         |        *
                      *    |         |         |    *
                         * |         |         | *
                           |*        |        *|
                           |  *      |      *  |
                           |    *    |    *    |
                           |      *  |  *      |
                           |       * | *       |
                           |        *|*        |
   Regret = 0  ----------------------*----------------------
                           |      Target       |
                     Target-PARM1        Target+PARM1

          REGRET = ( PARM2 * DEVIATION ) / ( PARM1 + DEVIATION )

Parameters:     TARGET = Value corresponding to ZERO REGRET.
                PARM1  = DEVIATION from TARGET with regret = half MAX.
                PARM2  = MAXIMUM possible regret.

REGRET Type:    RANGEMAX   (...linear in Max - Min )

Description:    Two variables measurements are required, the
                MINIMUM and MAXIMUM observed values in a random
                sample of fixed size (say, 10 measurements.)
                Economic Impact is assumed to be proportional to the
                RANGE from the min. to the max. values.

                         |    Range = ( Max. - Min. ) -->
                         |
                         |                          ***
                         |                       ***
                         |                    ***
                         |                 ***
                         |              ***
                         |           ***
                         |        ***
                         |     ***
                         |  ***
    Regret = 0  ---------***------------------------------
                         |
                TARGET = 0

Parameters:     No TARGET, PARM1 or PARM2 values need be specified.

Restrictions:   Range must be non-negative.  TARGET is implicitly ZERO.

---------------------------------------------------------------------

REGRET Type:    NONCEXPT

Description:    Two variables measurements are required, the
                EQUIVALENT NONCONFORMANCES and the EQUIVALENT
                EXPECTANCY for each observation (production lot,
                period, etc.)

                With input data of this type, no Regret Function is
                actually specified.  Similarly, no Regret Mean or
                Variance are needed to Poissonize the regret.

Parameters:     No TARGET, PARM1 or PARM2 values need be specified.

-------------------------------------------------------------------------

                     Equivalent Nonconformance & Expectancy

The process of converting Regret into "Equivalent Nonconformances" and
"Equivalent Expectancy" is called "Poissonization"...

   REGRET = Long Range Economic Impact and/or Customer/Regulatory
            Dissatisfaction associated with Deviations from intended
            Target Value(s).

EXPREGRET = Expected Value of REGRET within the Historical Distribution
            of Process Capability.

VARREGRET = Variance of REGRET within the Historical Distribution of
            Process Capability.

     EN = Equivalent Nonconformances = REGRET * EXPREGRET / VARREGRET.

     EE = Equivalent Expectancy = EXPREGRET * EXPREGRET / VARREGRET.

Note, in particular, that this conversion process involves nothing more
than a simple "Change-of-Scale."  REGRET is multiplied by the EXPREGRET
/ VARREGRET ratio to compute Equivalent Nonconformances, EN.
Multiplication by this constant value assures that the mean and variance
of EN are equal (to EE = Equivalent Expectancy.)  This equality of mean
and variance is an essential characteristic of Poisson distributions.

The two key parameters needed to establish a successful application of
variables data to regret quantification are thus the expected value
(EXPREGRET) and the variance of the regret (VARREGRET) at standard quality.
Many different shapes for regret functions might be appropriate for any
particular variable in any particular production process.  The exact
form of the regret function chosen is sometimes not terribly important.
As a result, even after the regret function and all of its describing
parameters (TARGET, PARM1, and PARM2) have been specified, the critical
final phase of customizing a CPQ application still remains...choice of
numerical values for EXPREGRET and VARREGRET.

While it might be possible to specify the distribution of regret at
standard quality using only technical assumptions and theoretical
calculations, the more standard approach is an empirical one in which
actual data on the operation of the process are converted to regrets,
and the statistical distribution of those sample regrets is then studied.
If one has data on only a dozen or so lots, it could be misleading to
use the observed sample values of the mean and variance of regret as
EXPREGRET and VARREGRET, respectively, because small sample estimates
are imprecise.

On the other hand, even if one had data for hundreds of lots, it could
still be misleading to use the observed sample mean and variance of
regret to establish CapQuant parameter values because even large sample
results can be biased.  There could be several different causes of bias.
The data at hand may not represent the results of the process operating
at (or even near) an industry-wide "standard" quality level.  The
history being used might, in fact, reflect an operation in which
quality is either well above or well below standard.  Modern, new
manufacturing equipment (using, say, robotics) or a change in ingredient
formulations may have been introduced without changing the quality
standard that was barely within the capability of the old technology.

If you aren't an expert on the operation of the manufacturing process in
question, consult with an expert.  Develop opinions about the quality
level of the process as reflected in its history.  Ask yourself, "How
did I react to these quality monitoring results when I first saw them?"
(Or, "How would I have reacted if I had been the manager in charge at
that time?")  Were you ever concerned that the process might be out of
"statistical control?"  Did you ever become alarmed because rejection
rates jumped at final inspection or because in-process yield dropped?
Might you have reacted quite differently if the data had been only
slightly different?  Or, would your reactions have been basically the
same even if the data had shifted even more than it did in level and/or
were even more highly variable from lot-to-lot?

A common situation is that all the observed history reflects data taken
from the process when it was operating well within its current process
capability.  In other words, the variable could have deviated much more
from its target without management having been alarmed at all!  This
means that the values for EXPREGRET and VARREGRET that should be specified
to CapQuant will indeed differ from what is observed in the history.
General rules-of-thumb for this well-within-capability situation are...

   ...the EXPREGRET parameter should usually be chosen to be rather close
      to the observed value of the sample mean regret if the history that
      is available consists of 50 or more observations.

   ...the VARREGRET parameter, on the other hand, might be selected to be
      10 or even 100 times larger than the observed regret variance of the
      available data. (Note: This corresponds to a "Standard Error"
      value between 3 and 10 times larger than that actually observed.)

There are two primary reasons for using a rather large VARREGRET value.
Again, the history data may be very well behaved, and management would
not have been alarmed even if the deviations of measurements from the
target had been much larger than observed.  The second reason for using
a large variance is that variables data are very rich in information.
(Variables data are usually much more informative than nonconformance
data.)

   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
   ³ NOTE:  CapQuant does not actually accumulate results across  ³
   ³ variables, across products or over time to form either       ³
   ³ composite statistics or reporting-period summaries.  But, by ³
   ³ using one or more CapQuant output files, you can accumulate  ³
   ³ results any way you wish.  Because of "Poissonization", the  ³
   ³ composite Equivalent Nonconformances and Expectancies are    ³
   ³ both simply the respective SUMs over all relevant parts.     ³
   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

The CapQuant philosophy is to fine-tune parameter values by making
repeated "iterations" as follows:

    (i)   The general form and specific parameter values of the Regret
          Function are set using item "S" on the Regret Menu.

    (ii)  Using item "I" on the Regret Menu, the sample mean and variance
          of regret are displayed and you are prompted to enter values
          for EXPREGRET and VARREGRET.  As explained above, you may wish to
          consider using EXPREGRET and VARREGRET values that are not very
          close, numerically, to the values in your sample.

    (iii) Goodness-of-Fit of sample results to a Poisson distribution
          (with "intensity" EXPREGRET*EXPREGRET/VARREGRET) can then be checked
          using a Kolmogorov-Smirnov test (item "L" on the Regret Menu.)
          Statistically significant Lack-of-Fit is NOT fatal.  On the
          other hand, insignificance of distributional differences is
          always a welcome indication that your choices are supported
          by the available data.  [Of course, you could return to step
          (ii) now to see if different values of EXPREGRET and VARREGRET
          reduce Lack-of-Fit.]

    (iv)  Make a detailed Process Capability plot using item "C" on the
          Main MENU.  Study these results, using the on-screen cursor
          activated by the "V" key, and determine whether your results
          are consistent with the opinions of subject matter experts.

    (v)   If you are unhappy with the outcome of step (iv), you should

          either (1st choice)

              ...return to step (ii) and try out different values of
                 EXPREGRET and VARREGRET

          or (2nd choice)

              ...return to step (i) and try different regret function
                 parameters or even a different regret function family.

          Once you are happy with the outcome of step (iv), the modeling
          process is complete.

                             REFERENCES

CONOVER, W. J. (1980). Practical Nonparametric Statistics, 2nd. Ed.,
        Wiley [Kolmogorov-Smirnov table and approximation, page 462.]

HOADLEY, Bruce. (1981). "The Quality Measurement Plan, QMP."  Bell
        System Technical Journal, 60, 215-273.

HOADLEY, Bruce. (1986). "QUALITY MEASUREMENT PLAN(QMP)."  Encyclopedia
        of Statistical Sciences. (Kotz, Johnson and Read, Editors)
        Volume 7, pages 393-398.  New York, John Wiley.

INTRODUCTION TO QUALITY TREND CHARTS.  Bell Communications Research,
        Inc., January 1986 (18 page booklet.)

LINK, P. A., and RIPACKI, B. R., "Quality Assurance Approach to Fiber
        Optic Cable," International Wire and Cable Symposium
        Proceedings, 1985.

OBENCHAIN, Robert. "Regret Indices and the Quantification of Process
        Capability."  Submitted to Technometrics. 1990.

QUALITY MEASUREMENT PLAN (QMP).  Bell Communications Research Technical
        Reference, TR-TSY-000438.  Issue 1, April 1987.

-----------------------------------------------------------------------

                              APPENDIX ONE

         Poissonization:  Conversion of Economic Impact Measures into
                          Equivalent Nonconformances and Equivalent Expectancy.


                Section A.1    Nonconformance Expectancy

Attributes Data
Definition:     Nonconformance Expectancy is the product of the Sample
                Size times the Quality Standard (expressed in expected
                nonconformances per unit.)

Example:        When the quality standard is 0.004 nonconformances per
                unit, one needs to inspect 250 units in order to expect
                to see 1 nonconformance when quality is at the standard
                level.

Information
Content:        Under a Binomial model, the "moments" of the sampling
                distribution would be given by the familiar expressions:
                mean = n*p and variance = n*p*(1-p).  QMP (the Quality
                Measurement Plan) is based upon the Poisson (maximum
                variance) model with mean = variance = n*p, which is the
                nonconformance expectancy.  Expectancy is the primary
                measure of "information content" used in QMP and CPQ for
                sampling inspection data. [See Section A.3, below, for
                details on information content.]

Variables Data
Definition:     Equivalent nonconformances and equivalent expectancy can
                be defined by "Poissonizing" any continuous measure of
                regret, R.  [See Section A.2, below, for details on
                poissonization.]

Reporting       Experience with use of QMP at both Bell Communications
Period:         Research (Bellcore) and at AT&T Bell Laboratories
                suggests the following "Rule-of-Thumb" for aggregating
                sampling inspection data over "reporting periods"
                (usually either the 12 calendar months or 8-per-year):

          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³ An effective quality monitoring program requires sufficient ³
          ³ sampling inspection to produce a nonconformance expectancy  ³
          ³ of at least 2 nonconformances per reporting period.         ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                If production is so low or nonconformances are so rare
                that one would have to inspect more than 20% of total
                production to achieve a nonconformance expectancy of at
                least 2 nonconformances per reporting period, then
                "quantitative" quality monitoring is probably
                impractical.  (After all, QMP is the "most powerful"
                statistical method currently available; if QMP can't get
                the monitoring job done, what method can?)


             Section A.2    Equivalent Nonconformances & Expectancy

Definition:     Equivalent nonconformances and expectancy can be defined
                by "Poissonizing" a continuous measure of regret, R.
                For example, if E is the expected value of R and V is
                the variance of R, then the number of "equivalent
                nonconformances" is said to be R*E/V, which is usually
                not an integer value.  But the mean and variance of
                R*E/V are both equal to the "equivalent expectancy" of
                E*E/V...and equality of mean and variance is an
                intrinsic property of all Poisson distributions.

Example:        Suppose a measurement produces a continuous variable, Z,
                that has (approximately) a "normal" distribution with
                mean = target value = T and variance = D, say, when
                quality is "at standard."  Consider the "Taguchi-like"
                measure of regret given by the sum-of-squares of N
                deviations of independent Z-values from the target, T,
                all divided by D.  Then normal distribution theory
                implies that E(R) = N and V(R) = 2N.  It follows that
                the number of "equivalent nonconformances" is R/2, and
                the "equivalent expectancy" is N/2.  (Note that the
                sample index value = nonconformances/expectancy is R/N;
                the average squared deviation from target,
                scaled by dividing by D.)

"Power" of
Variables
Data:           Variables data can be incredibly "rich" in sample
                information about quality compared with attributes data.
                The above "normal theory" example shows that a single
                continuous observation can yield a nonconformance
                expectancy of one-half!  And the "uniform" distribution
                would yield an even higher nonconformance expectancy of
                .66 per observation with the above "Taguchi-like" R
                measure!

Do-It-Right
from the
START:          Quality engineers should consult a professional
                statistician if there is any doubt in their minds about
                how to implement the above basic concepts.  One needs to
                utilize a realistic "Regret Function," which might need
                to be one-sided (rather than symmetric about the target)
                or linear or saturating (rather than always
                quadratically increasing.)  The calculation of the mean
                and variance of the regret depends upon the statistical
                distribution of test results when the manufacturing
                process is within its historical "process capability."
                Theoretical calculations can be complicated or require
                numerical integration; empirical studies of historical
                results are generally more straight-forward and more
                satisfactory.


                    Section A.3    Expectancy and Information

Contents of This Section:

                Two fundamental concepts are established by the highly
                technical arguments of this section.

                ...The information content in a set of regret measurements
                   is directly proportional to the Poissonized
                   "nonconformance expectancy" of the regrets at standard
                   process capability.

                ...The sample regret index (ratio of observed to
                   expected nonconformances) is the minimum variance,
                   unbiased estimate of the true index.


Minimum Variance Bound:

                If a sample statistic, tau, is an unbiased estimate of a
                parameter, theta, of the statistical distribution of the
                observed data vector, x, then the so-called "Cramer-Rao-
                Aitken-Silverstone Inequality" states that:

                 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                 ³  the product of the variance of tau times the    ³
                 ³                     ---------------              ³
                 ³  Fisherian Information in the data must be >= 1, ³
                 ³  --------- -----------                           ³
                 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                where this "information" is defined to be the expected
                value of the square of the derivative of the log-
                likelihood function of the data with respect to the
                parameter theta.  Furthermore, equality holds if and
                only if the derivative of the log-likelihood with
                respect to theta is of the form:

                                A(theta) * (tau-theta),

                in which case, tau is the minimum variance estimate of
                theta, and A(theta) is the Fisherian Information.


Poisson Example:

                If the observed numbers of nonconformances, { x(1),...,
                x(n) }, are stochastically independent and each follows a
                Poisson distribution with intensity parameter lambda(i),
                then the total number of observed nonconformances is
                also Poisson distributed with intensity parameter equal
                to the sum of the individual lambdas.  This total
                intensity can be re-expressed as:

           lambda(1)+...+lambda(n) = (nonconformance expectancy) * theta

                where theta is the true regret index (total lambda
                divided by the "standard" nonconformance intensity) and
                expectancy is n times the standard intensity.  As a
                result the log-likelihood function is

           [ x(1)+...+x(n) ] * log(theta) - expectancy * theta
                                    + terms that do not depend on theta.

                The theta-derivative of the log-likelihood is thus:

                  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                  ³  expectancy     x(1)+...+x(n)               ³
                  ³  ----------  (  -------------  -  theta )   ³
                  ³    theta         expectancy                 ³
                  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                Thus two basic facts are established by the C-R-A-S
                inequality...

                ...the sample index (observed / expected nonconformance
                   ratio) is the minimum variance estimate of the true
                   regret index, theta, and

                ...the (Fisherian) information content of the data
                   is A(theta) = expectancy / theta, which is directly
                   proportional to the nonconformance expectancy at
                   standard process capability.


                    Section A.4    Scale Invariance

Definition:     Equivalent nonconformances and expectancy are "scale
                invariant" quantities in the following sense:
                multiplying the regret by any strictly positive, constant
                value does not change the implied equivalent
                nonconformances and expectancy.  One implication of this
                is that it doesn't make any difference whether regret is
                expressed in terms of dollars or pennies or pounds
                sterling.

Proof:          Suppose that a regret measure, R, is multiplied by any
                constant value, K.  Then the expected value of K times R
                would be K times E, the original expected value of R.
                And the variance of K times R would be K-squared times
                V, the original variance of R.  As a result,
                multiplicative factors of K-squared cancel from both the
                numerators and the denominators of the ratios, R*E/V and
                E*E/V, that define equivalent nonconformances and
                expectancy.

Specific Implications for
the Nine Regret Families:

                ATTRIBUT.....Max Impact is unitless; call it ONE or
                BOUNDMAX     use any convenient value.

                LINEREGRET...The slope of the regret line is unimportant.
                RANGREGRET

                QUADRATC.....Regrets that are squared deviations from
                ENDPOINT     target values can be measured in any
                ONESIDED     convenient units.

                BILINEAR.....Either the Inventory Shortage or the Excess
                             Inventory Regret Slope parameter can be set
                             equal to 1 if the second Slope is expressed
                             as a MULTIPLE of the first.


                       Section A.5    Summary

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³                                                                    ³
 ³  Knowledge of the statistical distribution of Regret when Quality  ³
 ³  is at a STANDARD LEVEL (that is within the Present Capability     ³
 ³  of the Manufacturing Process) is needed for Poissonization.       ³
 ³                                                                    ³
 ³    The two statistical parameters which must be specified are:     ³
 ³            EXPREGRET = Expected Regret at Standard Quality,        ³
 ³            VARREGRET = Regret Variance at Standard Quality.        ³
 ³                                                                    ³
 ³    Poissonization is accomplished by multiplying Regret by         ³
 ³    EXPREGRET and then dividing by VARREGRET...                     ³
 ³                                                                    ³
 ³            EQUIVALENT DEFECTS = REGRET * EXPREGRET / VARREGRET.    ³
 ³                                                                    ³
 ³    Equivalent nonconformances have a statistical distribution that ³
 ³    is like the Poisson in the sense that the mean and the variance ³
 ³    of this distribution are EQUAL.  This common value is...        ³
 ³                                                                    ³
 ³            EQUIVALENT EXPECTANCY = EXPREGRET^2 / VARREGRET.        ³
 ³                                                                    ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ