CKDRIVE.COM 
                                  Version 2.0 
             
               Memory-Resident Driver for Add-On Computer Clocks 
             
                           Document revised 12/15/90
            
             
            IMPROVEMENTS IN THIS VERSION: 
             
                 Version 2.0 of CKDRIVE eliminates limitations of 
                 version 1.0 that required manual resetting for a 
                 new year or a leap year.  The program now (1) 
                 advances the year automatically after midnight 
                 December 31 and (2) advances the date to February 
                 29 instead of March 1 in leap years.  Other 
                 changes improve synchronization between the add-on
                 clock and the system clock; they now agree within
                 about .01 sec.
             
             
             
            AUTHOR:        Pete Petrakis 
            COMPANY:       Life Sciences Software 
                           812 Vista Drive 
                           Camano Island, Washington 98292 
             
            DISTRIBUTION:  Distributed as shareware, which means 
                           "try before you buy," not "free."  
                           Payment of $5 is required if you find 
                           after 21 days that CKDRIVE meets your 
                           needs.  Please send your payment (check 
                           or money order) to the above address.
             
             
                                       1
            DESCRIPTION: 
             
                 CKDRIVE is a memory-resident program that allows 
                 battery-powered add-on clocks to be set with the 
                 TIME and DATE commands in DOS.  It also 
                 automatically updates the DOS clock/calendar an 
                 instant before the time and date are displayed 
                 whenever you use DOS's TIME or DATE command or are 
                 running a program that reads the time and date. 
             
                 CKDRIVE eliminates the need to run special 
                 clocksetting programs such as SETCLOCK (to set the 
                 add-on clock) and GETCLOCK (to refresh the DOS 
                 clock/calendar from the add-on clock).  Whenever 
                 you want to change the time or date in your add- 
                 on clock, just change the time or date in DOS, and 
                 CKDRIVE will automatically pass the change along 
                 to the add-on clock.  Whenever you want to know 
                 the time or date in DOS, just ask for it in DOS, 
                 and CKDRIVE will refresh the DOS clock/calendar 
                 from the add-on clock an instant before the time 
                 or date is displayed on your screen. 
             
                 It's important to understand what is meant here by 
                 an add-on clock. Although the so-called slotless 
                 clocks, which plug into a ROM chip socket in your 
                 computer, are also add-on clocks, they are not the 
                 kind that CKDRIVE can work with.  Nor will it work 
                 with the CMOS clock, which is a battery clock but 
                 not an add-on, and is an integral part of the 
                 original equipment in AT and better computers. 
             
                 The add-on clock that CKDRIVE is designed to work 
                 with is the type that comes on a circuit board 
                 that plugs into an expansion slot in your 
                 computer.  Although some of these clocks, such as 
                 the one on the AST and Paradise multifunction 
                 cards, come from well known manufacturers, the 
                 clock-only type are typically quite inexpensive, 
                 with mail order prices often ranging from $7.50
                 to $15, and very often neither the card nor the box
                 it came in even has a manufacturer's name on it.
             
                 For example, the box mine came in says only, "Add- 
                 On Card for '88 or '286 Personal Computer" and 
                 "Made in China."  The word "clock" doesn't appear 


                                       2
                 anywhere on the box and there is not a shred of 
                 documentation.  The label on the diskette has only 
                 the handwritten letters, "CK," which presumably is 
                 an abbreviation for "CLOCK."  That's the type of 
                 clock CKDRIVE is designed for, and what is meant 
                 here by "add-on clock."  (Unfortunately, this does
                 not include Tandy's Smart Clock, which is also a
                 slot-type add-on clock but has altogether different
                 requirements.)

                 Despite its generic nature this cheap real-time
                 clock, which is typically used in XT-class computers,
                 is quite accurate (as computer clocks go) and in a
                 properly designed program can track time to the
                 millisecond (DOS can only display or set time to
                 1/100 second).
             
                 Interestingly, the cheap no-name generic imports 
                 and some brand-name clock boards use the same type 
                 of clock chip and usually the same set of I/O 
                 ports.  The base port is typically 240 hex, 2C0 
                 hex, or 340 hex (occasionally 3C0 hex) and most of 
                 the boards allow you to select from a pair of 
                 these port addresses (usually 240 hex and 340 hex) 
                 by moving a jumper.  When CKDRIVE is loaded, it 
                 checks to see which port addresses your add-on 
                 clock is using and configures itself accordingly 
                 for memory-resident operation.  If it finds no 
                 add-on clock at any of the four likely base ports, 
                 it reports that and quits. 
             
                 Some of the better known brands of add-on clocks, 
                 such as the one on the AST Six-Pack, come with 
                 their own memory-resident driver software.  AST's 
                 driver is called ASTCLOCK, which goes memory- 
                 resident when you run it with /R on the command 
                 line.  If your add-on clock came with that kind of 
                 software, you won't need CKDRIVE, although you 
                 could probably substitute CKDRIVE for the original 
                 driver software.  If yours didn't come with that 
                 kind of software, then CKDRIVE is for you. 
             
             


                                        3
            RUNNING THE PROGRAM: 
             
                 Type CKDRIVE at the DOS prompt, preferably 
                 immediately after boot-up.  The first thing 
                 CKDRIVE does when it's loaded is reset the DOS 
                 clock/calendar from the add-on clock.  Thereafter 
                 your DOS clock/calendar and your add-on clock will 
                 behave as a single clock, passing time and date to 
                 each other as needed.  It's advisable to put 
                 CKDRIVE in your AUTOEXEC.BAT file so it can reset 
                 the DOS clock/calendar from the battery clock 
                 whenever you boot the system.  Obviously it should 
                 go ahead of any program in the AUTOEXEC sequence 
                 that needs to check the DOS time and date. 
             
                 When loaded memory-resident, CKDRIVE takes less than
                 7k of RAM. 
             
             
            AUTOMATIC YEAR ADVANCE AND LEAP YEAR ADJUSTMENT: 
             
                 Version 2.0 of CKDRIVE will automatically advance 
                 the year in both the add-on clock and the DOS 
                 clock/calendar the first time you request the date 
                 in January -- provided you requested the date at 
                 least once with CKDRIVE installed during the 
                 previous month.  After midnight February 28 in a 
                 leap year it will automatically set the date to 
                 February 29 in both clocks -- provided you 
                 requested the date at least once with CKDRIVE 
                 installed between January 1 and February 28.  
                 (Requesting the date during those preliminary 
                 periods is practically unavoidable; you 
                 automatically request the date every time you save 
                 a new file to disk or date-stamp a new entry in a
                 data file, for example.) 
             

            SYNCHRONIZATION ACCURACY: 
             
                 When you set or read the time and date from DOS 
                 with CKDRIVE 2.0 loaded, the two clocks should 
                 agree within about .01 second, according to tests 
                 on my 8086 computer.  However, agreement between 
                 the two clocks thereafter will depend on two 
                 factors:  (1) the relative drift rates of the two 


                                        4
                 clocks and (2) the frequency of setting or reading 
                 the time.  Remember that all computer clocks 
                 drift, including DOS clock/calendars, battery- 
                 operated add-ons, and CMOS clocks.  So, if the 
                 add-on clock drifts a few seconds a day, its 
                 deviation from the true time will be passed to the 
                 DOS clock/calendar whenever you ask for the time; 
                 the two clocks will then agree, but both will 
                 deviate from true time to the extent that the add- 
                 on clock does.   
             
             
            KNOWN INCOMPATIBILITIES: 
             
                 If CKDRIVE is loaded, you should NEVER use the 
                 original software that came with your add-on clock 
                 for reading and setting it.  If you do, the hours, 
                 minutes, seconds, fractions of seconds, month, and 
                 day of the month will probably be OK, but the year 
                 will probably be read or set wrong, from CKDRIVE's 
                 perspective.  The reason is that the three ports 
                 available for year information in these clocks are 
                 for passive storage and are not controlled by the clock
                 chip, allowing each software developer to devise his
                 own method of managing that information.  Every 
                 program, including CKDRIVE, stores and reads 
                 information about years differently, so you should 
                 always read these clocks with the same software or 
                 software brand you used to set them.  Besides, you 
                 won't need any of that software if you use 
                 CKDRIVE; its purpose is to make those separate 
                 programs unnecessary. 
             
                 Use only one clock driver at a time.  If you 
                 already have a driver that does what CKDRIVE does, 
                 there is no need to load CKDRIVE too.  There will 
                 be trouble if you do; competition between the two 
                 drivers can slow things down dramatically and could
                 even cause a crash. 
             
                 The Microsoft BASIC Professional Development 
                 System (version 7.0 and probably 7.1 of BASIC)
                 is incompatible with CKDRIVE.  This is disappointing
                 but not surprising since Microsoft recommends that
                 no memory-resident programs at all be present when 
                 running that version of BASIC.  No system crash 


                                        5
                 results when BASIC 7 is loaded after CKDRIVE, and
                 the two clocks will continue to run, but each will
                 be oblivious to the other thereafter.  BASIC 7 messes
                 things up so the two clocks can no longer communicate
                 with each other through CKDRIVE, and you'll have to
                 reboot and reload CKDRIVE to get that interaction again. 
             
                 Finally, conflicts between memory-resident programs
                 are a fact of life, and they may require you to modify
                 the sequence in which such programs are loaded. 
             
             
            PROGRAM HISTORY: 
             
                 CKDRIVE.COM was inspired by CLKDRV10.SYS, a driver 
                 for slot-type add-on clocks that is loaded as a 
                 device in the CONFIG.SYS file and was written by 
                 my friend Tom Strickland of Alexandria, Virginia.  
                 Tom's driver is part of my TIMESET 6.0 package,
                 which can be found on Compuserve and BBSs around
                 the country (depending on the sysop's preference,
                 the archive file will be named TSET60 or TIMSET60
                 (.ZIP, .ARC, etc.).
             
                 Tom programs in assembly and C.  I program in 
                 BASIC and wanted to see if I too could write a 
                 driver for these clocks using Microsoft's BASIC 
                 Professional Development System (BASIC 7.0) and 
                 linkable assembly routines from MicroHelp, Inc. 
                 and Crescent Software, as well as some special 
                 purpose assembly routines that I wrote.  Crescent 
                 Software's P.D.Q. replacement library for 
                 QuickBASIC is mainly responsible for the program's 
                 small size (for a BASIC program) and its being a 
                 TSR. 

                 How do the two drivers compare?  Surprisingly 
                 well.  With my 8086 computer, the DOS clock and 
                 the add-on clock usually agree within 0.01 sec,
                 making version 2.0 of CKDRIVE.COM precise enough
                 to be used with TIMESET.
             
             


                                      6
            DISTRIBUTION AND DISCLAIMER: 
             
                 You can distribute CKDRIVE.COM to anyone you want 
                 provided you do not charge money for it (that's my
                 department) and do not separate it from this document.
                 Use of the program is at your own risk.  Pete Petrakis
                 does not claim that the program will work for everybody 
                 and he accepts no responsibility or liability for 
                 anything that might go wrong. 

            (Please don't forget to register.  It's only five bucks.)





Pete Petrakis
Camano Island, Washington
December 15, 1990

Your comments and suggestions are most welcome.  I can be reached on
Compuserve (76555,1175).



























                                      7