NAME
                BitClr -- Clear a bit within a value
                BitSet -- Set a bit within a value
                BitTst -- Test a bit within a value

        SYNOPSIS
                void BitClr(value, bit);    unsigned value, int bit;
                void BitSet(value, bit);    unsigned value, int bit;
                LOGICAL BitTst(value, bit); unsigned value, int bit;


        DESCRIPTION
        These three macros manipulate individual bits with integer
        values.  This is somewhat easier and more clear than ANDing
        and ORing bit masks.
        BitClr will clear a bit in the specified value, BitSet will
        set a bit in the specified value, and BitTst will test a bit
        without changing it.
        Bit numbers begin at 0 for the least significant bit.


        EXAMPLE
           int value = 0x55aa;		// pattern: 0101 0101 1010 1010
                                                    ^                ^
                                                   bit 15          bit 1

           if(BitTst(value, 1)) printf("Bit 1 in the value is set");  // TRUE
           else printf("Bit 1 in the value is clear");
           BitClr(value, 1);         // value becomes 0x55a8
           if(BitTst(value, 1)) printf("Bit 1 in the value is set");
           else printf("Bit 1 in the value is clear");           // NOW TRUE!