NAME
               crc functions -- crc misc. functions

       SYNOPSIS
               unsigned int crc = crc_clear()            clear crc value
               unsigned int crc = crc_update(crc, chr)   update crc value
               unsigned int crc = crc_finish(crc)        finish crc calculation
               crc = unsigned int crc value;

       DESCRIPTION
       These functions are used in crc calculations mainly for
       modem programs.  crc_clear is used to clear the crc value.
       However, if speed is a concern, just zero the crc value since
       crc_clear does nothing other than return a zero.
       crc_update is called once for each character to add to the crc.
       It receives the running crc and the character to be added.
       crc_finish actually calls crc_update twice with a value of
       0 in order to flush the 16 bit calculation and return the final crc
       calculation.  As supplied, the CCITT calculation polynomial is
       used.  The source can be easily changed to CRC16 if desired.

       EXAMPLE
              unsigned int crc;
              unsigned char next_chr;
              crc = crc_clear();
              /* for each character processed: */
              crc = crc_update(crc, next_chr);
              /* finally, */
              crc = crc_finish;



       NOTE:
       These functions are from a public domain source, author
       unknown,  They are not copyrighted.