NAME
                gameport functions -- manipulate game port

        SYNOPSIS
                (void)init_game(mode);    initialize and set mode
                (void)clear_game();       clear pending input
                r = get_press();          get waiting keypress
                (void)debounce();         input debouncer
                int mode;                 single/multi stroke mode
                unsigned char r;          key value


        DESCRIPTION
        This series of functions is used to read and debounce the
        four switch inputs on the joystick input port.  The
        analog joystick inputs are not supported.
        init_game() is called to setup the processor.  If its
        argument is TRUE, then multiple key inputs are allowed.
        If FALSE, any multiple key closure will be locked out.
        debounce() must be called periodically in order to
        debounce and process the switch inputs.  It is suggested
        that debounce() be called about 75 to 100 times per second.
        The structure "gamesw" contains information used by
        these routines.  The number of times debounce must be invoked
        to return a valid input is contained in gamesw.seed, and may
        be altered as desired.
        get_press() is called to return any fully debounced input.
        A value of 0 indicates no input available.
        Calling clear_game() clears any pending input and forces
        the debouncer to assume a new input sequence.

        The game port was originally intended for playing games via
        an arcade-style joystick.  However, for the serious engineer,
        this port is an excellent "quick and dirty" 4 bit TTL level
        input port.  It may be used for reading external switches,
        sensors, etc.

        Switch values are returned as an 8 bit value, with only the
        lowest 4 bits in use.  A set bit indicates a closed switch.
        If multiple keystrokes are not allowed, then get_press() will
        return 0, 1, 2, 4, or 8.  If multiples are allowed, then
        all values 0-15 (0-0x0f) may be returned.

           bit position            pin number on connector
               0                            2
               1                            7
               2                            14
               3                            10


     gameport functions    page 2

        EXAMPLE

            main() {
               unsigned char i;
               init_game(FALSE);    /* allow only single switch inputs */
               for ever() {
                  debounce();       /* call this regularly */
                  i = get_press();
                  if(i is 0) continue;
                  printf("switch value is %x\n", i);
                  }
               }