SOUNDKIT 1.0

                           August 14, 1990




                           Copyright 1990,
                         All rights reserved,

                         Russell B. Hildreth




                 Documentation and Programmer's Notes







        Soundkit 1.0  Documentation and Programmer's Notes:





        INTRODUCTION:

        Soundkit 1.0 is a collection of functions designed
        especially for users of Microsoft C compliers (MSC and
        QuickC).  The functions are provided as shareware in
        library format (SOUNDKIT.LIB).  All source code is
        available to programmers who register Soundkit with
        the author.

        Microsoft does not provide any ready to use sound
        functions with its languages as Borland does with
        the Turbo series.  Soundkit remedies this situation
        by providing sound support similar to that of Borlands.

        Soundkit, however, goes one step further by additionally
        providing a collection of ready to use sound routines.
        There are close to forty sound functions in the first
        Soundkit release, and there will be even more in the
        future.  These routines include musical selections,
        utility beeps, buzzes, and alarms, and generally silly
        sounds.  An attempt has been made to provide a wide
        variety of routines to satisfy programmers.

        Programmers can also, of course, use the core Soundkit
        functions [ tone(), soundon(), and soundoff() ] to
        create their own sound routines.

        All the currently available Soundkit routines can be
        tried out with the DEMO program included in the shareware
        release.  To illustrate using Soundkit functions, the
        source code to the DEMO program has been included.

        Soundkit is shareware.  If you use the routines provided
        in the SOUNDKIT.LIB file, you are obligated to register
        with the author.  Please see the section on registering
        in this document, and the SOUNDKIT.REG file.



        USING SOUNDKIT

        Using the Soundkit routines is very straightforward.  A
        programmer can run the DEMO program to assist in selecting
        desired sound routines.  Once the desired routines have
        been identified, the programmer needs only to #include the
        SOUNDKIT.H file and call the desired routines by name
        in a program.  For example,

        #include "SOUNDKIT.H"
        .
        .
        .

        void main(void)
        {
                .
                .
                .
                bach1();
                .
                .
                .
        }

        When a programmer compiles a program containing Soundkit
        routines, the SOUNDKIT.LIB file should be linked from the
        command line, or specified within a development environment.

        For example, to compile the SAMPLE.C file from the command
        line with Quick C, use the following line:

                QCL SAMPLE.C SOUNDKIT.LIB

        Failure to link the SOUNDKIT.LIB file will result in a
        program that will not properly execute any Soundkit functions
        (they simply won't be available to the program).



        INCLUDED FUNCTIONS:

        Core functions:

                delay()         This function provides the necessary
                                delays to make notes sound the same
                                length of time on any speed CPU.
                                Call delay() with an unsigned int
                                value, i.e., delay(5);  Experimentation
                                is usually necessary to obtain the
                                optimum delay time.  The delay()
                                function is written in assembly
                                language to increase delay length
                                accuracy (the delay routine suggested
                                by Microsoft in the QuickC sample
                                programs in an example of terrible
                                programming!).  Calling delay() with a
                                value of 0 is not advised, as it is
                                liable to lock up your machine.

                flushkb()       Flushes the keyboard.  This routine
                                is used by many of the Soundkit
                                which can be stopped by pressing a
                                key, to make sure that the user does
                                not stop a sound routine before it
                                has a chance to begin.

                soundon()       Takes an integer value and sounds the
                                PC speaker with that value.  This
                                sound will continue until the
                                soundoff() function is called.

                soundoff()      Turns off the PC speaker.  Use this to
                                shut the computer up at the end of
                                your sound functions.

                tone()          For many programmers this will be the
                                primary sound function.  It takes two
                                values, both unsigned integers.  The
                                first is a hz note value (musical note),
                                and the second is a delay length.  The
                                note is played for the delay length.
                                For example  tone(440,6)  would play an
                                A note for a short time.  The file
                                NOTE.CHT provides a complete list of
                                notes and their corresponding hz values.


        Sound routines:

        The DEMO program provides a complete list of all currently
        available sound routines.  These include musical routines
        from Bach and other favorites, alarms, buzzes, beeps,
        sirens, and other noises that programmers might find handy
        at one point or another.

        Many of the longer sound routines can be stopped by a
        keypress.  These include all of the music routines, the alarms,
        and several others.  Each of these calls the flushkb()
        function first to make sure that the routine will get a chance
        to play.  The shorter routines simply play themselves out,
        ignoring keypresses.



        GENERAL NOTES:

        A prewritten OFF.EXE program has been included to shut
        the speaker up from the command line.  The author
        experienced several instances in which he left the speaker
        on at the end of a routine by accident, and found the
        OFF program convenient for turning it back off while
        editing and recompiling.

        One important thing for novice programmers to realize is
        that just because there are many routines in the SOUNDKIT.LIB
        file, only those routines you call in your program will be
        actually used.  If your program only uses one beep routine,
        then its size will only grow in proportion to the one beep
        routine, NOT the full size of the SOUNDKIT.LIB file!

        Every effort has been made to keep these routines as small
        as possible.  They add very little overhead to the size
        of finished programs.  Further, the author is committed to
        making these routines even smaller in future releases of
        Soundkit.  Register now to get the next release as soon as
        it becomes available.

        Turbo C:  The author has absolutely no idea whether any of
        the Soundkit functions will work with Turbo C or Turbo C++.
        Probably they will not.  The author will, however, make a
        Borland compatible version of Soundkit available if demand
        warrants doing so.




        CPU DEPENDENT ROUTINES:

        There are several routines included which are CPU dependent.
        This means that they will not sound the same on all machines,
        primarily because faster machines will process the loops more
        quickly, distorting the sound.  These routines have been
        optimized to sound best on an 8mhz AT.  For consistency
        programmers should only use these routines in programs which
        will not be distributed to the world at large.  The CPU
        dependent routines are noted in the DEMO program as being such.
        All other Soundkit routines will perform identically on all
        machines--they are processor independent.  They have been
        tested on machines ranging from 4.77mhz to 20mhz with identical
        results in every instance.  Programmers should rely more heavily
        on these routines.

        Programmers constructing their own routines should be aware
        of the way different speed CPUs handle loops.  To create a
        routine that is CPU independent, always nest a minimal delay
        (i.e., delay(1);).  The delay() function performs identically
        on every CPU.  A routine which lacks a delay function will
        not be consistent among different processors (though such a
        routine might very well be used to create a desired sound
        effect).

        Programmers who possess the registered version of the Soundkit
        have access to the source code for each routine and can compare
        a CPU dependent routine such as siren2() with a processor
        independent routine such as siren1().



        REGISTRATION:

        There are three very good reasons for registering with the
        author.  One is that the programmer receives all of the
        source code used to create the SOUNDKIT.LIB.  This includes
        the core functions and all of the sound routines.  The
        programmer can then use these as examples for his or her
        own routines, or modify them to make new routines.  Also, the
        programmer can see how the core routines work and perhaps
        modify these also.

        Another reason is that the author will continually update
        Soundkit with a) additional sound routines and b) improved
        core routines.  The author is committed to producing the
        best possible sounds through the limited PC speaker, and is
        always searching for new ways to do more.

        The third reason deals with copyright laws.  Soundkit is
        copyright by the author, Russell B. Hildreth, 1990, who
        retains all rights to the routines.  If a programmer uses
        any of the Soundkit routines in a program that is to be
        distributed to the public, be it shareware, freeware, or
        retail software, the programmer (or distributor, as the
        case may be) is legally bound to register Soundkit with the
        author.  Most programmers, however, will probably want to
        register anyway, in order to obtain the source code.

        And finally, it is nice to support the work of others.  The
        author of Soundkit actively supports the shareware community.
        Further, all income derived from Soundkit is used by the
        author to assist in offsetting the ever increasing costs of
        obtaining a higher education.

        Please use the SOUNDKIT.REG form for registering.  Send
        $25.00 to
                        Russell B. Hildreth
                        P.O. Box 72431
                        Davis, CA  95617-2431



        CONTACTING THE AUTHOR:

        The author can be contacted on Compuserve at 71041,2132, or
        by U.S. Mail at the registration address.

        The author welcomes your suggestions for improvements to the
        Soundkit routines, as well as criticims and bug reports.