The CASM.C Assembly-language-to-CRL-Format Preprocessor
                                For BDS C v1.46
                                 March 3, 1982
 
                                  Leor Zolman
                                  BD Software
                                33 Lothrop st.
                        Brighton, Massachussetts 02135
 
 
The files making up the CASM package are as follows:

CASM.C         Source file for CASM program
CASM.SUB       Submit file for performing entire conversion of CSM file to CRL
CASM.DOC       This file
USERCODE.C,    Library for taking user area prefixes on filenames
USERCODE.CRL                          for input files (optional).

Also needed:

ASM.COM
DDT.COM (or SID.COM)

Description:
------------
 
     The only means previously provided to BDS C users for creating relocatable
object  modules  (CRL  files)  from  assembly language programs was a painfully
obscure  macro  package  (CMAC.LIB)  that  required  Digital  Research's  macro
assembler (MAC.COM) in order to work.  This  was especially bad because MAC, if
not already owned, cost almost as much as BDS  C  to  purchase.  This  document
describes the program "CASM", which I am placing in the public domain. CASM  is
a  preprocessor  that takes, as input, an assembly language source file of type
".CSM" (mnemonic for  C aSseMbly language) in a format much closer to "vanilla"
assembly language than  the  bizarre  craziness  of CMAC.LIB, and writes out an
".ASM" file which may then be assembled by the standard,  FREE,  CP/M assembler
(ASM.COM).  CASM  automatically recognizes which assembly language instructions
require relocation parameters and inserts the appropriate pseudo-operations and
extra opcodes into  the  output  file  to  cause that file to properly assemble
directly  into  CRL  format. In addition, some  rudimentary  logic  checks  are
performed; doubly-defined  and/or  undefined  labels are detected and reported,
with  the  feature of allowing similarly-named labels  to  exist  in  different
functions.  
 
     The pseudo-operations  that  CASM  recognizes  as special control commands
within a .CSM file are as follows:  
 
 
 
 
FUNCTION <name>          There is no need to specify  a  directory  of included
                         functions  at the start of a .CSM file. Each  function
                         must begin with  "function" pseudo-op, where <name> is
                         the name that will  be  used  for  the function in the
                         .CRL  file  directory.  No  other  information  should
                         appear on this line.  
 
 
EXTERNAL <list>          If   a   function  calls  other  C  or  assembly-coded
                         functions,  an "external" pseudo-op naming these other
                         functions must follow immediately after the "function"
                                        1



                         op.  One or more names may appear in the list, and the
                         list may be spread  over  as  many "external" lines as
                         necessary. Note that for the current version of BDS C,
                         only function names may appear  in  "external"  lines;
                         data  names (e.g. for external variables defined in  C
                         programs)  cannot  be placed in "external" statements.
 
 
ENDFUNC                          
(or) ENDFUNCTION         This op (both forms  are equivalent) must appear after
                         the end of the code for  a  particular  function.  The
                         name  of the function need not be given as an operand.
                         The  three   pseudo-ops   just  listed  are  the  ONLY
                         pseudo-ops  that  need to appear  among  the  assembly
                         language instructions of a ".CSM" file, and at no time
                         do  the assembly instruction  themselves  need  to  be
                         altered for relocation, as was the case with CMAC.LIB.
 
 
INCLUDE <filename>                     
(or) INCLUDE "filename"  This  op  causes  the named file to be inserted at the
                         current line of the  output  file.  If the filename is
                         enclosed in angle brackets (i.e., <filename>)  then  a
                         default  user  area  and  logical drive are assumed to
                         contain the named file (the specific defaults for your
                         system may be custimzed by  changing  the  appropriate
                          defines  in  CASM.C).  If  the  name  is enclosed  in
                         quotes,  than  the  current  drive and user  area  are
                         searched. Note that you'll usually want to include the
                         file BDS.LIB at the start of your  .CSM  file, so that
                         names   of  routines  in  the  run-time  package   are
                         recognized  by  CASM  and not interpreted as undefined
                         local forward references,  which  would  cause CASM to
                         generate  relocation parameters for those instructions
                         having run-time  package  routine  names  as operands.
                         Note  that  the  pseudo-op  MACLIB  is  equivalent  to
                         INCLUDE and may be used instead.  
 
 
Additional notes and bugs:  
 
0. If  a  label appears on an instruction, it MUST begin in column one  of  the
   line. If a label does not begin in column one, CASM will not recognize it as
   a label and relocation will not be handled correctly.  
 
1. Forward  references  to  EQUated  symbols in executable instructions are not
   allowed, although forward references  to  relocatable  symbols  are OK.  The
   reason  for  this  is that CASM is a one-pass preprocessor, and any  time  a
   previously unknown symbol  is  encountered  in  an instruction, CASM assumes
   that  symbol  is relocatable and generates a relocation  parameter  for  the
   instruction.  
 
2. INCLUDE and MACLIB only work for one level of inclusion.  
 
3. When a relocatable value needs to be specified in a "DW" op, then it must be
   the ONLY value  given  in  that  particular DW statement, or else relocation
   will not be properly handled.  
 
4. Characters  used  in  symbol  names should  be  restricted  to  alphanumeric
   characters; the dollar sign ($)  is  also  allowed,  but  might  lead  to  a
   conflict with labels generated by CASM.  
 
                                        2



5. The  .HEX file produced by ASM after assembling the output of CASM cannot be
   converted  into a binary file by using the LOAD.COM command; instead, DDT or
   SID must be  used  to  read  the  file into memory, and then the CP/M "SAVE"
   command must be issued to save the  file as a .CRL file. CASM inserts a line
   into the ASM file ending in the character  sequence  "!.",  specifically  so
   that  the  line  will  be flagged as an error. The user may then look at the
   value printed out at the left margin to see exactly how many 256-byte blocks
   need to be saved; this is the value to be used with the "SAVE" command.  
 
   The reason that "LOAD" cannot  be  used  is  that  CASM puts out the code to
   generate the CRL File directory at the END of the ASM file, using ORG to set
   the  location counter back to the base of the TPA, and  the  "LOAD"  command
   aborts with the cryptic message "INVERTED LOAD ADDRESS" when out-of-sequence
   data like  that  is  encountered.  Rather than require CASM to write out the
   directory into a new file and append the entire previous output onto the end
   of the directory, I require the user  to have to enter a SAVE command.  What
   the heck; you'd have to rename the file anyway if it were LOADed, right?  
 
6. The CASM.SUB submit file may be used to  perform  the  entire  procedure  of
   converting a .CSM file to a .CRL file. For a file named "FOO.CSM", just say:
   	submit casm foo
 
   and enter the "SAVE" command just the way says when all is done.  
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                        3