Here is a list of features and changes in ZCPR33.

MAJOR SYSTEM ENHANCEMENTS

    1.  Transient programs are now installed automatically at execution time 
        (not at load time).  No longer will you need Z3INS (or Z-RIP), and 
        no longer will you have files fail to operate correctly because you 
        forgot to install them.

    2.  Extended command processors (ECPs) and error handlers can now 
        coexist.  If a ZCPR33-compatible ECP encounters an error in 
        operation, it can return control to the command processor for error 
        handling.  In fact, any program can force invocation of the error 
        handler to process the command by which the program was invoked.  
        This can be useful when the program detects a syntax error and would 
        like to afford the user the opportunity to edit the command.

    3.  The command processor can load programs automatically to starting 
        addresses other than 100H using a new type-3 environment descriptor.  
        If the environment type number in the program header is more than 2, 
        then the word after the environment address (i.e., the word at 10bh) 
        will be used as the load address for the program.  By linking 
        extended command processors and error handlers to an address high in 
        memory, one can cause these programs to be loaded so as not to 
        affect a transient program loaded in the TPA at 100H.  This means 
        that the GO command can be used after an erroneously entered command 
        has caused the ECP and error handler to be invoked.  The same could 
        be done with small shell programs, such as a history shell.  The new 
        FCP package loads the transient IF processor in high memory also, 
        and the new RCP dynamically allocates its buffers at the top of the 
        TPA, so that, again, the GO command can be used fairly predictably.  
        A further use of the new dynamic loading feature is to make 
        transient programs that act as pseudo-residents.  For example, one 
        can now have a transient SAVE program (which could be much more 
        powerful than the resident one).  If SAVE.COM is linked with a type-
        3 environment with a load address of 8000H, then it can be used to 
        save any memory image in the range 100H-7FFFH.  Programs like 
        FINDERR and MEX2Z, which have to examine the memory image left by 
        the previous program that ran, can now be made to examine any part 
        of memory, even at the bottom of the TPA, by linking them to load in 
        high memory.

    4.  The command processor can now, like the ZCPR3 utilities, configure 
        itself dynamically according to parameters set in the environment 
        descriptor (Z3ENV).  The features that can be controlled by the 
        environment are:
                a.  the maximum allowed drive and user number
                b.  the acceptance of the DU form (DUOK)
                c.  the addresses of the RCP, FCP, and NDR
        The ability to get the RCP, FCP, and NDR addresses from the 
        environment makes it possible to allocate a single large buffer in 
        different proportions under the control of an alias.


SPEED ENHANCEMENTS

    1.  The SCANCUR option now works correctly so that the command processor 
        does not automatically scan the user's current directory first.  One 
        can now have a command search path that looks first in the directory 
        where one's most often used programs reside before searching the 
        current directory.  The current directory can be omitted from the 
        path so that it is scanned only when a colon is included before the 
        command name.  The latter feature is particularly useful with ram 
        disks.  To make it easier to get the effect of a leading colon (a 
        shifted character), a period (not a shifted character) can be used 
        instead.

    2.  An option allows searching of the command path and the extended 
        command processor to be bypassed when an explicit directory is 
        specified with the command.  Then when one makes a typing mistake or 
        uses the wrong name for a file, time will not be wasted scanning the 
        entire path, which may include some slow devices, before the error 
        handler is invoked.

    3.  With the tremendous power offered by an extended command processor, 
        a significant fraction of the user's commands may be intended for 
        the ECP.  If a command is entered with a leading space, the 
        processing of the command will be directed to the ECP immediately, 
        saving the time of searching the path.

    4.  The minimum path and root path features have now been implemented 
        correctly and efficiently (the minpath no longer takes up any room 
        in the command processor).  Since the minimum path prevents the 
        command processor from looking more than once in the same directory 
        for a file, operating speed is improved.


COMMAND PROCESSING PRIORITY CHANGES

    1.  Commands in the resident command package (RCP) are now scanned 
        before those that are resident in the command processor (CPR) 
        proper.  In this way, when an RCP is loaded that supports a more 
        powerful version of a command present in the CPR, the RCP command 
        will take precedence.

    2.  Command line input to the command processor now comes from four 
        sources in the following order:
                a.  a running ZEX script
                b.  a running SUBMIT job
                c.  the shell stack
                d.  the user
        By moving the priority of ZEX input to the top, ZEX jobs can now run 
        nicely and quickly under shells (since the shell does not have to be 
        reloaded for each line of the ZEX script), and the shells do not 
        have to contain complex code to check for ZEX input.  Once a ZEX job 
        has been started, it is treated as if its script were a single long 
        command line entered by the user.


IMPROVED SECURITY FEATURES

    1.  Security with the DU form of directory reference has been made more 
        rigorous.  It is now quite possible to allow the DU form to be used 
        and still have a secure system.  The highest drive and user number 
        are now under control of the environment, as noted above.  In 
        addition, if a user has reached a drive or user number beyond that 
        range by using a named directory, the D: or U: forms cannot then be 
        used to reach other drives or users that are out of range.  All 
        directories accessed by any DU-type form (DU:, D:, or U:) are fully 
        checked.

    2.  For enhanced performance in systems with DU accesses disabled by the 
        DUOK flag or with some named directories beyond the max DU limits, 
        DU expressions that reference directories for which there is a named 
        directory with no password will always be accepted.  For example, if 
        the maximum allowed drive is C but there is a named directory FLOPPY 
        which is J0:, the commands "J0:" and "XD J0:" will work exactly the 
        same as if FLOPPY had appeared in the place of J0.

    3.  For convenience, password checking of named directories can be 
        automatically disabled when the wheel byte is on.

    4.  Optionally, attempts to log in illegal directories can be passed 
        directly to the extended command processor for action.  One use of 
        this is to display a message and a listing of the allowed areas (by 
        running PWD, for example).

    5.  To reduce the nuisance to users in a secure system, password and 
        range checking are not applied to references to the currently logged 
        in directory.  Thus, for example, once you have entered an area 
        named SECRET (B7) by using the password, commands like "XD SECRET:" 
        or "XD B7:*.COM" will be accepted.  Such commands would not normally 
        be entered manually but are often generated by alias scripts.  I 
        have had some aliases ask me for a password four or five times for a 
        directory that I am already logged into!

    6.  Password checking is no longer performed for commands scanned while 
        the current IF state is false.  In ZCPR30 the user was asked for the 
        password whenever a passworded directory appeared in a command, even 
        if the command was not going to be executed.  As a result, complex 
        aliases could result in the user being asked numerous times for the 
        password even though only one of several possible commands would 
        actually execute.


ENHANCEMENTS TO CPR-RESIDENT COMMANDS

    1.  The command table (and certain other information) is placed in a 
        standard location in the code (as in the RCP and FCP modules) so 
        that an 'H' command in the RCP or a SHOW command can display 
        information about the resident commands (and other options) 
        supported in the command processor.

    2.  Command errors now result in the invocation of the error handler.  
        This is very important when the failure of a command could have a 
        serious detrimental impact on the rest of a command line script.  
        For example, if a SAVE or REN failed, later operations on the 
        resulting file would not work as planned.  By vectoring to an error 
        handler, the user is given the opportunity either to fix the command 
        or to abort the entire script.

    3.  When the SAVE or REN command will overwrite an existing file, the 
        user is prompted.  In ZCPR33 the operation of ZEX is temporarily 
        suspended so that unplanned prompts like this will not upset the ZEX 
        script.  If you have ever experienced this situation, you know what 
        a mess it used to cause.

    4.  The command REN NEWFILE=OLDFILE has enhanced exception checking.  
        Previously, if NEWFILE already existed and OLDFILE did not, the user 
        would nevertheless be asked if NEWFILE should be erased.  With an 
        affirmative answer, only after NEWFILE was erased would the user be 
        informed that there was no OLDFILE.  Now, the existence of OLDFILE 
        is checked first.

    5.  The JUMP command has been significantly enhanced so that it can now 
        serve a useful purpose.  Previously, the command "JUMP 1000" left 
        the default FCBs and the command tail set based on the string 
        "1000".  Now the command line is reparsed after the address token.  
        This means, for example, that "JUMP 100 COMMAND-TAIL" functions 
        identically to "GO COMMAND-TAIL".  It is now possible to execute 
        code loaded at an arbitrary address AND pass parameters to it in the 
        usual way.

    6.  The SAVE command can now save a specified number of sectors using 
        the syntax described in "ZCPR3, The Manual", namely, using the form 
        "SAVE nn FILENAME S" or "SAVE nnH FILENAME S".

    7.  The DIR command has the additional default forms "DIR /A" and "DIR 
        /S" to display all files in the directory with any attribute or with 
        the SYS attribute respectively.

    8.  The GET command will not allow a file to be loaded over the first 
        page of memory (this happened often in the past because of the 
        documentation error that indicated that the first parameter with GET 
        was supposed to be the page address rather than the full address).


MISCELLANEOUS NEW FEATURES

    1.  The address of the environment descriptor is passed in the HL 
        register when a program is called.  This affords an alternative 
        method for automatically installing programs, one that does not 
        depend on the standard 'Z3ENV' header at the beginning of the 
        program.

    2.  The address of the beginning of the current command is always kept 
        in the message buffer at address Z3MSG+4.  Formerly this occurred 
        only when there was an error, and the information was going to be 
        needed by the error handler.  With the new code, programs can make 
        whatever use they wish of this information.  In Z33FCP (soon to be 
        released) this feature is used to determine easily whether or not an 
        explicit directory or colon occurred before an IF command.  Shells 
        can use this feature to determine precisely how they were first 
        invoked by the user, namely with an explicit DU: form, an explicit 
        DIR: form, or neither.

    3.  The drive/user area from which a program was actually loaded by the 
        command processor is put into the S1 (user) and S2 (drive) bytes of 
        the external FCB at offsets 13 and 14 into the FCB.  Programs can 
        thus determine where the CPR was able to locate them.  (Note that 
        once the file has been loaded, only the name and type fields of the 
        FCB need be preserved for use by programs; the remaining bytes can 
        be used for any purpose.)

    4.  The two entry point vectors in the command processor have been 
        replaced by relative rather than absolute jumps.  The byte at offset 
        2 that is freed up contains a version ID (33H) that programs can use 
        to determine whether they are running under version 3.3 of ZCPR.  
        After the second jump (i.e., at offset 5) there are three 
        configuration bytes, where each bit indicates whether or not a 
        specific optional feature of ZCPR33 has been implemented.  The 
        structure of these bytes can be determined from the source code, and 
        they will be documented later.  Here is one example of a use for 
        this.  A program can determine whether or not SCANCUR (automatic 
        inclusion of the current directory at the head of the path) is in 
        effect in the command processor and can then follow the same 
        convention.  ARUNZ used to scan for the ALIAS.CMD file with SCANCUR 
        enabled.  In a future version, I will make ARUNZ follow the command 
        processor.  Another use is with a version of the SHOW command that 
        will tell one much more about the CPR configuration.  (Note that the 
        table of commands now begins at an offset of 08H in the CPR; the "H" 
        command in my experimental RCP145 will have to be modified to work 
        correctly -- it presently looks for the command table at an offset 
        of 6.)


BUG FIXES AND CODE ENHANCEMENTS

    1.  The length of the command tail that is copied from the command line 
        to the tail buffer at 80h is now length limited so that the tail 
        cannot overwrite code at 100h.  If the tail is too long, it will be 
        truncated and a warning message will be displayed.  Processing will 
        continue, however.  Without this checking, the system could easily 
        be crashed or even damaged by entering commands with very long 
        tails.

    2.  The default file control blocks are now properly initialized and 
        filled when the extended command processor is invoked.

    3.  The root path element is now computed correctly with the minimum 
        path feature enabled (in fact, the latter is no longer an option -- 
        it is always enabled).

    4.  The command processor will no longer go into an infinite loop when 
        the error handler cannot be found.  The built-in error handling will 
        always take over under this condition.

    5.  When a command error occurs during a false IF condition, invocation 
        of an external error handler was futile, because the error handler 
        command line would be flushed.  Results would be unpredictable and 
        invisible.  Now, when error handling is invoked during a false IF 
        state, the internal error handler is always given control, and it 
        echoes the flushed command line to the screen so that the user knows 
        what has happened.

    6.  In ZCPR30 the code for loading a file into memory made sure that the 
        CPR was not overwritten, but it did not allow for the case where a 
        resident system extension (RSX) was present that protected memory 
        even below the CPR.  ZCPR30 could overwrite the RSX code.  In ZCPR33 
        the address of the highest free memory is calculated correctly.

    7.  The sending of carriage-return-linefeeds during invocation of the 
        extended command processor has been fixed so that the ECP looks 
        exactly like the normal command processor (in ZCPR30 there used to 
        be another new line for each ECP invocation).

    8.  The code for previously existing functions has been significantly 
        shortened by using better algorithms, by eliminating redundant or 
        unused sections of code, by rearranging the code to eliminate jumps, 
        and by using the special Z80 opcodes.  The previously existing 
        functions were implemented so much more efficiently that most of the 
        new features are accommodated without an increase in total code 
        size.  The logical arrangement of the code has been greatly 
        improved, routines now being grouped by function and placed into 
        modules.  The code is now fully, clearly, and extensively commented.