.op
12/15/81
ACI software documentation:   T.COM vers 1.0

Description:   This program utility is provided on the systems
     master diskette with the .COM filetype extention.  The program
     requires that ACIDOS (CP/M * ) is booted prior to operating.

Purpose:       To facilitate the connection of an ACI-1, or ACI-2
     to other resources via some data communications link. A hard-
     ware connection can be made to either the printer or modem
     ports (or both), with the appropriate baud rate set for that
     link; (modem, cable, etc.).  The program then functions to provide
     either half or full duplex terminal emulation to those ports.
     A facility is also provided to SAVE portions of the session to
     several files, allowing them to be viewed or edited at a later
     date.

Entry syntax:  To invoke the program key T<ret> from the operating
     system for half-duplex emulation, or T F<ret> for FULL-DUPLEX
     operation.  Once in this mode, All characters (EXCEPT ASCII
     RS) are echoed from the terminal keyboard to the PRINTER &
     MODEM PORTS. In half duplex mode, keyboard characters are also
     echoed to the screen. ALSO, all characters entering the PRINTER
     & MODEM ports are displayed to the screen.  To exit from the 
     program you must push the system reset switch.

     When it is desired to save portions of the interactive session
     to files, indicate the START by keying the ASCII RS (control ^ 
     or control, shift, and 6 keys at same time).  The portion will
     be saved in memory (approx 55K max size), until ANOTHER RS is 
     keyed to indicate the END of save.  The process can be repeated
     during one session, and the filenames created will be:
     MFILE0, MFILE1, MFILE2,....,etc.

     NOTE: T.COM uses 8-bit data and does not mask any bits, therefore
     parity or the communication of binary data may be performed.

Installation note:  When file SAVE is initiated, a reverse video
     command is sent to the terminal to clearly indicate the mode.
     The default command in the distribution version is for the 
     televideo 950 terminal: ESC b (rev ON), ESC d (rev OFF)
     If your terminal uses different commands, use DDT.COM to patch
     the T.COM program:  (operator types in lower case portion)

     A>ddt t.com<ret>
     DDT VERS 2.2
     NEXT  PC
     0380 0100
     -f0105,0105,hex value of first character of reverse video ON
     -f0106,0106,hex value of second character of rev video ON
     -f0108,0108,hex value of first char of rev video OFF
     -f0109,0109,hex value of second char of rev video OFF
     -^c
     A>save 3 t.com<ret>